## Slide 1: VoIP Tutorial
Brian Rosen
Distinguished Engineer
Neustar, Inc.

## Slide 2: What Is Internet Protocol?
A way to send data on a high speed network
Data is broken up into packets, which are variable sized
A packet is a sequence of bytes, with a “header” and a “payload”
Data is typically sent serially, bit by bit, byte by byte
IP is a layered protocol

## Slide 3: “Trace Route” - UPS version
Location Date Local Time Activity
Zelienople, PA, United States 05/27/2014 11:40 A.M. Delivered
05/27/2014 7:03 A.M. Destination Scan
05/27/2014 6:43 A.M. Arrival Scan
Pittsburgh, PA, United States 05/27/2014 6:15 A.M. Departure Scan
Pittsburgh, PA, United States 05/24/2014 6:00 A.M. Destination Scan
05/24/2014 5:54 A.M. Arrival Scan
Louisville, KY, United States 05/24/2014 4:47 A.M. Departure Scan
05/24/2014 12:28 A.M. Import Scan
Louisville, KY, United States 05/23/2014 2:37 P.M. Import Scan
05/23/2014 1:30 A.M. Arrival Scan
Anchorage, AK, United States 05/22/2014 3:37 P.M. Departure Scan
05/22/2014 1:51 P.M. Arrival Scan
Shanghai, China 05/22/2014 8:58 P.M. Departure Scan
Shanghai, China 05/21/2014 7:51 P.M. Export Scan
05/21/2014 4:25 P.M. Arrival Scan
05/21/2014 4:10 P.M. Departure Scan
05/21/2014 2:52 P.M. Origin Scan
China 05/21/2014 12:07 A.M. Order Processed

## Slide 4: “traceroute” - IP network version
traceroute to pdx.edu (131.252.115.23), 64 hops max, 52 byte packets
1 10.33.192.2 (10.33.192.2) 20.692 ms 21.152 ms 20.891 ms
2 stco6509a-gi-3-2.va.neustar.com (10.33.0.6) 31.958 ms 21.069 ms 20.038 ms
4 stsc1285b-eth-s1s1p2.va.neustar.com (10.91.0.3) 22.745 ms 22.654 ms 27.122 ms
5 209.173.53.226 (209.173.53.226) 26.276 ms 24.248 ms 25.873 ms
6 dcx2-edge-02.inet.qwest.net (65.123.192.93) 32.139 ms 29.091 ms 22.520 ms
7 dcp-brdr-04.inet.qwest.net (67.14.28.34) 24.099 ms 52.813 ms 27.055 ms
8 te0-16-0-14.ccr41.iad02.atlas.cogentco.com (154.54.12.245) 23.296 ms 22.105 ms
be2176.ccr21.dca01.atlas.cogentco.com (154.54.41.54) 23.200 ms
be2154.ccr41.ord01.atlas.cogentco.com (154.54.30.198) 50.699 ms
be2159.mpd22.mci01.atlas.cogentco.com (154.54.24.81) 70.447 ms
be2131.ccr22.den01.atlas.cogentco.com (154.54.26.129) 73.082 ms 75.397 ms
13 be2127.ccr21.slc01.atlas.cogentco.com (154.54.25.70) 102.761 ms
te4-2.ccr01.boi01.atlas.cogentco.com (154.54.40.90) 96.096 ms
te0-0-0-2.rcr11.pdx02.atlas.cogentco.com (154.54.40.97) 97.065 ms
te2-7.ccr01.pdx01.atlas.cogentco.com (154.54.0.85) 95.403 ms
portlandstateuniversity.demarc.cogentco.com (38.99.222.130) 98.326 ms 98.469 ms 97.227 ms
131.252.5.220 (131.252.5.220) 94.479 ms 95.821 ms 93.371 ms
22 131.252.115.23 (131.252.115.4) 96.072 ms !H 98.743 ms !H

## Slide 5: Package Switching Network

## Slide 6
Packet Switching Network

## Slide 7: TCP/IP architecture
 |  OSI- Model |  |  |  TCP/IP - Model
 7 | application |  |  | application
 6 | presentation |  |  | 
 5 | session |  |  | 
 4 | transport |  |  | transport
 3 | network |  |  | network
 2 | datalink |  |  | link
 1 | physical |  |  | 

## Slide 8: Protocol Layering
TCP segment
IP datagram
Network-level packet
TCP Header
User data
Application byte stream
Network
Header
IP
Header

## Slide 9: Routing Basics
Routers have multiple ports
Maintain a “Routing Table” mapping network IDs to ports
Copies packets from one port to another
Ports don’t have to be the same link type
LAN B
2
Router X
3
1
LAN A
P
R
Q
LAN C
Network | Port
P | 1
Q | 2
R | 3

## Slide 10: Routing Basics
Typically, with a collection of routers, there is more than one way to get from A  B
The job of the router is to recieve a packet on one of its ports and send it to the next hop router on another one of its ports based on the IP address of the destination
Routers choose the “best” next hop (port) that they know at the time
  “Best” is in the eyes of the beholder
  Can consider pipe size, delay, error rates, etc
  Each route has a metric, routers chose routes based on the metric
“Routing Protocols” (e.g. RIP, IGMP, ISIS, BGP) distribute routes and routing metrics among routers
These protocols run between routers and are not visible to users

## Slide 11: IPv4 Datagram
Version
IHL
Type of Service
Total Length
Identification
Fragment Offset
Flags
Time to Live
Protocol
Header Checksum
Source Address
Destination Address
Options + Padding
20 octets
0
4
8
16
31
(a) IPv4
Bit:

## Slide 12: Format of an IPv6 Datagram
Version
Priority
Flow Label
Next Header
Source Address
Destination Address
10x32 bits = 40 octets
0
4
8
16
31
(b) IPv6
Bit:
Payload Length
Hop Limit
24
Notes: Can you guys fix the layout

## Slide 13: TCP vs UDP
Transmission Control Protocol
  Connection oriented
  Byte stream
  Ordered: out of order packets are handled correctly
  Lossless: packets repeated until acknowledged
  Window based ack
Universal (User) Datagram Protocol
  Connectionless
  Datagram (packet) oriented
  No order guaranteed
  Lossy
  No ack

## Slide 14: Addressing
Host Bits (h) (32-[CIDR subset mask]) | Hosts per subnet (2h-2)
2 [/30] | 2
3 [/29] | 6
4 [/28] | 14
5 [/27] | 30
6 [/26] | 62
7 [/25] | 126
8 [/24] | 254
9 [/23] | 510
10 [/22] | 1022
11 [/21] | 2046
12 [/20] | 4094
13 [/19] | 8190
14 [/18] | 16382
Network-Prefix | Subnet-Number | Host-Number
Extended-Network-Prefix
Internet Routed
Network Address
Ignored by
Internet Routers
Network
Host

## Slide 15: Service Provider Network

## Slide 16: Internet Multimedia aka VoIP
A way to send real-time two-way media over an IP network
Real Time Protocol (RTP) – media packets
Real Time Control Protocol (RTCP) – monitor & report
Session Initiation Protocol (SIP) – call control
Session Description Protocol (SDP) – media session description

## Slide 17: Real Time Transport Protocol (RTP)
RTP is a transport protocol that provides end to end delivery services for data with real time characteristics
RTP consists of two closely linked parts
  RTP to carry data
  RTCP to report the quality of service and to convey information about the participants in an on going session
Applications typically run RTP on top of UDP to make use of its framing, multiplexing and checksum services

## Slide 18: RTP For Voice
Voice data is digitized, compressed, and packetized
Packetization implies a packetization period (playback time for one packet)
  Bigger packets are more efficient (less overhead)
  Smaller packets have less delay
    Because you have to fill the packet before you send it
Because RTP normally rides on UDP, it is unreliable
  Usually, we simply ignore errors
  We also drop out of order packets

## Slide 19: Session Initiation Protocol (SIP)
Internet Standard – RFC3261
  RFC – http://www.ietf.org/rfc/rfc3261.txt
Reuse Internet Addressing (URIs, DNS, proxies)
  Uniform Resource Identifiers: e.g. http://www.google.com, sip:brian.rosen@neustar.biz, or sip:sws1.east.verizon.net
  Domain Name Service translates e.g. sws1.east.verizon.net to IP address 123.15.23.114
  A “proxy” is a signaling entity in the middle of the path that usually echoes a signaling message while routing, enhancing, or policing it
Reuse HTTP Style
  Text based, human readible
Makes no assumptions about underlying protocol:
  TCP, UDP, etc.

## Slide 20: Ideal SIP Trapezoid
RTP/RTCP
SIP
Media Goes Direct
SIP Signaling Goes through several intermediaries
SIP
SIP
Proxy Server
Proxy Server

## Slide 21: SIP Session Setup Example
200 OK
ACK
INVITE sip:picard@vz.net
BYE
200 OK
host.att.net
sip.vz.net
SIP User
Agent Client
SIP User Agent Server
Media Stream

## Slide 22: Proxy Server Example
200 OK
BYE
200 OK
INVITE sip:picard@ibm.com
200 OK
ACK
INVITE sip:picard@bm.com
Host.ibm.com
sip.neustar.biz
SIP User Agent Client
SIP Proxy
Server
SIP User
Agent Server
Media Stream

## Slide 23: SIP Requests Example 1
INVITE sip:picard@ibm.com SIP/2.0
Via: SIP/2.0/UDP host.ibm.com:5060
From: Alan Johnston <sip:alan.johnston@lucent.com>
To: Jean Luc Picard <sip:picard@ibm.com>
Call-ID: 314159@host.ibm.com
CSeq: 1 INVITE
Uniquely identify this session request
}
Required Headers (fields):

## Slide 24: SIP Requests Example 2
INVITE +12025551212@example.net;user=phone SIP/2.0
Via: SIP/2.0/UDP host.lucent.com:5060
From: Alan Johnston <+17035551234@lucent.com;user=phone>
To: Jean Luc Picard <+12025551212@example.net;user=phone>
Call-ID: 314159@host.lucent.com
CSeq: 1 INVITE
Contact: sip:+7035551234@lucent.com
Content-Type: application/sdp
Content-Length: 124
v=0
o=ajohnston 5462346 332134 IN IP4 host.lucent.com
t=0 0
c=IN IP4 10.64.1.1
m=audio 49170 RTP/AVP 0 3
Typical SIP Request:

## Slide 25: SIP Responses Example 2
SIP/2.0 200 OK
Via: SIP/2.0/UDP host.lucent.com
From: Alan Johnston <sip:+17035551234@lucent.com;user=phone>
To: Jean Luc Picard <sip:+12025551212@example.net;user=phone>
Call-ID: 314159@host.lucent.com
CSeq: 1 INVITE
Contact: sip:+12025551212@example.net;user=phone
Content-Type: application/sdp
Content-Length: 107
v=0
o=picard 124333 67895 IN IP4 example.net
t=0 0
c=IN IP4 11.234.2.1
m=audio 3456 RTP/AVP 0
Typical SIP Response (Containing SDP)

## Slide 26: Service Provider Network
PSTN
SP2
SP1
VoIP Phone
IP Network
Session Border Controller
Softswitch
Session Border Controller
Route Server
Session Border Controller
Softswitch
Gateway
VPN

## Slide 27: Protocol Comparisons
SS7
Layered Protocol: MTP1/2/3/ISUP
Endpoints addressed by TN
Signaling not same path as media
Signaling points addressed by Point Codes
STP
SSP
SIP
Layered Protocol: Phy/Link/IP/UDP/SIP
Endpoints addressed by URI, which can contain a TN
Signaling not same path as media
“Signaling Points” addressed by URIs
SIP Proxy Server
Route Server (ENUM), sort of

## Slide 28: IMS Network
CS Domain
-or-
PSTN
-or-
Legacy
-or-
External
PS Domain
IMS Core
Operator 2
“Mb/Gi-Cloud”
HSS
IMS Terminal
(TE and MT)
Radio Access
HLR
BGCF
MGCF
Sh
Si
Sh
ISC
Gm
CAP
Uu
Gr
Gc
Go
Mr
Mg
Mi
Mm
Mj
Mn
Cx
Dx
Mp
CSCF
PDF
SLF
Iu
Mw
Mk
MRF-C
MRF-P
IMS Services
AS
OSA-SCS
IM-SSF
MGW
Gn
GGSN
SGSN
BGCF
CSCF
Multimedia IP Networks

## Slide 29: Routing
Today, routing is direct: TN to termination switch
There are medium term proposals to use two steps: TN to effectively SPID, SPID to POI, using ENUM
Both of these are not effective because optimal POI depends on dynamic factors:
  Who the originating and termination SP are
  Where the caller and called parties are (in network terms)
  What the current load and failure conditions are
Routing therefore needs the first step (TN to SPID), but then needs a negotiation between origination and termination parties to determine the optimal route
This is very straightforward computer stuff, not requiring any technology that isn’t ho-hum.
But it’s not just a database – it’s an algorithm and a set of metrics dynamically determined