LNP Problem/Issue Identification and Description Form

Submittal Date (mm/dd/yyyy):  07 /11/2017

Company(s) Submitting Issue: iconectiv

Contact(s):  Name John P. Malyar

Contact Number 732/699/7192

Email Address jmalyar@iconectiv.com

(NOTE: Submitting Company(s) is to complete this section of the form along with Sections 1, 2 and 3.)

- Problem/Issue Statement: (Brief statement outlining the problem/issue.)

During iconectiv LNPA transition testing of a local system, issues were discovered that impacts the execution and/or verification of an Industry Test Case (ITC) required for certification.  These issues relate to a nonconformance to Industry Specification(s), an undocumented capability or feature, or a difference of interpretation (between LNPAs) of an Industry Specification.  The specific issue herein needing resolution concerns the creation of port-to-original (PTO) SVs.  The PTO SV create message did not conform to the specifications.

- Problem/Issue Description: (Provide detailed description of problem/issue.)

- Examples & Impacts of Problem/Issue:

| Observation Specification / Requirement |  |
| --- | --- |
| DPC/SSN values included in PTO SV Create message all set to “No Value Needed”, which are prohibited as identified in the requirements. It is anticipated that any prohibited attribute (including other “XML Optional Data” attributes) that can be set to a null or “no value needed” value could be sent in this PTO SV Create message with a null or “no value needed” value. Violates FRS requirements: RR5-179 Create Inter-Service Provider PTO Subscription Version - New Service Provider Data Attributes – Rejected NPAC SMS shall reject an Inter-Service Provider Create Request that includes the following data attributes from NPAC personnel or the new Service Provider, when the Porting to Original flag is set to True: (reference NANC 399) • LRN • Class DPC • Class SSN • LIDB DPC • LIDB SSN • CNAM DPC • CNAM SSN • ISVM DPC • ISVM SSN • WSMSC DPC (if supported by the Service Provider SOA) • WSMSC SSN (if supported by the Service Provider SOA) • Porting to Original • Billing Service Provider ID • End-User Location - Value • End-User Location - Type • SV Type • Alternative SPID |  |

B.   Frequency of Occurrence: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- NPAC Regions Impacted:

Canada___ Mid Atlantic ___ Midwest___ Northeast___ Southeast___ Southwest___ Western___

West Coast___ ALL_X US regions__

D.  Rationale why existing process is deficient: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

E.   Identify action taken in other committees / forums: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

F.   Any other descriptive items: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- Suggested Resolution:

Local System should identify the impact of functionality not being supported.  If not conforming to industry specifications, local system should provide support for the nonconformance.  If undocumented or misinterpreted functionality is required by the Industry, the appropriate Industry Specifications will need to be updated to reflect the required functionality and the change order once accepted should be forwarded to the NAPM LLC for the purpose of requesting a Statement of Work (SOW) from iconectiv.

LNPA WG: (only)

Item Number: PIM 093

Issue Resolution Referred to: _________________________________________________________

Why Issue Referred: __________________________________________________________________ ____________________________________________________________________________________________________________________________________________________________________________