LNP Problem/Issue Identification and Description Form

Submittal Date (mm/dd/yyyy):  07 /31/2017

Company(s) Submitting Issue: iconectiv

Contact(s):  Name John P. Malyar

Contact Number 732/699/7192

Email Address jmalyar@iconectiv.com

(NOTE: Submitting Company(s) is to complete this section of the form along with Sections 1, 2 and 3.)

- Problem/Issue Statement: (Brief statement outlining the problem/issue.)

During iconectiv LNPA transition testing of a local system, issues were discovered that impacts the execution and/or verification of an Industry Test Case (ITC) required for certification.  These issues relate to a nonconformance to Industry Specification(s), an undocumented capability or feature, or a difference of interpretation (between LNPAs) of an Industry Specification.  The specific issue herein needing resolution concerns recovery of Network Data objects.  The Local System expected optional attributes in recovery messages.

- Problem/Issue Description: (Provide detailed description of problem/issue.)

- Examples & Impacts of Problem/Issue:

| Observation | Specification / Requirement |
| --- | --- |
| Local System does not come out of recovery when Network Data exists in the SWIM list. Vendor indicated that incumbent LNPA NPAC provides the SP Name in SWIM Network Data recovery responses. It is also anticipated that the incumbent LNPA NPAC provides the SP Name in time-range and record-based Network Data recovery. | In the ASN.1 for Recovery of network data, the SP Name is defined as an Optional attribute. The iconectiv solution populates in the SWIM list whatever was originally broadcast for the network data, which does not include the SP Name. |

B.   Frequency of Occurrence: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- NPAC Regions Impacted:

Canada___ Mid Atlantic ___ Midwest___ Northeast___ Southeast___ Southwest___ Western___

West Coast___  ALL_X US regions__

D.  Rationale why existing process is deficient: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

E.   Identify action taken in other committees / forums: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

F.   Any other descriptive items: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- Suggested Resolution:

Local System should identify the impact of functionality not being supported.  If the issue is a nonconformance to industry specifications, local system should provide remediation for the nonconformance if impacted.  If issue is related to undocumented or misinterpreted functionality that is required by the Industry, the appropriate Industry Specifications will need to be updated to reflect the required functionality and the change order once accepted should be forwarded to the NAPM LLC for the purpose of requesting a Statement of Work (SOW) from iconectiv.

LNPA WG: (only)

Item Number:  PIM 096

Issue Resolution Referred to: _________________________________________________________

Why Issue Referred: __________________________________________________________________ ____________________________________________________________________________________________________________________________________________________________________________