NANC CHANGE ORDER SUMMARY

(Rev: 24 – 08/29/97)

| Release I Open Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Proposed Resolution | Level of Effort |
| NPAC | LSMS SOA |

NANC

| 83 | Illinois Meeting 5/1/97 |
| --- | --- |

NPAC Time Synchronization

It has been requested that a requirement be added to the FRS to require that the NPAC SMS systems use NTP to synchronize from a Stratum 1 host.  This would insure that all NPAC SMS vendors are synchronized on their times.  The requirement would be as follows:

NPAC Clock Synchronization

| NPAC SMS shall synchronize its system clock using NTP. | Low | FRS |
| --- | --- | --- |

Perot will synchronize using NTP. M&P was to be put in place in the future to insure that the Lockheed and Perot NPAC vendor systems do not get more than +- 5 minutes out of sync.

A question was raised about what Perot was syncing off of if not a stratum 1 host. They will be synchronizing from the naval observatory host manually.  There was a question on whether Perot would synchronize off of Lockheed.  Perot feels that setting up the security for this would be difficult to do in the short term and that by using the naval observatory clock they would only be off a few seconds from Lockheed.

Perot provided the M&P for at minimum a weekly synchronization of their hosts. They are investigating dial-up to a stratum 1 for release 1.

ILL 131

MCI

12/16/96

Creation of old SV for Every Change

The NPAC SMS should create an old subscription version for each change made to an active TN subscription version, regardless of how that change is made. That is, even for events such as an NPA split, an old SV should be

created to preserve the SV containing the former NPA. Requirements should be added to the FRS to insure this is clear.

Medium

|  | IIS / FRS |
| --- | --- |

This feature has been requested for Release 3.  Detailed requirements have been developed.

This change has been implemented in Release 1.  This change order was grouped into release 3 in error.

RE-OPENED – A question was raised on whether this functionality was really implemented in release 1 by the vendors.  Perot has not implemented this change order in Release 1.  Lockheed will implement this change in their October release.  The requirement is in the FRS.

Perot to follow up on this internally.  To be discussed.

This change order will be re-applied to the Release 2 FRS document.

NANC 134

AT&T

8/10/97

Disconnect Action Behavior Discrepancies

Disconnect Action GDMO is currently in conflict with requirements as follows: “If a delete request fails for the disconnect subscription version after the retry periods have expired, the version status will be set to failed or partially failed based on if the create failed in all or some of the Local SMSs respectively.  The current active version will remain active and an error will be returned for the action.”  It should be reworded to state: “If a delete request fails for the disconnect subscription version after the retry periods have expired, the version status will be set to active if all LSMS’s fail or old if one or more but not all  LSMS’s fail.”

Table and Flow Graph in the FRS and IIS should also be updated as follows:

| Sending to Old -NPAC SMS automatically sets a sending Subscription Version to old after a disconnect or “porting to original” port to all Local SMS successfully completes. Disconnects that fail to one or more and not all will also be set to old. | Low | FRS/IIS |
| --- | --- | --- |

Documents would be updated in the next release.

Pending review.

| Lockheed Martin will check on behavior for what happens in failures for LSSP ports. | N/A | N/A |
| --- | --- | --- |
| NANC 134 (cont.) |

Sending to Active-

NPAC SMS automatically sets a sending Subscription Version to active after the Subscription Version activation is successful in all of the Local SMSs.

NPAC SMS automatically sets a sending Subscription Version to active after the Subscription Version modification is successfully broadcast to any of the Local SMSs.

| NPAC SMS automatically sets a sending Subscription Version to active after a failure to all Local SMSs on a disconnect. |
| --- |
|  | NANC 135 | Perot Team 8/10/97 |

Download File Clarifications

The following clarifications for download files defined in FRS 1.4 and 2.2 should be added:

Subscription Versions in the download file are selected by an NPA-NXX begin and end range.

The name of the Subscription Version file is formatted NPANXX-NPANXX.DD-MM-YYYYHH24MISS,  the NPANXX-NPANXX values map to the selection criteria and the time stamp maps to the current time.

The download reason in all download files is always set to new.

There are no selection criteria for the NPA-NXX, LRN or SPID down load files.  All data is included.

The name of the Service Provider download file is SPID.DD-MM-YYYYHH24MISS, where the SPID portion is the literal string ‘SPID’.

The name of the NPA-NXX download file is NPA-NXX.DD-MM-YYYYHH24MISS, where the NPA-NXX portion is the literal string ‘LRN’.

| The name of the LRN download file is LRN.DD-MM-YYYYHH24MISS, where the LRN portion is the literal string ‘LRN’. | Low | FRS |
| --- | --- | --- |

FRS would be updated in the next release.

| Pending review. There is also a file name in the example with a month of 13 that should be corrected. | N/A | N/A |
| --- | --- | --- |
| NANC 137 | Lockheed Martin Team 8/13/97 |

Disconnect Active SV Behavior Clarification

We have a conflict between the FRS and the GDMO dealing with disconnecting active subscription versions. In the FRS, requirement R5-64.1 states that we shall not allow a disconnect of an active SV if there is a "pending" SV for that same TN until that "pending" SV is cancelled.

In the GDMO in IIS 1.2, section 5.0, Action Behaviors, states  “there is a pending SV and an active SV, and the currentSP has not authorized the port, the active one will be disconnected, and the pending one will go into conflict. If the SP has not  authorized the port, the disconnect will fail”

| The GDMO should be corrected to state, “if there is a pending SV and an active SV, the disconnect of the active SV will fail.” | Low | IIS |
| --- | --- | --- |

IIS would be updated in the next release.

| Pending review. | N/A | N/A |
| --- | --- | --- |
| NANC 138 |

CMA 8/11/97

Definition of Cause Code Values - REVISITED

NANC 54 defined the cause code values and the FRS was to be updated.  Due to an oversite this update was not made in the FRS.  The change was going to be applied in FRS 1.4 and 2.2.  However, a discrepanccy as found. The defined values specified in NANC 54 where are as follows:

The values less than 50 were reserved for SMS NPAC internal use.

Other defined values are:

0 – NULL (DO NOT MODIFY)

1 -	NPAC automatic cancellation

50 -	LSR Not Received

51 -	FOC Not Issued

52 -	Due Date Mismatch

53 -	Vacant Number Port

54 -	General Conflict

In table in the FRS the following cause code is defined:  NPAC SMS Automatic Conflict from Cancellation

| There is no corresponding code defined in Change Order NANC 54. Is there a numeric value or is this cause code valid? | Medium | FRS |
| --- | --- | --- |

Update to be made to the FRS.

Pending review by the vendors.  Lockheed does not set a cause code when the NPAC SMS automatically puts a cancelled order into conflict.  Perot is reviewing there implementation.

There is not a requirement in the FRS for a cause code of NPAC SMS Automatic Conflict from Cancellation.

Operations flows are being reviewed.

NANC 142

NANC

8/18/97

Port to Original Flow Clarifications

There is currently not a clear definition of the flow in the IIS for port to original. What is defined in the IIS could never be implemented and work. The issue to date is what notification on what subscription versions should be sent to the old and SOA systems. NPAC and SOA vendor implementations conflict.

Proposed flows for the IIS have been sent out to the group for review.

| Perot and Lockheed are reviewing. The notifications seem to be the biggest issue. The exact processing order of events may also be an issue. SOA vendors have also been asked to review the proposed flows. |
| --- |
| NANC 143 | AGCS 8/27/97 |

Subscription Version M-Delete to LSMS

When a telephone number is being ported, the NPAC currently sends a request to the LSMS to create a new subscription version object. The LSMS is expected to search in its database to see if any existing subscription version object has the same telephone number. If such an object is found, the LSMS is expected to delete the existing object. This requirement is not documented in the FRS or IIS.

FRS/IIS

The suggested solution is to have the IIS adhere to the TMN specification. The NPAC should issue an M-Delete message for an existing object before creating the new object. A variation would be for the NPAC to issue an M-Set instead of an M-Create or M-Action message.

| If neither of the above solutions is possible, the deviation from the standard specification should be explicitly called out in the FRS or IIS. |
| --- |
| NANC 144 | AGCS |

Filter implementation in the NPAC SMS

| FRS requirements RR3-5 and RR3-6 state that filters will be used for subscription broadcast. These requirements don't include subscription queries, mass updates and lnpDownload requests. Lockheed Martin has interpreted these requirements to include applying the filter on subscription queries and mass updates. Perot has interpreted the requirements as they are written. The only filter subscription broadcast. | Medium | FRS |
| --- | --- | --- |

| Release I CLOSED Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Final Resolution | Level of Effort |
| NPAC | LSMS SOA |
| NANC 126 | Nortel |

Use of Time in the Due Date

| It has been determined that the Lockheed System uses the time if specified in the Due Date where the Perot system normalizes the time to 00:00:00.0 when the time is specified. It has been requested that the Lockheed implementation be changed to normalize the time. | Low | IIS |
| --- | --- | --- |

Lockheed will make the change in a future release(see change order NANC 149)  but for relase 1 the time will not be specified by vendor systems.

| NANC 136 | Bellcore 8/10/97 |
| --- | --- |

Download File Carriage Return Clarification

The following clarifications should be made to the download file explanation in the FRS 1.4 and 2.2:

The sample NPA-NXX and LRN files should have a carriage return (CR) after each record.

The last record in each file should not be treated differently from any other record.  It should be followed with a (CR).

| The CR value is ASCII 13. | Low | FRS |
| --- | --- | --- |

FRS would be updated in the next release.

| Tekelec raised the use of CR as an issue. It has been proposed that the new line character (ASCII 0A) be used since it is recognized by Unix and C standard procedures. The group closed this item due to the fact that when the file is FTP-ed, not in binary mode, the CR would be converted to new line. | N/A | N/A |
| --- | --- | --- |
| NANC 140 | Sprint 8/18/97 |

Concurrence Timer Values

| The requirements (R5-21.3 and R5-23.3) state that the initial and final concurrence values should have default values of 9 hours. However, the system tunable table (Appendix C) states that the default is 18 hours. The table should be updated. | Low | FRS |
| --- | --- | --- |

The FRS should be updated in the next release.

Closed for FRS release 1.5.

NANC 141

Lockheed Martin Team

8/18/97

Cancel of Disconnect Pending

| The requirement R5-71.10 states “NPAC SMS shall set the subscription version status to Active upon receiving a cancellation for a subscription version with a status of disconnect pending.”. However, there are requirements R5-3.10, R5-3.11, and R5-3.12 that define a tunable parameter for retention of canceled versions with a pre-cancellation status of disconnect pending. This tunable is not needed and should be removed. The requirements R5-3.10, R5-3.11, R5-3.12 and the reference to the tunable in the table in appendix C should be removed. | Medium | FRS |
| --- | --- | --- |

The FRS should be updated in the next release.

Closed for FRS release 1.5.

| Release 2 Open Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Proposed Resolution | Level of Effort |
| NPAC | LSMS SOA |
| NANC 68 | Illinois |

Mass Update Requirements Modification

The current requirements R3-7.1 and R3-7.2 for Mass Update do not reflect the business need and should be replaced with the following:

R3-7.1	Select Subscription Versions mass changes for one or more Subscription Versions

NPAC SMS shall allow NPAC personnel to select Subscription Versions for mass update which match a user defined combination of any of the follow: TN, TN range, Service Provider ID, LRN, DPC values, SSN values, Billing ID, End User Location Type or End User Location Value.

R3-7.2 Administer Mass updated on one or more selected Subscription Versions

| NPAC SMS shall allow NPAC personnel to specify a mass update action to be applied against all Subscription Versions selected (except for Subscription Versions with a status of old, partial failure, sending, or canceled) for LRN, DPC values, SSN values, Billing ID, End User Location Type or End User Location Value. | High | FRS |
| --- | --- | --- |

This feature has been targeted for Release 2.

RE-OPENED:

M&P for throttling of changes to prevent impact to the LSMS’s and the networks.  This needed by Perot and Lockheed for next regional meeting. (e.g. one NPA-NXX etc.)

Lockheed will provide this information in M&P release 1.5 due out on 8/15.

Perot will provide M&P updates on at the Washington D.C. on 8/21 for review.

NANC 145

MCI

8/27/97

Notification Recovery Flows

| Flows need to be added in IIS 2.3 to show the recovery action being used by the SOA and LSMS. | Medium | IIS | Flows would be added to the IIS 2.3 release |
| --- | --- | --- | --- |

| Release 2 CLOSED Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Final Resolution | Level of Effort |
| NPAC | LSMS SOA |
| NANC 149 | Nortel |

Use of Time in the Due Date - Continued

It has been determined that the Lockheed System uses the time if specified in the Due Date where the Perot system normalizes the time to 00:00:00.0 when the time is specified.  It has been requested that the Lockheed implementation be changed to normalize the time.

The following IIS references to time would have to change:

| The Old and New Service Provider Due Dates would have the following GDMO sentence “If not specified, the time defaults to 00:00.00.” with “The time will be set to 00:00.0 regardless of what is specified.”. | Low | IIS | Lockheed will make this change in Release 2. The NANC 2.3 document will be updated. |
| --- | --- | --- | --- |

| Release 3 Open Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Proposed Resolution | Level of Effort |
| NPAC | LSMS SOA |
| ILL 5 | External Design Meeting 10/15/96 |

Round-Robin Broadcasts across LSMS associations

| The NPAC SMS would support the adding of additional LSMS associations and manage distributing transactions across the associations. For example, due to performance problems or high-availability requirements, an LSMS may want to start another association for network/subscription downloads...the NPAC SMS would accept the association, manage security, and distribute network/subscription PDUs across the 2 associations (One PDU per association invoke id.). | Medium Low | NPAC SMS functionality / IIS | This feature has currently been targeted for Release 3 if needed. | ? | Medium Low |
| --- | --- | --- | --- | --- | --- |
| ILL 8 | Lockheed Martin Team / 10/17/96 |

Portability Areas

| Establishment of Portability Areas (NPA-NXX groupings, such as a LATA or MSA). | Low | NPAC SMS functionality |
| --- | --- | --- |

This feature has been targeted for Release 3.  Detailed requirements have been developed.

| Related to ILL 9 and ILL 10. | Medium | N/A |
| --- | --- | --- |
| ILL 9 | Lockheed Martin Team / 10/17/96 |

Portability Area Specific Tunables

| Establishment of portability area Tunable Parameters to allow timing and feature functionality to vary by portability area within a Regional NPAC to satisfy potential regulatory differences. | Low | NPAC SMS functionality |
| --- | --- | --- |

This feature has been targeted for Release 3.  Detailed requirements have been developed.

| Related to ILL 8. | High | N/A |
| --- | --- | --- |
| ILL 10 | Lockheed Martin Team / 10/17/96 |

Billing Enhancements

| Performance of Cost Reapportionment and billing on a portability area basis to allow for different cost recovery methods employed or mandated by regulatory agencies, if applicable. | Low | NPAC SMS functionality |
| --- | --- | --- |

This feature has been targeted for Release 3.  Detailed requirements have been developed.

| Related to ILL 8. | Medium High | N/A |
| --- | --- | --- |
| ILL 17 | External Design Meeting 10/15/96 |

Report Size Warning

| A request was made to warn the user of the NPAC Operational GUI of the size of a report before its creation to prevent accidental creation of large reports. | High | NPAC SMS report functionality |
| --- | --- | --- |

A report size warning would be displayed to the user of the NPAC SOA Low-tech or NPAC Adminstrative Interface before the report is created in number of pages.  The user would then be given the option to continue or cancel.  If the user chooses to cancel then they should be returned to the report generation screen and be allowed to modify the report options or exit.

| This change order has been targeted for Release 3. | Medium | N/A |
| --- | --- | --- |
| ILL 23 | External Design Meeting 10/15/96 |

Detailed Integrity Sample Results Report

| A request was made for an additional NPAC SMS report for detailed integrity sample results. This report would list all of the discrepancies found for a given Data Integrity Sampling by service provider. | ? | FRS |
| --- | --- | --- |

Requirements would be added to the FRS.

This change order has been targeted for Release 3.

| There is also an issue being discussed on whether the discrepancies found should be fixed. | ? | N/A |
| --- | --- | --- |
| ILL 58 | External Design Meeting 10/29/96 |

Single Audit Report Modification

| For each discrepancy listed in the single audit report the service provider serving the TN should be specified in addition to the service provider who has a discrepancy for that TN. | Low | FRS, IIS |
| --- | --- | --- |

FRS requirement R8-21.2 would be modified to add a bullet  as follows:

Identification of SP owning the TN for which the discrepancy was found.

The single audit report in the External design would

also be modified.

| This change order has been targeted for Release 3. | Low | Low |
| --- | --- | --- |
| ILL 75 | Forum Meeting 11/19/96 |

Validate Due Date is > than the NPA-NXX effect date upon Pending Version Creation

| A request has been made for additional requirements for due date validation upon pending version creation for an NPA-NXX that is not in effect. The due date would not be considered valid if it was not greater than the NPA-NXX effective date. This change would keep activations of a pending subscription version from occurring before the effective date of an NPA-NXX. | Medium High | FRS and NPAC SMS functionality | This feature has been targeted for Release 3. | Low | Low |
| --- | --- | --- | --- | --- | --- |
| ILL 130 |

AT&T

1/6/97

Application Level Errors

| Errors in the SOA interface are being treated as CMIP errors and it may sometimes be difficult for a SOA to know the true reason for an error from the NPAC SMS and therefore indicate a meaningful error message to its users. It has been requested that application level error be defined where appropriate and returned as text to the SOA. | High | IIS |
| --- | --- | --- |

This feature has been targeted for Release 3.

| Application level errors would be defined in the IIS. | High | Medium High |
| --- | --- | --- |
| ILL 183 |

MCI

2/14/97

Download of Service Provider Data ASN.1 Issue

The NetworkDataDownload ASN.1 definition is as follows:

NetworkDownloadData ::= SET OF SEQUENCE {

service-prov-data [0] SEQUENCE {

service-prov-id ServiceProvId,

service-prov-name ServiceProvName

OPTIONAL

},

service-prov-npa-nxx-data [1]

NPA-NXX-DownloadData OPTIONAL,

service-prov-lrn-data [2] LRN-DownloadData

OPTIONAL

}

| NPA-NXX_DownloadData and LRN-DownloadData both have download reason which basically specify whether to add, delete or modify instances, however, service_prov_data does not. There is not an way to indicate that a serviceProvNetwork object has been deleted in a network data download. | Medium | IIS |
| --- | --- | --- |

It is proposed that since service provider deletion is not a frequent activity that addition of this functionality be added in a later release.

| This change has been targeted for Release 3. | Medium | Medium |
| --- | --- | --- |
| NANC 34 |

Perot

3/17/97

AuditServiceProvIdRange ASN.1 Modification

| It has been suggested that serviceProvName be modified to be ServiceProvId. ServiceProvId is guaranteed to be unique. | Medium Low | IIS ASN.1 |
| --- | --- | --- |

This feature has been targeted for Release 3.  Detailed requirements have been developed.

| A request has been made to Lockheed and Perot to provide information on what would occur today if a name were ambiguous. | Medium Low | Medium Low |
| --- | --- | --- |
| NANC 35 |

Perot

3/17/94

ContactPagerPin ASN.1 Modification

| In IIS 1.5 contactPagerPIN is a digit string without length. It has been requested that this be bound to the length of 10 as specified in the FRS. | Low | IIS ASN.1 | This feature has been targeted for Release 3. Detailed requirements have been developed. | Low | Low |
| --- | --- | --- | --- | --- | --- |
| NANC 44 |

MFS

3/24/97

Effective Release Date Validation

| The effective release date is on optional value that can be used in conjunction with a disconnect. This is the date the NPAC removes the subscription from the LSMS's. Without this date the NPAC doesn't do any data validation on the customer due date but does an immediate broadcast to remove the subscription from the LSMS's. If a subscription is erroneously entered without this date a customer would be removed from the LSMS's in error. It has been decided that the NPAC will validate the effective release date to insure that it is greater than or equal to the due date. If the effective release date is not greater than or equal to the due date then the disconnect request will be rejected with an invalid attribute for the effective release date. If the effective release date is not specified it is assumed to be the date of the request. | High | FRS |
| --- | --- | --- |

This feature has been targeted for Release 3.  Detailed requirements have been developed.

|  | Medium Low | N/A |
| --- | --- | --- |
| NANC 45 | NANC meeting 3/24/97 |

Audit a list of Service Providers

| The capability should be added to the audit functionality to audit a list of Service Providers. Currently the requirement (R8-3) states that audits are for all or one service provider. The IIS would have to be modified to reflect this change. | Medium Low | FRS / IIS / ASN.1 | This feature has been targeted for Release 3. Detailed requirements have been developed. | Medium | Medium |
| --- | --- | --- | --- | --- | --- |
| NANC 48 | NANC meeting 3/24/97 |

Multiple SPIDs per Service Provider SOA

| It has been requested that multiple Service Provider Ids be associated with a single service provider SOA within an NPAC SMS. This issue is currently being investigated and proposed requirements are being developed. | Medium High | FRS / IIS / GDMO / ASN.1 |
| --- | --- | --- |

This feature has been requested for a future release. This change has not been associated with a group.

Additional business and technical write-ups were provided for the 4/25 call as a follow up to previous write-ups and discussions.

Vendors are to assess the proposed solutions for impact and be prepared to discuss these at the NANC T&O meeting on 5/13.

| Option 2 from the e-mail is the approach for which the effort sizing is done. | High | High |
| --- | --- | --- |
| NANC 114 | Lockheed Martin Team 6/23/97 |

Download subscripion-version-id optional

| The "subscription-version-id" is defined as optional in ISS 2.0 in the SubscriptionDownloadData but it should be required. The OPTIONAL tag should be removed. The tagging could also be removed from the ASN.1. | High | IIS / ASN.1 |
| --- | --- | --- |

This change should be made in the IIS.

|  | Medium Low | Medium Low |
| --- | --- | --- |

Release 3 CLOSED Change Orders

| Chg Order # | Orig. / Date | Description | Priority | Category | Final Resolution | Level of Effort |
| --- | --- | --- | --- | --- | --- | --- |
| NPAC | LSMS SOA |

| Release 4 Open Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Proposed Resolution | Level of Effort |
| NPAC | LSMS SOA |
| ILL 67 | Ameritech / 11/08/96 |

DPC Validation

The NPAC SMS should have a DPC table which would validate valid DPC data for each service provider.  This validation would be performed by the NPAC SMS on any subscription version transactions.  This enhancement would support the Service Providers' abilities to maintain

| network reliability. Current design will allow any DPC data to broadcast throughout the entire serving area's networks. If invalid data were to be broadcast this would be a difficult to troubleshoot and identify the source of trouble. | Hold | IIS |
| --- | --- | --- |

This feature has been requested for Release 4.  Detailed requirements need to be developed.

Pending review by originator before moving to pending delete.

| Release 4 CLOSED Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Final Resolution | Level of Effort |
| NPAC | LSMS SOA |

| Future Release Open Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Proposed Resolution | Level of Effort |
| NPAC | LSMS SOA |
| ILL 186 |

2/22/97

Ameritech

Mass Update Failure Criteria Change

In the current Lockheed implementation for Mass Updates, versions that are in sending and partially failed download states will prevent the whole mass update from proceeding.    It has been requested that these versions be treated as exceptions and that the mass update be allowed to proceed for those versions that are currently in a sending or partially failed state in addition to those defined in the requirements.

This change is related to requirements R3-6, R3-7.1, and R3-7.2.

| The exceptions should be printed in a report and in some manner be corrected via an operational Methods and Procedure process. | Medium High | NPAC SMS |
| --- | --- | --- |

This feature has been requested for a future release. Detailed requirements need to be developed.  It is currently ungrouped.

In the Perot the mass update is implemented best effort with no error report on the broadcasts.

|  | Medium Low | N/A |
| --- | --- | --- |
| NANC 46 | NANC meeting 3/24/97 |

NPAC to NPAC

| NPAC to NPAC exchange of information has been requested as a potential NPAC SMS enhancement. Currently this issue is being investigated and framed for the group. | Hold | FRS |
| --- | --- | --- |

This feature has been requested for a future release.  Detailed requirements need to be developed. This change has not been associated with a group.

| The working group is working on this from paragrah 22 2nd report and order (the order number is 97289). A report is due on October 7th. It will be sent be sent to the group prior to October 7th if possible. |
| --- |
| NANC 47 | NANC meeting 3/24/97 |

Time Zone

| Handing of multiple time zones within an NPAC SMS has been requested as a potential NPAC SMS enhancement. Currently this issue is being investigated and framed for the group. | Low | FRS |
| --- | --- | --- |

This feature has been requested for future release.  Detailed requirements need to be developed. This change has not been associated with a group.

| This functionality may be covered by ILL 9. | ? | ? |
| --- | --- | --- |
| NANC 49 |

GTE

3/26/97

Multiple SP Contacts for a Contact Type

The FRS 0.1 and associated GDMO / ASN.1 in the IIS 1.5 currently allows only a single entry for each Service Provider Contact Type.  See Table 3.3 - NPAC Customer Contact Data Model in the FRS for additional information on the Service Provider Contact Type.

The operational impact of this is that the NPAC personnel are only allowed to take requests and send responses, reports, etc., to personnel and locations contained in the Service Provider Data.  This creates a problem for Service Providers with multiple Operations Centers.  It has been propose that each Contact Type in the Service Provider Data be allowed to contain multiple entries. Suggested text for an additional FRS requirement to support multiple entries for each Contact Type is shown below:

R4-8.2   Multiple Entries for each Service Provider Data Contact Type

| NPAC/SMS shall support multiple entries of all Contact Types in the Service Provider Data. | Medium Low | FRS / IIS / GDMO |
| --- | --- | --- |

This feature has been requested for a future release.  Detailed requirements need to be developed. This change has not been associated with a group.

|  | Medium Low | Medium Low |
| --- | --- | --- |

NANC

77

AT&T

4/16/97

TimeRange ASN.1 Definition

| The startTime and stopTime of TimeRange are defined as OPTIONAL. Since all requests involving TimeRange will include startTime and stopTime, the OPTIONAL is not needed and should be removed. | Low | IIS/ASN.1 | The IIS will be updated. This change order has not been grouped. | Low | Low |
| --- | --- | --- | --- | --- | --- |
| NANC 80 | NANC 4/18/97 |

Audit indication of SP’s not Audited Due to a Download Filter

| It has been requested that the audit results indicate the service providers not audited due to download filtering. | Medium | FRS / IIS / GDMO / ASN.1 | This feature has been requested for a future release. This change has not been associated with a group. | Medium Low | Medium Low |
| --- | --- | --- | --- | --- | --- |
| NANC 81 | NANC 4/18/97 |

Audit Download Filtered LSMS

| It has been requested that audits be allowed to audit LSMS’s that have download filtered NPA-NXX’s always or only upon request. Today audits are not performed on Local SMS’s for filtered NPA-NXX’s. | Hold | FRS / IIS / GDMO / ASN.1 |
| --- | --- | --- |

This feature has been requested for a future release. This change has not been associated with a group.

Audit changes are very low priority so this change order has been put on hold.

Repair would be to recognize the filter and not add the TN if a missing filtered Tn is found and to delete a filtered TN if found.

|  | Medium | N/A |
| --- | --- | --- |
| NANC 90 |

MCI

4/30/97

SP Download Indicator Addition to IIS

| RR3-1 and RR3-2 refer to a download indicator. This download indicator is associated with a SP but is not available for modification/viewing over the CMIP interface. It has been requested that it be added in a future release. | Low |
| --- | --- |

IIS/ASN.1/

| GDMO | This feature has been requested for a future release. This change has not been associated with a group. |
| --- | --- |
| NANC 103 |

AT&T

5/23/97

Increase in OSI Selector Size

| Currently in the IIS and FRS the OSI TSAP, SSAP, and PSAP sizes are limited to 4 characters. It has been requested that these be increased in size. | Medium |
| --- | --- |

IIS/ASN.1/

FRS

This feature has been requested for a future release.

| The selector would be defined as a range from 4…?. The originator is being contacted to determine what the upper bound would be. | Medium High - ? | Medium Low |
| --- | --- | --- |
| NANC 104 |

Bellcore

5/23/97

Delta Download File Creation by Time Range

| It has been requested that a requirement be added to the FRS to allow for creation of a delta download files by time range. | Hold | FRS |
| --- | --- | --- |

This feature has been requested for a future release.

This item is on hold until further experience is gained with download This change is expected to help with a service provider catch-up faster after an extend outage when the database becomes large.

NANC 108

NANC

6/8/97

IIS Discrepancy with R5-26

| Requirement R5-26 in the FRS 1.2 states that the status is required for the modification of a subscription version. The IIS has this field as optional. A change should be made to the IIS ASN.1 for ModifyAction to remove OPTIONAL tag on the version-status field. | MR | IIS/ASN.1 | This IIS will be updated in a future release. | Low | Low |
| --- | --- | --- | --- | --- | --- |
| NANC 109 |

NANC

6/9/97

Number Pooling

| Number Pooling has been requested for a future NPAC release. E-mail has been sent to the group to begin initial discussion. | Hold | FRS |
| --- | --- | --- |

This change has been requested for a future release.

Pending INC decision

NANC 121

AGCS

7/16/97

lnpSpecificInfo attribute

It has been pointed out that lnpSpecificInfo is an orphan attribute (and an orphan parameter). Some toolkits optimizes out the code for this attribute because it is not bound to any managed object. It has been requested that the references be made explicit.

IIS

This change order is currently ungrouped.

| The group has decided not to implement changes for certain compiler implementations. Many vendors have to change the file to accommodate their OSI tool kits. |
| --- |
| NANC 122 | NANC 7/17/97 |

Enhanced Key Expiration Strategy

It has been requested that the key exchange strategy be revised for a more secure implementation.  The strategy would be as follows:

NPAC would expire its key when:

an abort from a service provider occurs on an active association.

a key change is desired.

Service Providers would expire their key when:

an abort from the NPAC occurs on an active association.

when accessDenied is returned.

a key change is desired.

| This change request is related to the Release 1 change order NANC 112. | Hold | FRS/IIS |
| --- | --- | --- |

This change order is currently ungrouped.

The group is unsure of the need to change the key exchange strategy at this time.

NANC 129

8/5/97

AT&T

End User Location Type and Value Definition

In the NANC IIS V1.2 the following ASN.1 definitions are found:

EndUserLocationType ::= CHOICE {

value [0] NumberString(SIZE2)),

no-value-needed [1] NULL

}

EndUserLocationValue ::= CHOICE {

value [0] NumberString(SIZE(1..12)),

no-value-needed [1] NULL

}

However, in the FRS V1.2 the following is found in Table 3-5:

End User Location Type C(2)

End User Location Value C(12)

| where "C" is defined as "Character or Alphanumeric Strings". | Low | FRS/IIS -? | Should the IIS be changed to match the FRS or vise versa? |
| --- | --- | --- | --- |
| NANC 131 |

AT&T

8/5/97

LRN-DownloadData Modification

In LRN-DownloadData the LRN Value should be optional. Due to the fact that when we try deleted LRN or NPA-NXX, we get sent only the ID and the DownloadReason not the LRN value. Note that the NPA-NXX value is optional in the NPA-NXX –DownloadData.

LRN-DownloadData ::= SET OF SEQUENCE {

Service-prov-lrn-id LRN-ID,

service-prov-lrn-value LRN Optional,

service-prov-download-reason DownloadReason,

service-prov-lrn-creation-timestamp GeneralizedTime OPTIONAL

| } | MR | IIS/ASN.1 | Update the IIS and ASN.1 in a future release. | Low | Low |
| --- | --- | --- | --- | --- | --- |
| NANC 133 |

ESI

8/5/97

Audit Object Definition

| The IIS contradicts it self for the audit object. The subscriptionAuditBehavior states that "All attributes must be specified on create with the exception of the subscriptionAuditAttributeList and the subscriptionAuditTN-ActivationRange". If this is the case, then the subscriptionAuditAttributeList and subscriptionAuditTN-ActivationRange must have default values. By default all attributes are required on M-CREATEs. | Low | IIS |
| --- | --- | --- |

The IIS would be updated.

| Holly from ESI is investigating this change order. It may be withdrawn. | Medium Low | Medium Low |
| --- | --- | --- |
| NANC 139 | Ameritech 8/12/97 |

Network Data Download to SOA

| A request has been made to allow network data downloads (M-CREATE, M-DELETE, and M-SET) to be sent to and of applicable instantiated on the SOA in addition to the LSMS (i.e. Service Provider, LRN and NPA-NXX information). This functionality would be implemented such that a service provider could specify to the NPAC wether the want to receive data on the LSMS only, the SOA only, or both LSMS and SOA. | Medium | IIS/FRS | The IIS and FRS would be updated in a future release | Medium High | High |
| --- | --- | --- | --- | --- | --- |
| NANC 146 | Bellcore 8/27/97 |

SP Contact Data Handling

| Currently there is no way to delete or blank out Service Provider contact data in the profile. The attributes do not have a NULL or absent setting. The ANS.1 should be changed for the address information to be a choice of the address information or NULL. |
| --- |
| IIS/ASN.1 |
|  | NANC 147 | AT&T 8/27/97 |

Version ID rollover stragegy

| Currently there is no strategy defined for rollover if the maximum value for any of the id fields (sv id, lrn id, or npa-nxx id) is reached. One should be defined so that the vendor implementations are in sync. Currently the max value used by Lockheed is a 4 byte signed integer and for Perot it is a 4 byte unsigned integer. |
| --- |
| FRS |
|  | NANC 148 |

Bellcore

8/25/97

LNP Type in  SV Object Creation Notification

It has been requested that "LNP Type" be added to the subscription version object object create notifications.

IIS/ASN.1/GDMO

| Future Release CLOSED Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Final Resolution | Level of Effort |
| NPAC | LSMS SOA |

| Pending DELETE Change Orders |
| --- |
| Chg Order # | Orig. / Date | Description | Priority | Category | Final Resolution | Level of Effort |
| NPAC | LSMS SOA |
| ILL 65 | Ameritech / 11/08/96 |

Network Level Audit

| The NPAC SMS should provide the capability to have audit processing down to the network element level. This would require the NPAC-LSMS interface to support functionality including asynchronous responses from the LSMS for audit processing down to the SCP level. | Pending DELETE as of 8/22/97 | IIS |
| --- | --- | --- |

This feature has been requested for Release 4.  Detailed requirements need to be developed.

| Withdrawn by originator. |
| --- |
| ILL 66 | Ameritech / 11/08/96 |

Network Level Activation Capability

| The NPAC SMS should provide the capability to process activate messages down to the network element level. This would require the NPAC-LSMS interface to support asynchronous responses from the LSMS for activation responses to the SCP level. | Pending DELETE as of 8/22/97 | IIS |
| --- | --- | --- |

This feature has been requested for Release 4.  Detailed requirements need to be developed.

Withdrawn by originator.

| ILL 77 | Forum Meeting 11/19/96 |
| --- | --- |

Modification of NPA-NXX effective date

| A requests was made to allow the modification of the NPA-NXX effective date over the interface. This includes the ability to M-SET to the NPAC SMS from the Local SMS and SOA interface as well as the capability to M-SET the value from the NPAC SMS to the Local SMS. Existing pending versions with a due date less than the new effective date would have to be handled to prevent the due date from being less than the effective date. | Pending DELETE as of 8/8/97 | IIS, FRS |
| --- | --- | --- |

This change order has been targeted for Release 3.

| There was a move to delete this change due to the fact there is a manual work around and there seems to not be an straight forward approach to handling pending versions. | ? | ? |
| --- | --- | --- |
| ILL 187 |

2/22/97

AT&T

NXX split handling for 6 digit

| Currently there are no requirements or functionality in the NPAC SMS to address NPA-NXX splits only NPA splits. Further investigation and requirement development needs to be done to support this functionality. | Pending DELETE as of 8/22/97 | NPAC SMS |
| --- | --- | --- |

This feature has been requested for a future release.  Detailed requirements need to be developed. This change has not been associated with a group.

Change order withdrawn by the originator.

ILL 134

Worldcom

1/8/97

Do Not Allow Port for the New NPA-NXX Involved in an Split Prior to Permissive Dialing Window

| It was requested that a check be put into the NPAC to insure that a pending port was not created for the new NPA-NXX involved in the split prior to the permissive dialing period. It was felt that setting the effective date of the new NPA-NXX to the same time as the permissive dialing period start was not enough of a safe guard. | Pending DELETE as of 8/22/97 | FRS |
| --- | --- | --- |

This feature has been requested for Release 4.  Detailed requirements need to be developed.

| Group felt that this functionality was unnecessary. Originator has been contacted. |
| --- |
| NANC 79 | NANC 4/18/97 |

Multiple SPIDs per Service Provider LSMS

| It has been requested that multiple Service Provider Ids be associated with a single service provider LSMS within an NPAC SMS. Further business requirements need to be developed. | Pending DELETE as of 8/8/97 | FRS / IIS / GDMO / ASN.1 |
| --- | --- | --- |

This feature has been requested for a future release. This change has not been associated with a group.

| This change order is associated with NANC 48. | ? | ? |
| --- | --- | --- |
| NANC 82 | NANC 4/25/97 |

Mass Update SPID

| A request has been made to add SPID as an attribute to be modified for situations where service providers sell property or merge. | Pending DELETE as of 8/22/97 | FRS |
| --- | --- | --- |

This feature has been requested for a future release.  This change has not been associated with a group.

Pending delete due to coverage in NANC 68.

NANC 121

AGCS

7/16/97

lnpSpecificInfo attribute

| It has been pointed out that lnpSpecificInfo is an orphan attribute (and an orphan parameter). Some toolkits optimizes out the code for this attribute because it is not bound to any managed object. It has been requested that the references be made explicit. | Pending DELETE as of 8/22/97 | IIS |
| --- | --- | --- |

This change order is currently ungrouped.

| The group has decided not to implement changes for certain compiler implementations. Many vendors have to change the file to accommodate their OSI tool kits. |
| --- |
| NANC 125 | ESI/AT&T 7/25/97 |

Intra Service Provider Port – Port to Original

Some confusion has occurred regarding support of porting to original in an intra-service provider port.  The FRS in section 5.1.2.2.1.2 Subscription Version  Creation - Intra-Service Provider Port  states the following: “This section provides the Subscription Version Creation requirements for performing an Intra-Service Provider port of a TN. An Intra-Service Provider port of a TN is when a TN is ported to a new location within the current Service Provider network (i.e., the routing data is modified, but the Service Provider remains the same).  A port to original port for an Intra-Service Provider port should be handled by a requesting user via submission of a Disconnect request to the NPAC SMS. Requirement R5-15.2 “Create “porting to original” Subscription Version - New Service Provider Input Data” states the following about the  port to original flag: NPAC SMS shall require the following data from NPAC personnel or the new Service Provider upon Subscription Version creation for an Inter-Service Provider “porting to original” port:

Porting to original – flag indicating whether or not this is a “porting to original” port.  This flag must be set to “TRUE” for “porting to original” port.

There is no mention of this field in the intra-service provider port section.

Pending Delete on 8/22/97

|  | FRS |
| --- | --- |

Support of port to original porting for intra-service provider porting has been requested. This change has been targeted for release 3.

The group felt that the current process in place (use of disconnect) was sufficient.

NANC 130

ESI

8/5/97

Notification to Old SP on Subsequent Port

The old service provider is getting the activate notification after the initial activate but when that TN is ported the next time to another service provider the old service provider does not get the status notification that the previously active subscription version is going to old.

| Should this notification be sent? In the current process flows and requirements there is no requirement to notify the old service provider on a previously ported number when it ports again. | Pending DELETE as of 8/15/97 | FRS/IIS |
| --- | --- | --- |

The group initially felt that this change order should not be implemented.  Research is to be done to determine if there really is a strong need for this functionality in SOA systems.

The submitter withdrew this change request. Closed Pending Deletion

NANC 132

MCI

8/5/97

Update FRS Data Models

| Several issues found in testing that had to do with data fields - what constitutes valid data in all fields, both those that may or may not be required. In order that we do not continue to stumble across these things one at a time during testing or as new SPs come on board, it has been requested that the data models be updated. They should be updated to reflect what constitutes valid data for each field. | Pending DELETE as of 8/22/97 | FRS |
| --- | --- | --- |

Upon further review no changes to the data models could be identified by the CMA.

This change order will be left open for further review by the initiator.

Deleted by initiator.

| Release # / Target Date | Change Orders | Backwards Compatible |
| --- | --- | --- |

Release 2

January 1 – test

February 21 – GA

September 2nd…evaluation due.

ILL 3 – NPA-NXX Filter enhancements (GDMO/ASN.1 impact)

ILL 79 – Notification Recovery (GDMO/ASN.1 impact)

NANC 68 – Mass Update Requirements Modification

NANC 120 - Filter Deletion

NANC 149 – Use of time in due date – continued

Y

Y

Y

Y

Y

Release 3

June 98 – GA

ILL 5 – Round Robin LSMS

ILL 8 – Establish Portability Areas

ILL 9 – Portability Area Specific Tunables

ILL 10 – Portability Area Billing Enhancements

ILL 17 – Report Size Warning

ILL 23 – Detailed Integrity Sampling Report

ILL 58 – Owning SP for TN in Audit Report

ILL 75 – Validate Due Date is > than the NPA-NXX effect date upon Pending Version Creation

ILL 130 – Application Level Errors (ASN.1 impact)

ILL 131 – Old SV for each change requirements enhancement

ILL 183 - Download of Service Provider Data (ASN.1 impact)

NANC 34 – AuditServiceProvIdRange (ASN.1 impact)

NANC 35 – ContactPagerPin (ASN.1 impact)

NANC 44 – Effective Release Date Validation

NANC 45 – Audit a list of  Service Providers (ASN.1 impact)

NANC 48 – Multiple Service Provider Ids per SOA Association

NANC 114 - Download subscripion-version-id optional

Y

Y

Y

Y

Y

Y

Y

Y

?

Y

?

Y

Y

Y

?

?

Y

Release 4

| December 98 – GA | ILL 67 – DPC Validation |
| --- | --- |
|  | Not Grouped |

ILL 186 - Mass Update Failure Criteria Change

NANC 46 - NPAC to NPAC

NANC 47 - Time Zone

NANC 49 - Multiple SP Contacts for a Contact Type

NANC 77 – Time Range ASN.1 definition

NANC 80 - Audit indication of SP’s not Audited Due to a Download Filter

NANC 81 - Audit Download Filtered LSMS

NANC 90 – SP Download Indicator in IIS

NANC 103 – Increase in OSI Selector Size

NANC 104 – Download File Creation by Time Range

NANC 108 – IIS Discrepancy with R5-26

NANC 109 – Number Pooling

NANC 122 – Enhanced Key Expiration Strategy

NANC 129 - End User Location Type and Value Definition

NANC 131 - LRN-DownloadData Modification

NANC 133 - Audit Object Definition

NANC 139 - Network Data Download to SOA

NANC 146 – SP Contact Data Handling

NANC 147 – Version ID rollover strategy

NANC 148 – LNP Type in SV Object Creation Notification

Y

?

Y

?

Y

?

?

Y

Y

Y

Y

Y

Y

Y

Y

Y

Y

?

?

?