Change Order Number: NANC 204

IMPACT/CHANGE ASSESSMENT

| FRS | IIS | ASN.1 | GDMO | NPAC | SOA | LSMS |
| --- | --- | --- | --- | --- | --- | --- |
| Y | Y | Y | Y | Y | Y | N |

Inter Service Provider Communication Process

Subscriber Name, Address, City, State, Zip have been requested as information to be exchanged between old and new SP’s when creating a pending port.  This information originates from the new service provider only.  This data would not remain in the NPAC SMS after the port has been activated or cancelled. Data would be needed in the Create Subscription Version Initial Concurrence Window (T1 Timer), Create Subscription Version Final Concurrence Window (T2 Timer), and object creation notifications to service providers that support Inter Service Provider processing. It is believed at this time that the address information definition in the NANC IIS for the NPAC SMS customer contact data is sufficient for wireless use.   The current definition is as follows:

| Field | Size/Type |
| --- | --- |
| Name | 40 character |
| Address Line 1 | 40 character |
| Address Line 2 | 40 character |
| City | 20 character |
| State | 2 character |
| Zip | 9 character |
| Country | 20 character |
| Province | 2 character |

NOTE:  The NPAC Vendor must provide performance impact information for this change order at the time of sizing.

Process Flow

The process flow for “Subscriber Name and Address Mismatch” is shown on the diagram on the next page.

FRS Requirements

Key points for requirements written below are as follows:

Only the new Service Provider can specify customer informationsubscriber name and address on a create message.

Only the new Service Provider can modify the customer informationsubscriber name and address prior to concurrence by the old Service Provider.  An attribute value change notification will be emitted to the old and new service provider when the subscriber name and address is modified.

Issue: Can the new Service Provider modify customer information or should it be prevented?  It was consensus that modification of the subscription version by the new service provider should be prevented by the NPAC SMS after concurrence by the old service provider occurs.   The question remains as to whether the information should be allowed to be modified at all.

The customer informationsubscriber name and address can only be queried (or read) by the old and new service provider prior to activation or approximately two days (between 48 and 72 hours, depending on the time of execution of the cancellation purge job on the NPAC SMS and the time the subscription was cancelled) after cancellation of the subscription version (i.e., when the subscription version is in a “pending” state).   This data will not be present on the subscription version after activation or approximately two days after cancellation (once the cancellation purge job is executed on the NPAC SMS).

Issue:  Should customer information be viewable in cancelled state by old and new SP?  Should information be purged after due date + 1 day?  One idea would be to have the Subscription Version go into cancel pending and allow it to remain there for due date + 1 day before cancellation.

For backward compatibility, the Service Provider profile will have to have an indicator on whether or not the service provider, as the old service provider, supports receipt of customer informationsubscriber name and address.

If the old service provider does not support receipt of customer informationsubscriber name and address in the subscription version create from, the NPAC SMS will reject the new service provider subscription version create containing customer informationsubscriber name and address.

If an old Service Provider supports customer informationsubscriber name and address then the data would be present on the initial object creation notification sent to the old service provider if the new service provider provided customer informationsubscriber name and address.

If an old Service Provider supports customer informationsubscriber name and address then the data would be present on the T1 notification (i.e. the first request for concurrence) sent to the old service provider if the new service provider provided customer informationsubscriber name and address.

If an old Service Provider supports customer informationsubscriber name and address then the data would be present on the T2 notification (i.e. the final request for concurrence) sent to the old service provider if the new service provider provided customer informationsubscriber name and address

If the old Service Provider does not agree with the customer informationsubscriber name and address specified by the new Service Provider then they can send a subscription version cancellation for FOC/LSR mismatch.  This would cause the subscription version to be cancelled and a cause code to be set as specified by the old service provider.

The only cause codes that can be sent with a subscription version cancellation for FOC/LSR mismatch are cause codes specifically defined for that purpose.  These FOC/LSR mismatch cause codes can not be used in existing conflict processing and vise versa.

Existing conflict processing can occur at any point for a subscription version with customer informationsubscriber name and address specified.

Inter-Service Provider Processing for Customer InformationSubscriber name and address Mismatch

The following is a process flow forproposed for discussion purposes for handling of situations were customer informationsubscriber name and address mismatch were data provided by the new service provider is not as expected by the old service provider.

The new service provider creates a subscription version with customer informationsubscriber name and address specified.

The old service provider determines that the customer informationsubscriber name and address does not match what is expected and proceeds to step 3 or step 6 otherwise proceed to step 9.

The old service provider may contact the new service provider to have them modify the subscriber name and address..

The New Service Provider may modify the subscriber name and address.  If the subscriber name and address is modified an attribute value change notification is sent to for the subscriber name and address.

If the old service provider is satisfied proceed to step 9 or if the modification did not occur or the old service provider is not satisfied the old service provider could proceed to step 3 or step 6.

The old service provider issues cancels thea subscription version cancellation for FOC/LSRsubscription version name and address mismatch specifying a cause code such as “address mismatch”.

The subscription version is cancelled and the cause code specified by the old service provider is specified in the subscription version.

The new service provider must may contact the old service provider to discuss the conflict before issuing another subscription version create for the TN that was cancelled.

The old service provider may optionally contact the new service provider after cancellation of the subscription version for FOC/LSRsubscription version name and address mismatch.

Porting can proceed as usual with a new subscription version if cancellation has occurred or with the existing subscription verisonversion.

Requirement 1 – Input of Subscription Version Customer InformationSubscriber name and address

NPAC SMS shall support the input of subscription version customer informationsubscriber name and address used for inter-service provider communication only from the new service provider.

Requirement 2.1 – Modification of Subscription Version Customer InformationSubscriber name and address

NPAC SMS shall support the modification of subscription version customer informationsubscriber name and address used for inter-service provider communication only by the new service provider prior to old service provider concurrence.

Requirement 2.2 – Modification of Subscription Version Subscriber name and address – Error

NPAC SMS shall reject a modification of a subscription version subscriber name and address used for inter-service provider communication by the new service provider after old service provider concurrence.

Requirement 2.3 – Modification of Subscription Version Subscriber name and address – Service Provider Notification

NPAC SMS shall send the subscription version subscriber name and address to the old and new service provider supporting inter-service provider communication in the attribute value change notification that occurs when the new service provider modifies the subscriber name and address.

Requirement 3 – Query Support of Subscription Version Customer InformationSubscriber name and address

NPAC SMS shall support the query by the old and new service provider of subscription version customer informationsubscriber name and address used for inter-service provider communication prior to subscription version activation or approximately two days after cancellation (between 48 and 72 hours, depending on the time of execution of the cancellation purge job on the NPAC SMS and the time the subscription was cancelled).  Note: The subscription version customer informationsubscriber name and address can not be queried after activation or approximately two days after cancellation.

Assumption 1 – Unique Wireless and Wireline Service Provider Ids.

Service providers supporting wireless porting will have unique wireless and wireline Service Provider Ids. One service provider id can not support both wireless and wireline porting activity if wireless and wireline support for FOC/LSR is different..

Requirement 4 – Service Provider Profile – Customer InformationSubscriber name and address Acceptance Indicator

NPAC SMS shall support an indicator in the service provider profile as to whether or not the service provider, as the old service provider, supports the receipt over the SOA to NPAC SMS interface of subscription version customer informationsubscriber name and address for inter-service provider communication.

Requirement 5 – Service Provider Profile - Customer InformationSubscriber name and address Acceptance Indicator Default

NPAC SMS shall default to false (not supported) the indicator in the service provider profile as to whether or not the service provider, as the old service provider, supports the receipt over the SOA to NPAC SMS interface of subscription version customer informationsubscriber name and address for inter-service provider communication.

Requirement 6 – Customer InformationSubscriber name and address in Old Service provider Creation Notification

NPAC SMS shall send the subscription version customer informationsubscriber name and address to the old service provider supporting inter-service provider communication on in the creation notice sentnotice sent  when the subscription version is sent to pendingupon initial subscription version creation.

Requirement 7 – Customer InformationSubscriber name and address in Old Service Provider Initial Concurrence Notification

NPAC SMS shall send the subscription version customer informationsubscriber name and address to the old service provider supporting inter-service provider communication in the notification that occurs when the initial concurrence window expires.

Requirement 8 – Customer InformationSubscriber name and address in Old Service Provider Final Concurrence Notification

NPAC SMS shall send the subscription version customer informationsubscriber name and address to the old service provider supporting inter-service provider communication in the notification that occurs when the final concurrence window expires.

Requirement 9 – Rejection of New Service Provider Create for Customer InformationSubscriber name and address

NPAC SMS shall reject the subscription version create message from the new service provider containing customer informationsubscriber name and address if the old service provider does not support inter-service provider communication.

Requirement 10 – Cancellation of Pending Subscription for Inter-Service Provider InformationSubscriber name and address

NPAC SMS shall allow the old service provider to cancel a pending subscription version for a customer informationsubscriber name and address mismatch if they have not concurred to the subscription version containing customer informationsubscriber name and address.

Note: Cancellation can occur for other reasons using the existing cancellation process defined.

Requirement 11 – Cancellation of Pending Subscription for Inter-Service Provider InformationSubscriber name and address - Setting of the Cause Code

NPAC SMS shall allow upon cancellation of a pending subscription version that contains customer informationsubscriber name and address that the old service provider does not concur with set the cause to the value specified by the new old service provider and set the subscription version status to cancel.

Note: Currently an order can only be put into conflict one time.  If the order is put into conflict during FOC/LSR processing it can not be put into conflict again for another reason.

Requirement 12 - SOA to NPAC SMS Cancellation of Pending Subscription Version for Inter Service Provider InformationSubscriber Name and Address Mismatch via an NPAC SOA Low-tech Interface

NPAC SMS shall support cancellation of Subscription Versions by the old service provider for inter-service provider informationsubscriber name and address mismatch via a secure, NPAC SOA Low-tech Interface.

Section 3 Modifications

In the subscription version data model in section 3, a new cause code value will be added as follows:

The following cause codes can only be used for Cancellation of a subscription version that contains customer informationsubscriber name and address that the old service provider does not concur with.  These cause codes are only valid for this type of cancellation and can not be used for any other processing.

Name Mismatch     - 100080

Address Mismatch  - 100181

Name and Address Mismatch - 1002Others??

The service provider profile would be updated in Table 3-2 as follows to add:

| NPAC New Functionality Support | M | ( |
| --- | --- | --- |

Each bit in the mask represents a Boolean indicator is set to true if a service provider does NOT support the functionality defined below.  This bit mask is used to support backward compatibility.

| Subscriber Name and Address Acceptance Indicator – True if the SOA supports Subscriber Name and Address over the interface. |
| --- |
| Subscriber Name and Address Acceptance Indicator | B | ( |

A Boolean that indicates whether the Service Provider supports the Subscriber Name and Address data during the Subscription Version Create.

The default value is False.

IIS Modifications

The table in Appendix A “Errors” of the IIS, exhibit 18, would have the following added.

| invalidArgument ValueaccessDenied | Subscription Version Management | Customer informationSubscriptionNameAndAddress attribute has been specified by the new service provider when the old service provider does not support customer subscriber name and address information. |
| --- | --- | --- |
| AccessDenied | Subscription Version Management | The new service provider attempts to modify the subscription name and address after the old service provider has concurred to the subscription version port. |

GDMO Modifications

-- -- 8.0 LNP Log Record for the Subscription Version Old SP Concurrence Request

--     Notification

lnpLogOldSP-ConcurrenceRequestRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 :

1992":eventLogRecord;

CHARACTERIZED BY

lnpLogOldSP-ConcurrenceRequestPkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationPkg subscriptionNameAndAddressPkg PRESENT IF

!the new service provider has provided customer informationsubscriber name and address!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 8};

lnpLogOldSP-ConcurrenceRequestPkg PACKAGE

BEHAVIOUR

lnpLogOldSP-ConcurrenceRequestDefinition,

lnpLogOldSP-ConcurrenceRequestBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

subscriptionNewCurrentSP GET,

subscriptionNewSP-DueDate GET,

subscriptionNewSP-CreationTimeStamp GET,

accessControl GET;

;

lnpLogOldSP-ConcurrenceRequestDefinition BEHAVIOUR

DEFINED AS !

The lnpLogOldSP-ConcurrenceRequestRecord class is the managed

object that is used to create log records for the

subscriptionVersionOldSP-ConcurrenceRequest Notification.

!;

lnpLogOldSP-ConcurrenceRequestBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionOldSP-ConcurrenceRequest Notification.

!;

-- 21.0 LNP NPAC Subscription Version Managed Object Class

subscriptionVersionNPAC MANAGED OBJECT CLASS

DERIVED FROM subscriptionVersion;

CHARACTERIZED BY

subscriptionVersionNPAC-Pkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationsubscriptionNameAndAddressPkg PRESENT IF

!the new service provider has provided customer informationsubscriber name and address and

the subscription version has not yet been activated or is between 48

to 72 business hours after cancellationcancelled!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 21};

subscriptionVersionNPAC-Pkg PACKAGE

BEHAVIOUR

subscriptionVersionNPAC-Definition,

subscriptionVersionNPAC-Behavior;

ATTRIBUTES

subscriptionVersionStatus GET-REPLACE,

subscriptionOldSP GET-REPLACE,

subscriptionNewSP-DueDate GET-REPLACE,

subscriptionNewSP-CreationTimeStamp GET-REPLACE,

subscriptionOldSP-DueDate GET-REPLACE,

subscriptionOldSP-Authorization GET-REPLACE,

subscriptionStatusChangeCauseCode GET-REPLACE,

subscriptionOldSP-AuthorizationTimeStamp GET-REPLACE,

subscriptionBroadcastTimeStamp GET-REPLACE,

subscriptionConflictTimeStamp GET-REPLACE,

subscriptionCustomerDisconnectDate GET-REPLACE,

subscriptionEffectiveReleaseDate GET-REPLACE,

subscriptionDisconnectCompleteTimeStamp GET-REPLACE,

subscriptionCancellationTimeStamp GET-REPLACE,

subscriptionCreationTimeStamp GET-REPLACE,

subscriptionFailed-SP-List GET-REPLACE,

subscriptionModifiedTimeStamp GET-REPLACE,

subscriptionOldTimeStamp GET-REPLACE,

subscriptionOldSP-CancellationTimeStamp GET-REPLACE,

subscriptionNewSP-CancellationTimeStamp GET-REPLACE,

subscriptionOldSP-ConflictResolutionTimeStamp GET-REPLACE,

subscriptionNewSP-ConflictResolutionTimeStamp GET-REPLACE,

subscriptionPortingToOriginal-SPSwitch GET-REPLACE,

subscriptionPreCancellationStatus GET-REPLACE;

NOTIFICATIONS

subscriptionVersionOldSP-ConcurrenceRequest,

subscriptionVersionNewSP-CreateRequest,

subscriptionVersionOldSPFinalConcurrenceWindowExpiration,

subscriptionVersionNewNPA-NXX,

subscriptionVersionCancellationAcknowledgeRequest,

subscriptionVersionDonorSP-CustomerDisconnectDate,

subscriptionVersionStatusAttributeValueChange,

"CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 :

1992":attributeValueChange

accessControlParameter,

"CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 : 1992":objectCreation

accessControlParameter;

;

subscriptionVersionNPAC-Definition BEHAVIOUR

DEFINED AS !

The subscriptionVersionNPAC class is the managed object

that represents a subscription version on the NPAC SMS.

!;

…

-- 26.0 LNP Log Record for the Subscription Version Final Concurrence

-- Timer Expiration

lnpLogOldSPFinalConcurrenceWindowExpirationRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 : 1992":eventLogRecord;

CHARACTERIZED BY

lnpLogOldSPFinalConcurrenceWindowExpirationPkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationsubscriptionNameAndAddressPkg PRESENT IF

!the new service provider has provided customer informationsubscriber name and address!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 26};

lnpLogOldSPFinalConcurrenceWindowExpirationPkg PACKAGE

BEHAVIOUR

lnpLogOldSPFinalConcurrenceWindowExpirationDefinition,

lnpLogOldSPFinalConcurrenceWindowExpirationBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

accessControl GET;

;

lnpLogOldSPFinalConcurrenceWindowExpirationDefinition BEHAVIOUR

DEFINED AS !

The lnpLogOldSPFinalConcurrenceWindowExpirationRecord class is

the managed object that is used to create log records for the

subscriptionVersionOldSPFinalConcurrenceWindowExpiration

Notification.

!;

lnpLogOldSPFinalConcurrenceWindowExpirationBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionOldSPFinalConcurrenceWindowExpiration

Notification.

!;

-- ??.0 LNP Subscription Customer InformationSubscriber name and address Package

subscriptionCustomerInformationsubscriptionNameAndAddressPkg PACKAGE

BEHAVIOUR subscriptionCustomerInformationsubscriptionNameAndAddressPkgBehavior;

ATTRIBUTES

subscriptionCustomerInformationsubscriptionNameAndAddress GET-REPLACE;

REGISTERED AS {LNP-OIDS.lnp-package ??};

subscriptionCustomerInformationsubscriptionNameAndAddressPkgBehavior BEHAVIOUR

DEFINED AS !

This package provides for conditionally including the

subscriptionCustomerInformationsubscriptionNameAndAddress attribute.

!;

-- ??.0 LNP Subscription Version Customer InformationSubscriber name and address

subscriptionCustomerInformationsubscriptionNameAndAddress ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.AddressInformation;

MATCHES FOR EQUALITY;

BEHAVIOUR subscriptionCustomerInformationsubscriptionNameAndAddressBehavior;

REGISTERED AS {LNP-OIDS.lnp-attribute ??};

subscriptionCustomerInformationsubscriptionNameAndAddressBehavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the customer addsubscriber name and address information

for inter-service provider communication.

!;

7.0 LNP Subscription Version Modify Action

…

subscriptionVersionModifyBehavior BEHAVIOUR

DEFINED AS !

Preconditions: This action is issued from an lnpSubscriptions

object specifying the object to be modified by either

the subscriptionVersionId, the subscriptionTN or a range of TNs and

optionally the status of the subscription version.  All attribute

values to be modified shall also be specified.

Postconditions: The service provider has modified the subscription

version.  An error will be returned to the service provider if

there is no version that is modifiable or if the modification fails

due to authorization of the service provider or data validation.

Service Providers can modify attributes associated with active,

pending or conflict subscription versions.

Old service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionOldSP-DueDate

subscriptionOldSP-Authorization

subscriptionStatusChangeCauseCode

The subscriptionStatusChangeCauseCode is an optional field and is

only specified if the subscriptionOldSP-Authorization is false.

New service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionLRN

subscriptionNewSP-DueDate

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

subscriptionCustomerInformationsubscriptionNameAndAddress

Validation will be done for both old and new service provider

data that is specified for pending, cancel-pending, or conflict

subscription versions.

If validation fails no changes will be made and an error

will be returned. If validation passes, the version will be

modified and remain in a pending or active state.

New service providers can only modify the following attributes

for active subscription versions:

subscriptionLRN

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

If the data specified passes validation, the modified version

is immediately activated.  The modified subscription version will have

a status of sending and broadcasts will begin.  If validation fails,

no changes will be made and an error will be returned in the action

reply.

The subscriptionCustomerInformationsubscriptionNameAndAddress field would only be modifiable in

requests that are initiated by the new service providers prior to

old service provider concurrence or

to the subscription version activation

or cancellation.

!;

-- 10.0 LNP Subscription Version Old SP Concurrence Request Notification

subscriptionVersionOldSP-ConcurrenceRequest NOTIFICATION

BEHAVIOUR  subscriptionVersionOldSP-ConcurrenceRequestBehavior;

WITH INFORMATION SYNTAX LNP-ASN1.VersionOldSP-ConcurrenceRequest

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

service-prov-id subscriptionNewCurrentSP,

service-prov-due-date subscriptionNewSP-DueDate,

service-prov-authorization-creation-time-stamp

subscriptionNewSP-CreationTimeStamp,

access-control accessControl,

subscription-customer-informationsubscriber-name-address subscriptionCustomerInformationsubscriptionNameAndAddress;

REGISTERED AS {LNP-OIDS.lnp-notification 10};

subscriptionVersionOldSP-ConcurrenceRequestBehavior BEHAVIOUR

DEFINED AS !

This notification requests that a old service provider send

a create request for a subscription version for which

concurrence for porting the number has not been received.

The TN, the version id, and the new service provider id,

authorization flag and creation timestamp values are sent. If

the old service provider supports Inter Service Provider

communication processing, customer subscriber name and address information will

be sent.

!;

-- 12.0 LNP Subscription Version Final Concurrence Timer Expiration

--      Notification

subscriptionVersionOldSPFinalConcurrenceWindowExpiration NOTIFICATION

BEHAVIOUR

subscriptionVersionOldSPFinalConcurrenceWindowExpirationBehavior;

WITH INFORMATION SYNTAX

LNP-ASN1.VersionOldSPFinalConcurrenceWindowExpiration

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

access-control accessControl,

subscription-customer-informationsubscriber-name-address subscriptionCustomerInformationsubscriptionNameAndAddress;

REGISTERED AS {LNP-OIDS.lnp-notification 12};

subscriptionVersionOldSPFinalConcurrenceWindowExpirationBehavior BEHAVIOUR

DEFINED AS !

This notification will be sent by the NPAC SMS upon expiration of

the Final Concurrence Timer to the old service provider via the SOA

to NPAC SMS interface to inform them of the timer expiration. If

the old service provider supports Inter Service Provider communication

processing, customer subscriber name and address information will be sent.

!;

-- ??.0 LNP Subscription Version Subscriber Name and Address Cancel Action

subscriptionVersionInterServiceProviderCancel subscriptionVersionSubscriberNameAndAddressCancel ACTION

BEHAVIOUR

subscriptionVersionInterServiceProviderSubscriberNameAndAddressCancelDefinition,

subscriptionVersionInterServiceProviderSubscriberNameAndAddressCancelBehavior;

MODE CONFIRMED;

WITH INFORMATION SYNTAX LNP-ASN1.InterSPSubscriberNameAndAddress-CancelAction;

WITH REPLY SYNTAX LNP-ASN1.CancelReply;

REGISTERED AS {LNP-OIDS.lnp-action 4};

subscriptionVersionInterServiceProviderSubscriberNameAndAddressCancelDefinition BEHAVIOUR

DEFINED AS !

The subscriptionVersionInterServiceProviderSubscriberNameAndAddressCancel action is

the action that can be used by the old service provider SOA

to cancel a subscription version via the SOA to NPAC SMS

interface for subscriber name and address mismatch.

!;

subscriptionVersionInterServiceProviderSubscriberNameAndAddressCancelBehavior BEHAVIOUR

DEFINED AS !

Preconditions: This action is issued from an lnpSubscriptions

object specifying the object or objects to be canceled by either

the subscriptionVersionId, the subscriptionTN or a range of TNs

and the cause code for cancellation.  Note: Only cause codes

specified as valid for this action can be used.  Valid

values are as follows:

Name Mismatch     - 1000

Address Mismatch  - 1001

Name and Address Mismatch - 1002

Name Mismatch    - 80

Address Mismatch - 81

The subscription version(s) must be in a pending state, customersubscriber

information name and address must have been specified by the new service

provider, and the old service provider must not have concurred.

This action can only be sent by the old service provider.

Postconditions: The NPAC SMS has set the version status

to cancel in the subscription version and the cause code is

set to as specified by the new old service provider.  An error

will be returned to the service provider if there

is no version that can be canceled or if the cancellation

fails due to authorization of the service provider.

!;

ASN.1 Modifications

ModifyAction::= SEQUENCE {

subscription-version-action [0] EXPLICIT SubscriptionVersionAction,

version-status [1] VersionStatus OPTIONAL,

data-to-modify [2] SubscriptionModifyData,

subscription-customer-informationsubscriber-name-address AddressInformation OPTIONAL

}

VersionCreateConcurrenceRequest ::= SEQUENCE {

tn PhoneNumber,

version-id LnpKey,

service-prov-id ServiceProvId,

service-prov-due-date GeneralizedTime,

service-prov-authorization-creation-time-stamp GeneralizedTime,

access-control LnpAccessControl,

subscription-customer-informationsubscriber-name-address AddressInformation OPTIONAL

}

VersionOldSPFinalConcurrenceWindowExpiration ::= SEQUENCE {

tn PhoneNumber,

version-id LnpKey,

access-control LnpAccessControl,

subscription-customer-informationsubscriber-name-address AddressInformation OPTIONAL

}

InterSP-SubscriberNameAndAddressCancelAction ::= SEQUENCE {

Subscription-version-TN CHOICE {

subscription-version-action-key [0] EXPLICIT

SubscriptionVersionActionKey,

subscription-version-tn-range [1] TN-Range,

}

subscription-version-cause-code [2] SubscriptionStatusChangeCauseCode

}