Wireless Change Order Requirements – 054/1824/98

The following wireless change orders are documented in detail below:

NANC 201 – Unique Sets of Timers

NANC 202 – Unique Sets of Business Days/Hours

NANC 203 – Wireless Addition of WSMSC DPC and SSN Information

NANC 204 - Inter Service Provider Communication Process

| Downtime Required | Yes | No |
| --- | --- | --- |
| Recommendation Explanation |

| Installation | Staged | Flash Cut |
| --- | --- | --- |
| Recommendation Explanation |

Business Justification

The T&O LNPA Wire line Wireless Integration Task Force will provide the business justification for the wireless change orders.

Merged Change Order Tracking

Note: This table contains change orders that have been clarifications to previously documented wireless change orders and have been merged in this document as indicated.  Merged change orders will not be referenced separately as wireless requirements.

| Requirement Retained | Requirement Merged and Removed |
| --- | --- |

Change Order Number: NANC 201

IMPACT/CHANGE ASSESSMENT

| FRS | IIS | ASN.1 | GDMO | NPAC | SOA | LSMS |
| --- | --- | --- | --- | --- | --- | --- |
| Y | Y |
| Y | Y | Y |

Unique Sets of Timers

Wireless to wireless porting needs tunable values/timers defined that are independent from wire line tunable values/timers by region.  It was discussed that to support the wireless need in a generic manner that a unique set of tunable timers be defined.

Two approaches were discussed:

The NANC T&O Group selected SOLUTION 2.

Solution 1 - Maximum Flexibility for Unique Timer Set Support

In this option the service provider would specify the timers to be used on each subscription version port request.

Cons:

Nothing to prevent a Service Provider from using shortened timers inappropriately.  If short timers are used inappropriately the port could occur before the other Service Provider has an opportunity to stop it.  This could result in customer service issues for call completion/service.

A proposed solution is to force Service Provider concurrence.

Pro:

Maximum Flexibility for selecting timers to be used on a subscription version port.

Solution 2 – Service Provider ID Associated with Timer Type

A service provider profile would specify the set of timers the NPAC SMS would use for subscription version porting (in and out) for this service provider.

Con:

This approach limits service provider flexibility. One Service Provider can only use one set of timers for porting in and porting out.

Pro:

This approach prevents use of inappropriate timers without changes to the business process flows or the NPAC SMS interface.

The NANC T&O group selected solution 2.

Timers to be in the unique timer set would include:

| Tunable Timer | Long Timer Default | Short Timer Default | Value Range |
| --- | --- | --- | --- |
| Create Subscription Version Initial Concurrence Window (T1 Timer) | 9 business hours | 1 business hour | 1-72 business hours |
| Create Subscription Version Final Concurrence Window (T2 Timer) | 9 business hours | 1 business hour | 1-72 business hours |
| Conflict Restriction Window | 12:00 noon on the business day of the due date | N/A | 00:00 – 24:00 |
| Conflict Resolution New Service Provider Restriction | 6 business hours | 6 business hours | 1-72 business hours |
| Cancellation Initial Concurrence Window | 9 business hours | 9 business hours | 1-72 business hours |
| Cancellation Final Concurrence Window | 9 business hours | 9 business hours | 1-72 business hours |

NOTE:  Support of two additional timer types, medium 1 and medium 2 was discussed to potentially support wire line to wireless and wireless to wire line porting.  The requirements developed do not include these two timer types due to the fact that the values or these timer sets are not yet defined.  The requirements developed do not preclude inclusion of the additional timer types.

Service providers can specify in their profile as defined below the timers to be used for porting in when they are the new service provider or porting out were they are the old service provider.  Due to this fact the NPAC will have to use the longer timer of the timers supported by the service provider. (Another option discussed was to reject the message if the timers supported did not match.)  This selection of the longer timers by the NPAC SMS may result in longer timers being used when a service provider expects short timers to be used.

The following table illustrates the outcome of timers to be used based on the combinations possible.

|  | OLD Service Provider |
| --- | --- |
| New Service Provider | Timer Type | Port Out- Short | Port Out- Long |
|  | Port In – Short |

When both the old and new service providers support short timers for a subscription version port short timers will be used.

No action is necessary by either the old or new service provider operations personnel.

When the new service provider supports short timers and the old service providers supports long timers for a subscription version port long timers will be used.

| The new service provider who supports the short timers will have to recognize that the long timers are being used instead of the expected short timers. |
| --- |
|  | Port In – Long |

When the new service provider supports long timers and the old service providers supports short timers for a subscription version port long timers will be used.

The old service provider who supports the short timers will have to recognize that the long timers are being used instead of the expected short timers.

When both the old and new service providers support long timers for a subscription version port long timers will be used.

No action is necessary by either the old or new service provider operations personnel.

FRS Modifications

The following requirements would need to be updated to add the timer type:

R4-29	Service Provider subscription query options

R4-29	Service Provider subscription query options

NPAC SMS shall receive the attributes to be searched on for queries regarding Subscription Versions associated with the Service Provider. Allowable attributes are the following data elements from Table 3-5  Subscription Version Data Model:

Subscription Version ID

Subscription Version Status

Local Number Portability Type

Ported Telephone Number

Old facilities-based Service Provider Due Date

New facilities-based Service Provider Due Date

New facilities-based Service Provider ID

Authorization from old facilities-based Service Provider

Local Routing Number (LRN)

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

Billing Service Provider ID

End User Location Value

End User Location Type

Customer Disconnect Date

Effective Release Date

Disconnect Broadcast Complete Time Stamp

Conflict Time Stamp

Activation Time Stamp

Cancellation Time Stamp (Status Modified to Cancel Time Stamp)

New Service Provider Creation Time Stamp

Old Service Provider Authorization Time Stamp

Pre-cancellation Status

Old Service Provider Cancellation Time Stamp

New Service Provider Cancellation Time Stamp

Old Time Stamp (Status Modified to Old Time Stamp)

New Service Provider Conflict Resolution Time Stamp

Create Time Stamp

Modify Time Stamp

Porting To Original

Status Change Cause Code

Timer Type

R5-74.3	Query Subscription Version - Output Data

R5-74.3	Query Subscription Version - Output Data

NPAC SMS shall return the following output data for a Subscription Version query request initiated by NPAC personnel or a SOA to NPAC SMS interface user:

Subscription Version ID

Subscription Version Status

Local Number Portability Type

Ported Telephone Number

Old facilities-based Service Provider Due Date

New facilities-based Service Provider Due Date

New facilities-based Service Provider ID

Old facilities-based Service Provider ID

Authorization from old facilities-based Service Provider

Status Change Cause Code

Location Routing Number (LRN)

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

Billing Service Provider ID

End-User Location Value

End User Location Type

Customer Disconnect Date

Effective Release Date

Disconnect Broadcast Complete Time Stamp

Conflict Time Stamp

Activation Time Stamp

Cancellation Time Stamp (Status Modified to Canceled Time Stamp)

New Service Provider Creation Time Stamp

Old Service Provider Authorization Time Stamp

Pre-cancellation Status

Old Service Provider Cancellation Time Stamp

New Service Provider Cancellation Time Stamp

Old Time Stamp (Status Modified to Old Time Stamp)

New Service Provider Conflict Resolution Time Stamp

Create Time Stamp

Modified Time Stamp

Porting to Original

List of all Local SMSs that failed activation, modification, or disconnect.

Timer Type (for SOAs that support Timer Type)

R5-74.4	Query Subscription Version - Output Data

R5-74.4	Query Subscription Version - Output Data

NPAC SMS shall return the following output data for a Subscription Version query request initiated over the NPAC SMS to Local SMS interface:

Subscription Version ID

Ported Telephone Number

Location Routing Number (LRN)

New facilities-based Service Provider ID

Activation Time Stamp

Customer Disconnect Date

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

End-User Location Value

End-User Location Type

Billing Service Provider ID

Local Number Portability Type

Timer Type (for Local SMS’s that support Timer Type)

The following additional requirement would have to be added to support the timer type validation at subscription version creation:

R5-19.3	Create Subscription Version – Timer Type Validation

NPAC SMS shall validate that the old and new Service Provider in the create message support the same timer type.

Note: This requirement causes the create request to be rejected if the timer types supported do not match.

The following requirements support selection of the longer timers:

R5-19.3	Create Subscription Version – Timer Type Selection

NPAC SMS shall if the old and new service provider timer types match set the subscription version timer type to that timer type.

R5-19.4	Create Subscription Version – Timer Type Selection - Mismatch

NPAC SMS shall if the old and new service provider timer types do not match set the subscription version timer type to the longer timer type of the port out type for the old service provider and the port in type of the new service provider.

Appendix C would need to be updated to show each type of tunables (the defaults and ranges).  The existing tunables would be modified to indicate they are the long timers and new rows would be added for the short tunables.  Values would be as specified in the table above.

Requirements would need to be developed for the new tunables.

R5-21.1	Initial Concurrence Window - Tunable Parameter

NPAC SMS shall provide a long and short Initial Concurrence Window tunable parameters which is defined as the number of business hours subsequent to the time the Subscription Version was initially created by which both Service Providers can authorize transfer of service if this is an Inter-Service Provider port.

R5-21.2	Initial Concurrence Window - Tunable Parameter Modification

NPAC SMS shall allow the NPAC SMS Administrator to modify the long and short Initial Concurrence Window date tunable parameters.

R5-21.3	Long Initial Concurrence Window - Tunable Parameter Default

NPAC SMS shall default the long Initial Concurrence Window date tunable parameter to 9 business hours.

R5-21.4	Short Initial Concurrence Window - Tunable Parameter Default

NPAC SMS shall default the short Initial Concurrence Window date tunable parameter to 1 business hours.

R5-23.1	Final Concurrence Window - Tunable Parameter

NPAC SMS shall provide a long and short Final Concurrence Window tunable parameters which is defined as the number of business hsours after the concurrence request is sent by the NPAC SMS by which time both Service Providers can authorize transfer of subscription service for an Inter-Service Provider port.

R5-23.2	Final Concurrence Window Tunable - Tunable Parameter Modification

NPAC SMS shall allow the NPAC SMS Administrator to modify the short and long Final Concurrence Window tunable parameters.

R5-23.3	Long Final Concurrence Window Tunable - Tunable Parameter Default

NPAC SMS shall default the long Final Concurrence Window tunable parameter to 9 business hours.

R5-23.4	Short Final Concurrence Window Tunable - Tunable Parameter Default

NPAC SMS shall default the short Final Concurrence Window tunable parameter to 1 business hours.

RR5-42.5	Conflict Subscription Version – Short Timer Usage

NPAC SMS shall not apply the Conflict Restriction Window Tunable to subscription versions being ported using short timers.

RR5-32.1	Cancellation-Initial Concurrence Window - Tunable Parameter

NPAC SMS shall provide a short and long Cancellation-Initial Concurrence Window tunable parameters, which is defined as the number of business hours after the version is set to Cancel Pending by which the non-originating  Service Provider is expected to acknowledge the pending cancellation.

RR5-32.2	Cancellation-Initial Concurrence Window - Tunable Parameter Modification

NPAC SMS shall allow the NPAC SMS Administrator to modify the short and long Cancellation-Initial Concurrence Window tunable parameters.

RR5-32.3	Long Cancellation-Initial Concurrence Window - Tunable Parameter Default

NPAC SMS shall default the long Cancellation-Initial Concurrence Window tunable parameter to 9 business hours.

RR5-32.4	Short Cancellation-Initial Concurrence Window - Tunable Parameter Default

NPAC SMS shall default the short Cancellation-Initial Concurrence Window tunable parameter to 9 business hours.

RR5-33.1	Cancellation-Final Concurrence Window - Tunable Parameter

NPAC SMS shall provide a short and long Cancellation-Final Concurrence Window tunable parameters which is defined as the number of business hours after the second cancel pending notification is sent by which both Service Providers are expected to acknowledge the pending cancellation.

RR5-33.2	Cancellation-Final Concurrence Window Tunable Parameter Modification

NPAC SMS shall allow the NPAC SMS Administrator to modify the short and long Cancellation-Final Concurrence Window tunable parameters.

RR5-33.3	Long Cancellation-Final Concurrence Window - Tunable Parameter Default

NPAC SMS shall default the long Cancellation-Final Concurrence Window tunable parameter to 9 business hours.

RR5-33.4	Short Cancellation-Final Concurrence Window - Tunable Parameter Default

NPAC SMS shall default the short Cancellation-Final Concurrence Window tunable parameter to 9 business hours.

RR5-12.3	Conflict Resolution New Service Provider Restriction Tunable Parameter

NPAC SMS shall provide a long and short Conflict Resolution New Service Provider Restriction tunable parameters which is defined as a number of business hours after the subscription version is put into conflict that the NPAC SMS  will prevent it from being removed from conflict by the New Service Provider.

RR5-12.4	Long Conflict  Resolution New Service Provider Restriction - Tunable Parameter Default

NPAC SMS shall default the long Conflict Resolution New Service Provider Restriction tunable parameter to 6 business hours.

RR5-12.5	Short Conflict  Resolution New Service Provider Restriction - Tunable Parameter Default

NPAC SMS shall default the short Conflict Resolution New Service Provider Restriction tunable parameter to 6 business hours.

RR5-12.5	Conflict Resolution New Service Provider Restriction Tunable Parameter Modification

NPAC SMS shall allow the NPAC SMS Administration to modify the long and short Conflict Resolution New Service Provider Restriction tunable parameters.

The service provider profile would be updated as follows:

Table 3-2 would be modified to add:

| NPAC New Functionality Support | M | ( |
| --- | --- | --- |

Each bit in the mask represents a Boolean indicator is set to true if a service provider does NOT support the functionality defined below.  This bit mask is used to support backward compatibility.

| Timer Type – True if the SOA and LSMS support query support of timer type over the interface. |
| --- |
| Port In Timer Type | E | X |

Timer type supported by the Service Provider for porting were they are the New Service Provider:

S – Short Timers

| L – Long Timers |
| --- |
| Port Out Timer Type | E | X |

Timer type supported by the Service Provider for porting were they are the Old Service Provider:

S – Short Timers

L – Long Timers

Requirement 4-15 would be modified to add the bold italicized text.

R4-15.2	Modify restrictions on Service Provider data - NPAC Operations Personnel

NPAC SMS shall allow NPAC Operations personnel to modify the data in Table 3-2, with the exception of the NPAC Customer ID, NPAC New Functionality Support and Timer Type.

GDMO/ASN.1 Modifications

A GET only Timer Type attribute would need to be added to the subscriptionVersion managed object class. A note would be added that it is only returned on SOA queries to service providers that support that information.  The behavior would also be updated to note that the attribute would only be emitted on object creation notifications to service providers that support it.

Add object creation notification!!

The attribute will be added to the T1 and T2 notifications for the SOA’s that support the Timer Type attribute.

-- 7.0 LNP Log Record for the Subscription Version New SP Create Request

--     Notification

lnpLogNewSP-CreateRequestRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 :

1992":eventLogRecord;

CHARACTERIZED BY

lnpLogNewSP-CreateRequestPkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationPkg PRESENT IF

!the service provider has customer address and contact

information!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 7};

lnpLogNewSP-CreateRequestPkg PACKAGE

BEHAVIOUR

lnpLogNewSP-CreateRequestDefinition,

lnpLogNewSP-CreateRequestBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

subscriptionOldSP GET,

subscriptionOldSP-DueDate GET,

subscriptionOldSP-Authorization GET,

subscriptionOldSP-AuthorizationTimeStamp GET,

subscriptionStatusChangeCauseCode GET,

accessControl GET,

subscriptionCustomerInformation GET-REPLACE;

;

lnpLogNewSP-CreateRequestDefinition BEHAVIOUR

DEFINED AS !

The lnpLogNewSP-CreateRequestRecord class is the managed

object that is used to create log records for the

subscriptionVersionNewSP-CreateRequest Notification.

!;

lnpLogNewSP-CreateRequestBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionNewSP-CreateRequest Notification.

!;

-- 8.0 LNP Log Record for the Subscription Version Old SP Concurrence Request

--     Notification

lnpLogOldSP-ConcurrenceRequestRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 :

1992":eventLogRecord;

CHARACTERIZED BY

lnpLogOldSP-ConcurrenceRequestPkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationPkg subscriptionTimerTypePkg PRESENT IF

!the present if the Old SP SOA supports timer typeservice provider has customer address and contact

information!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 8};

lnpLogOldSP-ConcurrenceRequestPkg PACKAGE

BEHAVIOUR

lnpLogOldSP-ConcurrenceRequestDefinition,

lnpLogOldSP-ConcurrenceRequestBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

subscriptionNewCurrentSP GET,

subscriptionNewSP-DueDate GET,

subscriptionNewSP-CreationTimeStamp GET,

accessControl GET

subscriptionCustomerInformation subscriptionTimerType GET-REPLACE;

;

lnpLogOldSP-ConcurrenceRequestDefinition BEHAVIOUR

DEFINED AS !

The lnpLogOldSP-ConcurrenceRequestRecord class is the managed

object that is used to create log records for the

subscriptionVersionOldSP-ConcurrenceRequest Notification.

!;

lnpLogOldSP-ConcurrenceRequestBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionOldSP-ConcurrenceRequest Notification.

!;

-- 26.0 LNP Log Record for the Subscription Version Final Concurrence

-- Timer Expiration

lnpLogOldSPFinalConcurrenceWindowExpirationRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 : 1992":eventLogRecord;

CHARACTERIZED BY

lnpLogOldSPFinalConcurrenceWindowExpirationPkg;

CONDITIONAL PACKAGES

subscriptionTimerTypePkg PRESENT IF

!present if the Old SP SOA supports timer type!;    subscriptionCustomerInformationPkg PRESENT IF

!the service provider has customer address and contact

information!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 26};

lnpLogOldSPFinalConcurrenceWindowExpirationPkg PACKAGE

BEHAVIOUR

lnpLogOldSPFinalConcurrenceWindowExpirationDefinition,

lnpLogOldSPFinalConcurrenceWindowExpirationBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

accessControl GET,

subscriptionCustomerInformation subscriptionTimerType GET-REPLACE;

;

lnpLogOldSPFinalConcurrenceWindowExpirationDefinition BEHAVIOUR

DEFINED AS !

The lnpLogOldSPFinalConcurrenceWindowExpirationRecord class is

the managed object that is used to create log records for the

subscriptionVersionOldSPFinalConcurrenceWindowExpiration

Notification.

!;

lnpLogOldSPFinalConcurrenceWindowExpirationBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionOldSPFinalConcurrenceWindowExpiration

Notification.

!;

-- 106.0 LNP Subscription Customer Information

subscriptionCustomerInformation ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.AddressInformation;

MATCHES FOR EQUALITY, ORDERING;

BEHAVIOUR subscriptionCustomerInformationBehavior;

REGISTERED AS {LNP-OIDS.lnp-attribute 106};

subscriptionCustomerInformationBehavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the new service provider

originated subscription customer address and contact information.

!;

-- 27??.0 LNP Subscription Customer InformationTimer Type Package

subscriptionCustomerInformationPkg subscriptionTimerTypePkg PACKAGE

BEHAVIOUR subscriptionTimerTypeCustomerInformationPkgBehavior;

ATTRIBUTES

subscriptionTimerTypeCustomerInformation GETT-REPLACE;

REGISTERED AS {LNP-OIDS.lnp-package 27??};

subscriptionCustomerInformationPkgBehavior BEHAVIOUR

DEFINED AS !

This package provides for conditionally including the

subscriptionCustomerInformation subscriptionTimerType attribute.

!;

6.0 LNP Subscription Version Local SMS Create Action

…

subscriptionVersionLocalSMS-CreateBehavior BEHAVIOUR

DEFINED AS !

Preconditions: This action is issued from an lnpSubscriptions

object specifying the object(s) to be created by

the subscriptionVersionId and the subscriptionTN.  All attribute

values required for creation will be supplied.

Postconditions: A successful reply indicates the Local SMS can

decipher the subscription version create action. An error will be

returned to the NPAC SMS if the Local SMS cannot recognize the

action data.

The Local SMS will attempt to create all the specified subscription

versions. It will return the subscriptionVersionActionResults

notification to the NPAC SMS informing it of the success or

failure of the creation attempts.

If the SP supports customer address information for Inter Service

Provider communication processing, it may be specified in the create.

!;

7.0 LNP Subscription Version Modify Action

…

subscriptionVersionModifyBehavior BEHAVIOUR

DEFINED AS !

Preconditions: This action is issued from an lnpSubscriptions

object specifying the object to be modified by either

the subscriptionVersionId, the subscriptionTN or a range of TNs and

optionally the status of the subscription version.  All attribute

values to be modified shall also be specified.

Postconditions: The service provider has modified the subscription

version.  An error will be returned to the service provider if

there is no version that is modifiable or if the modification fails

due to authorization of the service provider or data validation.

Service Providers can modify attributes associated with active,

pending or conflict subscription versions.

Old service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionOldSP-DueDate

subscriptionOldSP-Authorization

subscriptionStatusChangeCauseCode

The subscriptionStatusChangeCauseCode is an optional field and is

only specified if the subscriptionOldSP-Authorization is false.

New service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionLRN

subscriptionNewSP-DueDate

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

subscriptionCustomerInformation

Validation will be done for both old and new service provider

data that is specified for pending, cancel-pending, or conflict

subscription versions.

If validation fails no changes will be made and an error

will be returned. If validation passes, the version will be

modified and remain in a pending or active state.

New service providers can only modify the following attributes

for active subscription versions:

subscriptionLRN

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

If the data specified passes validation, the modified version

is immediately activated.  The modified subscription version will have

a status of sending and broadcasts will begin.  If validation fails,

no changes will be made and an error will be returned in the action

reply.

The subscriptionCustomerInformation field would only be returned in

queries that are initiated by the old and new service providers prior

to the subscription version activation.

!;

-- 9.0 LNP Subscription Version New SP Create Request Notification

subscriptionVersionNewSP-CreateRequest NOTIFICATION

BEHAVIOUR  subscriptionVersionNewSP-CreateRequestBehavior;

WITH INFORMATION SYNTAX LNP-ASN1.VersionNewSP-CreateRequest

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

service-prov-id subscriptionOldSP,

service-prov-due-date subscriptionOldSP-DueDate,

service-prov-old-authorization subscriptionOldSP-Authorization,

service-prov-authorization-creation-time-stamp

subscriptionOldSP-AuthorizationTimeStamp,

status-change-cause-code subscriptionStatusChangeCauseCode,

access-control accessControl,

subscription-customer-information subscriptionCustomerInformation;

REGISTERED AS {LNP-OIDS.lnp-notification 9};

subscriptionVersionNewSP-CreateRequestBehavior BEHAVIOUR

DEFINED AS !

This notification requests that a new service provider send

a create request for a subscription version for which

concurrence for porting the number has not been received.

The TN, the version id and the old service provider id,

authorization flag and authorization timestamp values are sent. If

the new service provider supports Inter Service Provider

communication processing, customer address information will

also need to be sent.

!;

-- 10.0 LNP Subscription Version Old SP Concurrence Request Notification

subscriptionVersionOldSP-ConcurrenceRequest NOTIFICATION

BEHAVIOUR  subscriptionVersionOldSP-ConcurrenceRequestBehavior;

WITH INFORMATION SYNTAX LNP-ASN1.VersionOldSP-ConcurrenceRequest

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

service-prov-id subscriptionNewCurrentSP,

service-prov-due-date subscriptionNewSP-DueDate,

service-prov-authorization-creation-time-stamp

subscriptionNewSP-CreationTimeStamp,

access-control accessControl,

subscription-customer-informationtimer-type subscriptionCustomerInformationsubscriptionTimerType;

REGISTERED AS {LNP-OIDS.lnp-notification 10};

subscriptionVersionOldSP-ConcurrenceRequestBehavior BEHAVIOUR

DEFINED AS !

This notification requests that a old service provider send

a create request for a subscription version for which

concurrence for porting the number has not been received.

The TN, the version id, and the new service provider id,

authorization flag and creation timestamp values are sent. If

the new old service provider supports  Inter Service Provider

communication processing, customer addresstimer type, it will be sent. information will

also need to be sent.

!;

-- 12.0 LNP Subscription Version Final Concurrence Timer Expiration

--      Notification

subscriptionVersionOldSPFinalConcurrenceWindowExpiration NOTIFICATION

BEHAVIOUR

subscriptionVersionOldSPFinalConcurrenceWindowExpirationBehavior;

WITH INFORMATION SYNTAX

LNP-ASN1.VersionOldSPFinalConcurrenceWindowExpiration

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

access-control accessControl,

subscription-customertimer-information type subscriptionCustomerInformationsubscriptionTimerType;

REGISTERED AS {LNP-OIDS.lnp-notification 12};

subscriptionVersionOldSPFinalConcurrenceWindowExpirationBehavior BEHAVIOUR

DEFINED AS !

This notification will be sent by the NPAC SMS upon expiration of

the Final Concurrence Timer to the old service provider via the SOA

to NPAC SMS interface to inform them of the timer expiration. If

the new old service provider supports Inter Service Provider communication

processing, customer address information will need to be sent.timer type, it will be sent.

!;

ModifyAction::= SEQUENCE {

subscription-version-action [0] EXPLICIT SubscriptionVersionAction,

version-status [1] VersionStatus OPTIONAL,

data-to-modify [2] SubscriptionModifyData,

subscription-customer-information AddressInformation OPTIONAL

}

VersionCreateConcurrenceRequest ::= SEQUENCE {

tn PhoneNumber,

version-id LnpKey,

service-prov-id ServiceProvId,

service-prov-due-date GeneralizedTime,

service-prov-authorization-creation-time-stamp GeneralizedTime,

access-control LnpAccessControl,

subscription-subscription-customer-informationtimer-type AddressInformation Integer OPTIONAL

}

VersionNewSP-CreateRequest ::= SEQUENCE {

version-create-request [0] VersionCreateConcurrenceRequest,

service-prov-old-authorization [1] ServiceProvAuthorization,

subscription-status-change-cause-code [2] SubscriptionStatusChangeCauseCode,

subscription-customer-information [3] AddressInformation OPTIONAL

}

VersionOldSPFinalConcurrenceWindowExpiration ::= SEQUENCE {

tn PhoneNumber,

version-id LnpKey,

access-control LnpAccessControl,

subscription-subscription-customer-information AddressInformationtimer-type Integer OPTIONAL

}

The following attribute needs to be added to the GDMO:

Subscription Version Timer Type

subscriptionTimerType ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.Integer;

MATCHES FOR EQUALITY, ORDERING;

BEHAVIOUR subscriptionTimerTypeBehavior;

REGISTERED AS {LNP-OIDS.lnp-attribute ??};

subscriptionTimerTypeBehavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the subscription version

timer type being used to set tunable timers.

Current valid values are:

0 for long timers (used primarily for wireline to wireline)

1 for short timers (anticipated use for wireless to wireless)

Long timers (0) is set if any of the two service providers

supports only long timers.

!;

The NPAC will have to put M&P or functionality in the install processes to set the port in and out timers supported for service providers defined in the NPAC SMS database.

Change Order Number: NANC 202

IMPACT/CHANGE ASSESSMENT

| FRS | IIS | ASN.1 | GDMO | NPAC | SOA | LSMS |
| --- | --- | --- | --- | --- | --- | --- |
| Y | Y |
| Y | Y | Y |

Unique Sets of Business Days/Hours

Business hours/days for timers is need to be defined uniquelysupport for wireless to wireless porting. Saturday must be added and time must also be increased.  Default business hours will be 8:00 to 8:00 CT.  The tunable would be configurable by region. NPAC defined Holiday are OK as defined for wireless to wireless.

| Tunable | Long Short Timer Default | Short Long Timer Default | Value Range |
| --- | --- | --- | --- |
| Business Day Duration | 12 calendar hours | 12 calendar hours | 1 – 24 |
| Business Day Start Time | Determined per Region | 8:00 CT | 00:00 – 24:00 |
| Holidays | As specified today | As specified today | As specified today |
| Business Days | M-F | M-Saturday | M-Sunday |

Two approaches were discussed:

The NANC T&O Group selected SOLUTION 2.

Solution 1 - Maximum Flexibility for Unique Business Days/Hours Support

In this option the service provider would specify the business days/hours to be used on each subscription version port request.

Cons:

Nothing to prevent a Service Provider from using shortened longer business days/hours inappropriately.  If long timers are used inappropriately the port could occur before the other Service Provider has an opportunity to stop it.  This could result in customer service issues for call completion/service.

A proposed solution is to force Service Provider concurrence.

Pro:

Maximum Flexibility for selecting business days/hours to be used on a subscription version port.

Solution 2 – Service Provider ID Associated with Business Days/Hours Type

A service provider profile would specify the business days/hours the NPAC SMS would use for subscription version porting for this service provider.

Con:

This approach limits service provider flexibility. One Service Provider can only use one set of business days/hours.

Pro:

This approach prevents use of inappropriate business days/hours without changes to the business process flows or the NPAC SMS interface.

The NANC T&O group selected solution 2.

FRS Modifications

1. The following requirements would need to be updated to add the business hours/days type:

R4-29	Service Provider subscription query options

R4-29	Service Provider subscription query options

NPAC SMS shall receive the attributes to be searched on for queries regarding Subscription Versions associated with the Service Provider. Allowable attributes are the following data elements from Table 3-5  Subscription Version Data Model:

Subscription Version ID

Subscription Version Status

Local Number Portability Type

Ported Telephone Number

Old facilities-based Service Provider Due Date

New facilities-based Service Provider Due Date

New facilities-based Service Provider ID

Authorization from old facilities-based Service Provider

Local Routing Number (LRN)

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

Billing Service Provider ID

End User Location Value

End User Location Type

Customer Disconnect Date

Effective Release Date

Disconnect Broadcast Complete Time Stamp

Conflict Time Stamp

Activation Time Stamp

Cancellation Time Stamp (Status Modified to Cancel Time Stamp)

New Service Provider Creation Time Stamp

Old Service Provider Authorization Time Stamp

Pre-cancellation Status

Old Service Provider Cancellation Time Stamp

New Service Provider Cancellation Time Stamp

Old Time Stamp (Status Modified to Old Time Stamp)

New Service Provider Conflict Resolution Time Stamp

Create Time Stamp

Modify Time Stamp

Porting To Original

Status Change Cause Code

Business Hour Types

R5-74.3	Query Subscription Version - Output Data

R5-74.3	Query Subscription Version - Output Data

NPAC SMS shall return the following output data for a Subscription Version query request initiated by NPAC personnel or a SOA to NPAC SMS interface user:

Subscription Version ID

Subscription Version Status

Local Number Portability Type

Ported Telephone Number

Old facilities-based Service Provider Due Date

New facilities-based Service Provider Due Date

New facilities-based Service Provider ID

Old facilities-based Service Provider ID

Authorization from old facilities-based Service Provider

Status Change Cause Code

Location Routing Number (LRN)

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

Billing Service Provider ID

End-User Location Value

End User Location Type

Customer Disconnect Date

Effective Release Date

Disconnect Broadcast Complete Time Stamp

Conflict Time Stamp

Activation Time Stamp

Cancellation Time Stamp (Status Modified to Canceled Time Stamp)

New Service Provider Creation Time Stamp

Old Service Provider Authorization Time Stamp

Pre-cancellation Status

Old Service Provider Cancellation Time Stamp

New Service Provider Cancellation Time Stamp

Old Time Stamp (Status Modified to Old Time Stamp)

New Service Provider Conflict Resolution Time Stamp

Create Time Stamp

Modified Time Stamp

Porting to Original

List of all Local SMSs that failed activation, modification, or disconnect.

Business Hour Types  (for SOAs that support Business Hours)

R5-74.4	Query Subscription Version - Output Data

R5-74.4	Query Subscription Version - Output Data

NPAC SMS shall return the following output data for a Subscription Version query request initiated over the NPAC SMS to Local SMS interface:

Subscription Version ID

Ported Telephone Number

Location Routing Number (LRN)

New facilities-based Service Provider ID

Activation Time Stamp

Customer Disconnect Date

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

End-User Location Value

End-User Location Type

Billing Service Provider ID

Local Number Portability Type

Business Hours (for Local SMS’s that support Business Hours)

2.

The following additional requirement would have to be added to support the business hours/days type validation at subscription version create.

R5-19.3	Create Subscription Version – Business Hours and Days Validation

NPAC SMS shall validate that the old and new Service Provider in the create message support the same type of business hours and days.

Note: This requirement causes the create request to be rejected if the timer types supported do not match.

The following requirements support selection of the shorter business hours/days timers:

R5-19.3	Create Subscription Version – Business Hours and Days Selection

NPAC SMS shall if the old and new service provider business hours and days match set the subscription version business type to the business type for the business hours and days supported.

R5-19.4	Create Subscription Version – Business Hours and Days Selection - Mismatch

NPAC SMS shall if the old and new service provider business hours and days do not match set the subscription version timer type to the shorter business hours and days.

Appendix C would need to be updated to show each long and short business hour/days (the defaults and ranges).  The Business Day Duration and Business Day Start Time that exist would be modified to reflect that they are the longshort business hours/days.  New rows would be added to the table for the shortlong business hours/days with values and defaults as indicated in the table above.

Requirements would need to be added/modified for the new business hours/days types:

RR3-10	Business Hours and Days

NPAC SMS shall support definition and processing of long and short business hours and days for operations involving business time calculation.

RR3-11.1	Business Day Definition -LongShort

NPAC SMS longshort business days shall be Monday through Friday excluding NPAC operations-defined holidays.

RR3-11.2	Business Day Definition -ShortLong

NPAC SMS shortlong business days shall be Monday through Saturday excluding NPAC operations-defined holidays.

RR3-12.1	Business Day Duration - Tunable Parameter

NPAC SMS shall provide a short and long Business Day Duration tunable parameter, which is defined as the number of hours from the tunable business day start time.

RR3-12.2	Business Day Duration - Tunable Parameter Modification

NPAC SMS shall allow the NPAC SMS Administrator to modify the short and long Business Day Duration tunable parameter.

RR3-12.3	LongShort Business Day Duration - Tunable Parameter Default

NPAC SMS shall default the longshort Business Day Duration tunable parameter to 12 hours.

RR3-12.4	ShortLong Business Day Duration - Tunable Parameter Default

NPAC SMS shall default the shortlong Business Day Duration tunable parameter to 12 hours.

RR3-13.1	Business Day Start Time - Tunable Parameter

NPAC SMS shall provide a short and long Business Day Start Time tunable parameter, which is defined as the start of the business day in Central Standard Time.

RR3-13.2	Business Day Start Time - Tunable Parameter Modification

NPAC SMS shall default the short and long Business Day Start Time tunable parameter to the value specified by the contracting region.

RR3-13.3	LongShort Business Day Start Time - Tunable Parameter Default

NPAC SMS shall default the longshort Business Day Start Time tunable parameter to 7:00 AM, Central Standard Time

.

RR3-13.4	ShortLong Business Day Start Time - Tunable Parameter Default

NPAC SMS shall default the shortlong Business Day Start Time tunable parameter to 87:00 AM, Central Standard Time.

The service provider profile would be updated as follows:

Table 3-2 would be modified to add:

| NPAC New Functionality Support | M | ( |
| --- | --- | --- |

Each bit in the mask represents a Boolean indicator is set to true if a service provider does NOT support the functionality defined below.  This bit mask is used to support backward compatibility.

| Business Hours – True if the SOA and LSMS support query ofsupports business days/hours over the interface. |
| --- |
| Business Hour/Days | E | X |

Business Hours supported by the Service Provider:

S – Short Business Hours

L – Long Business Hours

Requirement 4-15 would be modified to add the bold italicized text.

R4-15.2	Modify restrictions on Service Provider data - NPAC Operations Personnel

NPAC SMS shall allow NPAC Operations personnel to modify the data in Table 3-2, with the exception of the NPAC Customer ID, NPAC New Functionality Support and Business Hours/Days

GDMO/ASN.1 Modifications

A GET only atribute would need to be added to the subscriptionVersion managed object class.

Object creation notification

1. A GET only business type attribute would need to be added to the subscriptionVersion managed object class.  A note needs to be added that it will be returned on queries only for SOA’s that support the business hours/days.  The behavior would be updated to note that the attribute would only be emitted on object creation notifications for SOAs that support it.

The business type attribute will be added to the T1 and T2 notifications for the SOA’s that support the Business Type attribute.

-- 7.0 LNP Log Record for the Subscription Version New SP Create Request

--     Notification

lnpLogNewSP-CreateRequestRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 :

1992":eventLogRecord;

CHARACTERIZED BY

lnpLogNewSP-CreateRequestPkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationPkg PRESENT IF

!the service provider has customer address and contact

information!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 7};

lnpLogNewSP-CreateRequestPkg PACKAGE

BEHAVIOUR

lnpLogNewSP-CreateRequestDefinition,

lnpLogNewSP-CreateRequestBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

subscriptionOldSP GET,

subscriptionOldSP-DueDate GET,

subscriptionOldSP-Authorization GET,

subscriptionOldSP-AuthorizationTimeStamp GET,

subscriptionStatusChangeCauseCode GET,

accessControl GET,

subscriptionCustomerInformation GET-REPLACE;

;

lnpLogNewSP-CreateRequestDefinition BEHAVIOUR

DEFINED AS !

The lnpLogNewSP-CreateRequestRecord class is the managed

object that is used to create log records for the

subscriptionVersionNewSP-CreateRequest Notification.

!;

lnpLogNewSP-CreateRequestBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionNewSP-CreateRequest Notification.

!;

-- 8.0 LNP Log Record for the Subscription Version Old SP Concurrence Request

--     Notification

lnpLogOldSP-ConcurrenceRequestRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 :

1992":eventLogRecord;

CHARACTERIZED BY

lnpLogOldSP-ConcurrenceRequestPkg;

CONDITIONAL PACKAGES

subscriptionCustomerInformationPkg subscriptionBusinessTypePkg PRESENT IF

!the present if the Old SP SOA supports business typeservice provider has customer address and contact

information!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 8};

lnpLogOldSP-ConcurrenceRequestPkg PACKAGE

BEHAVIOUR

lnpLogOldSP-ConcurrenceRequestDefinition,

lnpLogOldSP-ConcurrenceRequestBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

subscriptionNewCurrentSP GET,

subscriptionNewSP-DueDate GET,

subscriptionNewSP-CreationTimeStamp GET,

accessControl GET

subscriptionCustomerInformation subscriptionBusinessType GET-REPLACE;

;

lnpLogOldSP-ConcurrenceRequestDefinition BEHAVIOUR

DEFINED AS !

The lnpLogOldSP-ConcurrenceRequestRecord class is the managed

object that is used to create log records for the

subscriptionVersionOldSP-ConcurrenceRequest Notification.

!;

lnpLogOldSP-ConcurrenceRequestBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionOldSP-ConcurrenceRequest Notification.

!;

-- 26.0 LNP Log Record for the Subscription Version Final Concurrence

-- Timer Expiration

lnpLogOldSPFinalConcurrenceWindowExpirationRecord MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 : 1992":eventLogRecord;

CHARACTERIZED BY

lnpLogOldSPFinalConcurrenceWindowExpirationPkg;

CONDITIONAL PACKAGES

subscriptionBusinessTypePkg PRESENT IF

!present if the Old SP SOA supports business type!;    subscriptionCustomerInformationPkg PRESENT IF

!the service provider has customer address and contact

information!;

REGISTERED AS {LNP-OIDS.lnp-objectClass 26};

lnpLogOldSPFinalConcurrenceWindowExpirationPkg PACKAGE

BEHAVIOUR

lnpLogOldSPFinalConcurrenceWindowExpirationDefinition,

lnpLogOldSPFinalConcurrenceWindowExpirationBehavior;

ATTRIBUTES

subscriptionTN GET,

subscriptionVersionId GET,

accessControl GET,

subscriptionCustomerInformation subscriptionBusinessType GET-REPLACE;

;

lnpLogOldSPFinalConcurrenceWindowExpirationDefinition BEHAVIOUR

DEFINED AS !

The lnpLogOldSPFinalConcurrenceWindowExpirationRecord class is

the managed object that is used to create log records for the

subscriptionVersionOldSPFinalConcurrenceWindowExpiration

Notification.

!;

lnpLogOldSPFinalConcurrenceWindowExpirationBehavior BEHAVIOUR

DEFINED AS !

This log record can be used by any CME wanting to log the

subscriptionVersionOldSPFinalConcurrenceWindowExpiration

Notification.

!;

-- 106.0 LNP Subscription Customer Information

subscriptionCustomerInformation ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.AddressInformation;

MATCHES FOR EQUALITY, ORDERING;

BEHAVIOUR subscriptionCustomerInformationBehavior;

REGISTERED AS {LNP-OIDS.lnp-attribute 106};

subscriptionCustomerInformationBehavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the new service provider

originated subscription customer address and contact information.

!;

-- 27??.0 LNP Subscription Customer InformationBusiness Type Package

subscriptionCustomerInformationPkg subscriptionBusinessTypePkg PACKAGE

BEHAVIOUR subscriptionBusinessTypeCustomerInformationPkgBehavior;

ATTRIBUTES

subscriptionBusinessTypeCustomerInformation GETT-REPLACE;

REGISTERED AS {LNP-OIDS.lnp-package 27??};

subscriptionCustomerInformationPkgBehavior BEHAVIOUR

DEFINED AS !

This package provides for conditionally including the

subscriptionCustomerInformation subscriptionBusinessType attribute.

!;

6.0 LNP Subscription Version Local SMS Create Action

…

subscriptionVersionLocalSMS-CreateBehavior BEHAVIOUR

DEFINED AS !

Preconditions: This action is issued from an lnpSubscriptions

object specifying the object(s) to be created by

the subscriptionVersionId and the subscriptionTN.  All attribute

values required for creation will be supplied.

Postconditions: A successful reply indicates the Local SMS can

decipher the subscription version create action. An error will be

returned to the NPAC SMS if the Local SMS cannot recognize the

action data.

The Local SMS will attempt to create all the specified subscription

versions. It will return the subscriptionVersionActionResults

notification to the NPAC SMS informing it of the success or

failure of the creation attempts.

If the SP supports customer address information for Inter Service

Provider communication processing, it may be specified in the create.

!;

7.0 LNP Subscription Version Modify Action

…

subscriptionVersionModifyBehavior BEHAVIOUR

DEFINED AS !

Preconditions: This action is issued from an lnpSubscriptions

object specifying the object to be modified by either

the subscriptionVersionId, the subscriptionTN or a range of TNs and

optionally the status of the subscription version.  All attribute

values to be modified shall also be specified.

Postconditions: The service provider has modified the subscription

version.  An error will be returned to the service provider if

there is no version that is modifiable or if the modification fails

due to authorization of the service provider or data validation.

Service Providers can modify attributes associated with active,

pending or conflict subscription versions.

Old service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionOldSP-DueDate

subscriptionOldSP-Authorization

subscriptionStatusChangeCauseCode

The subscriptionStatusChangeCauseCode is an optional field and is

only specified if the subscriptionOldSP-Authorization is false.

New service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionLRN

subscriptionNewSP-DueDate

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

subscriptionCustomerInformation

Validation will be done for both old and new service provider

data that is specified for pending, cancel-pending, or conflict

subscription versions.

If validation fails no changes will be made and an error

will be returned. If validation passes, the version will be

modified and remain in a pending or active state.

New service providers can only modify the following attributes

for active subscription versions:

subscriptionLRN

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

If the data specified passes validation, the modified version

is immediately activated.  The modified subscription version will have

a status of sending and broadcasts will begin.  If validation fails,

no changes will be made and an error will be returned in the action

reply.

The subscriptionCustomerInformation field would only be returned in

queries that are initiated by the old and new service providers prior

to the subscription version activation.

!;

-- 9.0 LNP Subscription Version New SP Create Request Notification

subscriptionVersionNewSP-CreateRequest NOTIFICATION

BEHAVIOUR  subscriptionVersionNewSP-CreateRequestBehavior;

WITH INFORMATION SYNTAX LNP-ASN1.VersionNewSP-CreateRequest

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

service-prov-id subscriptionOldSP,

service-prov-due-date subscriptionOldSP-DueDate,

service-prov-old-authorization subscriptionOldSP-Authorization,

service-prov-authorization-creation-time-stamp

subscriptionOldSP-AuthorizationTimeStamp,

status-change-cause-code subscriptionStatusChangeCauseCode,

access-control accessControl,

subscription-customer-information subscriptionCustomerInformation;

REGISTERED AS {LNP-OIDS.lnp-notification 9};

subscriptionVersionNewSP-CreateRequestBehavior BEHAVIOUR

DEFINED AS !

This notification requests that a new service provider send

a create request for a subscription version for which

concurrence for porting the number has not been received.

The TN, the version id and the old service provider id,

authorization flag and authorization timestamp values are sent. If

the new service provider supports Inter Service Provider

communication processing, customer address information will

also need to be sent.

!;

-- 10.0 LNP Subscription Version Old SP Concurrence Request Notification

subscriptionVersionOldSP-ConcurrenceRequest NOTIFICATION

BEHAVIOUR  subscriptionVersionOldSP-ConcurrenceRequestBehavior;

WITH INFORMATION SYNTAX LNP-ASN1.VersionOldSP-ConcurrenceRequest

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

service-prov-id subscriptionNewCurrentSP,

service-prov-due-date subscriptionNewSP-DueDate,

service-prov-authorization-creation-time-stamp

subscriptionNewSP-CreationTimeStamp,

access-control accessControl,

subscription-customer-informationbusiness-type subscriptionCustomerInformationsubscriptionBusinessType;

REGISTERED AS {LNP-OIDS.lnp-notification 10};

subscriptionVersionOldSP-ConcurrenceRequestBehavior BEHAVIOUR

DEFINED AS !

This notification requests that a old service provider send

a create request for a subscription version for which

concurrence for porting the number has not been received.

The TN, the version id, and the new service provider id,

authorization flag and creation timestamp values are sent. If

the new old service provider supports  Inter Service Provider

communication processing, customer addressbusiness type, it will be sent. information will

also need to be sent.

!;

-- 12.0 LNP Subscription Version Final Concurrence Timer Expiration

--      Notification

subscriptionVersionOldSPFinalConcurrenceWindowExpiration NOTIFICATION

BEHAVIOUR

subscriptionVersionOldSPFinalConcurrenceWindowExpirationBehavior;

WITH INFORMATION SYNTAX

LNP-ASN1.VersionOldSPFinalConcurrenceWindowExpiration

AND ATTRIBUTE IDS

tn subscriptionTN,

version-id subscriptionVersionId,

access-control accessControl,

subscription-customerbusiness-information type subscriptionCustomerInformationsubscriptionBusinessType;

REGISTERED AS {LNP-OIDS.lnp-notification 12};

subscriptionVersionOldSPFinalConcurrenceWindowExpirationBehavior BEHAVIOUR

DEFINED AS !

This notification will be sent by the NPAC SMS upon expiration of

the Final Concurrence Timer to the old service provider via the SOA

to NPAC SMS interface to inform them of the timer expiration. If

the new old service provider supports Inter Service Provider communication

processing, customer address information will need to be sent.business type, it will be sent.

!;

ASN.1 Modifications

ModifyAction::= SEQUENCE {

subscription-version-action [0] EXPLICIT SubscriptionVersionAction,

version-status [1] VersionStatus OPTIONAL,

data-to-modify [2] SubscriptionModifyData,

subscription-customer-information AddressInformation OPTIONAL

}

VersionCreateConcurrenceRequest ::= SEQUENCE {

tn PhoneNumber,

version-id LnpKey,

service-prov-id ServiceProvId,

service-prov-due-date GeneralizedTime,

service-prov-authorization-creation-time-stamp GeneralizedTime,

access-control LnpAccessControl,

subscription-subscription-customer-informationbusiness-type AddressInformation Integer OPTIONAL

}

VersionNewSP-CreateRequest ::= SEQUENCE {

version-create-request [0] VersionCreateConcurrenceRequest,

service-prov-old-authorization [1] ServiceProvAuthorization,

subscription-status-change-cause-code [2] SubscriptionStatusChangeCauseCode,

subscription-customer-information [3] AddressInformation OPTIONAL

}

VersionOldSPFinalConcurrenceWindowExpiration ::= SEQUENCE {

tn PhoneNumber,

version-id LnpKey,

access-control LnpAccessControl,

subscription-subscription-customer-information AddressInformationbusiness-type Integer OPTIONAL

}

The following attribute needs to be added to the GDMO:

Subscription Version Business Type

subscriptionBusinessType ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.Integer;

MATCHES FOR EQUALITY, ORDERING;

BEHAVIOUR subscriptionTimerTypeBehavior;

REGISTERED AS {LNP-OIDS.lnp-attribute ??};

subscriptionBusinessTypeBehavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the subscription version

business hours/days type being used to set tunable timers.

Current valid values are:

0 for shortlong business hours/days

(used primarily for wireline to wireline)

1 for longshort business hours/days

(anticipated use for wireless to wireless)

Long Short business hours (0)is set if any of the two

service providers supports only long short business hours.

!;

The NPAC will have to put M&P or functionality in the install processes to set the business hours/days supported for service providers defined in the NPAC SMS database.

Change Order Number: NANC 203

IMPACT/CHANGE ASSESSMENT

| FRS | IIS | ASN.1 | GDMO | NPAC | SOA | LSMS |
| --- | --- | --- | --- | --- | --- | --- |
| Y | Y | Y | Y | Y | Y | Y |

Wireless Addition of WSMSC DPC and SSN Information

Wireless Short Message Service Center (WSMSC) needs to be added as a new set of DPC and SSN information that is part of the subscription version received from SOA, stored on the NPAC SMS, and sent to the LSMS for wireless to wireless porting.  Validation rules for DPC and SSN information are assumed to be those in place today.

A bit mask in the NPAC SMS could will be used to indicate which LSMS and SOA systems support the new fields.  SOA systems would only need to recompile if they intend to send the WSMSC DPC and SSN information.  LSMS systems would only need to recompile if they indicated to the NPAC SMS that they would support downloading of the WSMSC DPC and SSN information.

FRS Modifications

The following information is needed in the subscription version data table in section 3.1.3.

| WSMSC DPC | N (9) |
| --- | --- |
| DPC for 10-digit GTT for WSMSC features. |
| WSMSC SSN | N (3) |
| WSMSC SSN for the Subscription Version. |

Requirement R3-8 should be updated to include the WSMSC DPC and SSN information in the download file. It would be noted that this data would only be present if the LSMS supports the WSMSC DPC and SSN data.

R3-8	Off-line batch updates for Local SMS Disaster Recovery

NPAC SMS shall support an off-line batch download (via 4mm DAT tape and FTP file download) to mass update Local SMSs with Subscription Versions and Service Provider Network data.

The contents of the batch download are:

Subscriber data:

Version ID

TN

LRN

New Current Service Provider ID

Activation Request Timestamp

Version Status

CLASS DPC

CLASS SSN

LIDB DPC

LIDB SSN

ISVM DPC

ISVM SSN

CNAM DPC

CNAM SSN

WSMS DPC

WSMSC DPC (for Local SMS’s that support WSMSC data)

WSMSC SSN (for Local SMS’s that support WSMSC data)

End User Location - Value

End User Location - Type

Billing ID

LNP Type

Download Reason

Network data:

NPAC Customer ID

NPAC Customer name

NPA-NXX-Download Data:

NPA-NXX ID

NPA-NXX Value

NPAC Customer ID

Effective TimeStamp

Download Reason

LRN-Download Data:

LRN ID

LRN Value

Download Reason

The download data file format in the appendix would also have to be updated.  The WSMSCCS DPC and SSN fields would be added to the end of the fileline if the Service provider requesting the file supports the data.

The following requirements would also need to be updated to add the WSMSC DPC and SSN information:

R4-29 Service Provider subscription query options

R4-29	Service Provider subscription query options

NPAC SMS shall receive the attributes to be searched on for queries regarding Subscription Versions associated with the Service Provider. Allowable attributes are the following data elements from Table 3-5  Subscription Version Data Model:

Subscription Version ID

Subscription Version Status

Local Number Portability Type

Ported Telephone Number

Old facilities-based Service Provider Due Date

New facilities-based Service Provider Due Date

New facilities-based Service Provider ID

Authorization from old facilities-based Service Provider

Local Routing Number (LRN)

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMS WSMSC DPC (for Local SMS’s that support WSMSC data)

WSMS WSMSC SSN (for Local SMS’s that support WSMSC data)

Billing Service Provider ID

End User Location Value

End User Location Type

Customer Disconnect Date

Effective Release Date

Disconnect Broadcast Complete Time Stamp

Conflict Time Stamp

Activation Time Stamp

Cancellation Time Stamp (Status Modified to Cancel Time Stamp)

New Service Provider Creation Time Stamp

Old Service Provider Authorization Time Stamp

Pre-cancellation Status

Old Service Provider Cancellation Time Stamp

New Service Provider Cancellation Time Stamp

Old Time Stamp (Status Modified to Old Time Stamp)

New Service Provider Conflict Resolution Time Stamp

Create Time Stamp

Modify Time Stamp

Porting To Original

Status Change Cause Code

R5-15.1	Create “Inter-Service Provider Port” Subscription Version - New Service Provider Input Data

R5-15.1	Create “Inter-Service Provider Port” Subscription Version - New Service Provider Input Data

NPAC SMS shall require the following data from NPAC personnel or the new Service Provider upon Subscription Version creation for an Inter-Service Provider port when NOT “porting to original”:

Local Number Portability Type - Port Type.  This field must be set to “LSPP” for Inter-Service Provider ports.

Ported Telephone Number(s) - this entry can be a single TN or a continuous range of TNs that identifies a subscription or a group of Subscription Versions that share the same attributes.

Due Date - date on which transfer of service from old facilities-based Service Provider to new facilities-based Service Provider is initially planned to occur.

New Facilities-based Service Provider ID - the identifier of the new facilities-based Service Provider.

Old Facilities-based Service Provider ID - the identifier of the old facilities-based Service Provider.

Location Routing Number (LRN) - the identifier of the ported-to switch.

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC (if supported by the Service Provider SOA)

WSMSC SSN (if supported by the Service Provider SOA)

Porting to Original - flag indicating whether or not this is a “porting to original” port.  This flag must be set to “FALSE” for this type of Inter-Service Provider port.

(SHOULD THIS BE R5-16 Optional? Optional raises some issues with DPC/SSN information.)

R5-18.1	Create Subscription Version - Field-level Data Validation

R5-18.1	Create Subscription Version - Field-level Data Validation

NPAC SMS shall perform field-level data validations to ensure that the value formats for the following input data, if supplied, is valid according to the formats specified in Table 3-5 upon Subscription Version creation for an Inter-Service Provider port:

LNP Type

Ported TN(s)

Old Service Provider Due Date

New Service Provider Due Date

Old Service Provider ID

New Service Provider ID

Authorization from old facilities-based Service Provider

Status Change Cause Code

LRN

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC

WSMSC SSN

Porting to Original

Billing Service Provider ID

End-User Location – Value

End-User Location - Type

RR5-4	Create “Intra-Service Provider Port” Subscription Version - Current Service Provider Input Data (SHOULD THIS BE RR5-4 Optional? Optional raises some issues with DPC/SSN information.)

RR5-4	Create “Intra-Service Provider Port” Subscription Version - Current Service Provider Input Data

NPAC SMS shall require the following data from the NPAC personnel or the Current (New) Service Provider at the time of Subscription Version Creation for an Intra-Service Provider port:

LNP Type - port type This field must be set to “LISP for Intra-Service Provider support.

Ported Telephone Number(s) - this entry can be a single TN or a continuous range of TNs that identifies a subscription or group of Subscription Versions that share the same attributes.

Due Date - date on which Intra-Service Provider port is planned to occur.

New facilities-based Service Provider ID - current Service Provider within which the Intra-Service Provider port will occur.

Old facilities-based Service Provider ID - current Service Provider within which the Intra-Service Provider port will occur.

Location Routing Number (LRN) - identifier of the ported-to switch

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC (if supported by the Service Provider SOA)

WSMSC SSN (if supported by the Service Provider SOA)

RR5-6.1	Create “Intra-Service Provider Port” Subscription Version - Field-level Data Validation

RR5-6.1	Create “Intra-Service Provider Port” Subscription Version - Field-level Data Validation

NPAC SMS shall perform field-level data validations to ensure that the value formats for the following input data, if supplied, is valid according to the formats specified in Table 3-4 upon Subscription Version creation for an Intra-Service Provider port:

LNP Type

Ported TN(s)

Current Service Provider Due Date

Old Service Provider ID

New Service Provider ID

LRN

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC

WSMSC SSN

Billing Service Provider ID

End-User Location - Value

End-User Location - Type

R5-27.1	Modify Subscription Version - New Service Provider Data Values

R5-27.1	Modify Subscription Version - New Service Provider Data Values

NPAC SMS shall allow the following data to be modified in a pending or conflict Subscription Version for an Inter-Service Provider or Intra-Service Provider port by the new/current Service Provider or NPAC personnel:

Location Routing Number (LRN) - the identifier of the ported to switch.

Due Date - date on which transfer of service from old facilities-based Service Provider to new facilities-based Service Provider is planned to occur.

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC

WSMSC SSN

R5-29.1	Modify Subscription Version - Field-level Data Validation

R5-29.1	Modify Subscription Version - Field-level Data Validation

NPAC SMS shall perform field-level data validations to ensure that the value formats for the following input data, if supplied, is valid according to the formats specified in Table 3-4 upon Subscription Version modification.

LNP Type

Ported TN(s)

Old Service Provider Due Date

New Service Provider Due Date

Old Service Provider Authorization

Status Change Cause Code

Old Service Provider ID

New Service Provider ID

LRN

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC

WSMSC SSN

Billing Service Provider ID

End-User Location - Value

End-User Location - Type

R5-36	Modify Active Subscription Version - Input Data

R5-36	Modify Active Subscription Version - Input Data

NPAC SMS shall allow the following data to be modified for an active Subscription Version:

Location Routing Number (LRN) - the identifier of the ported to switch

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC

WSMSC SSN

R5-38.1	Modify Active Subscription Version - Field-level Data Validation

R5-38.1	Modify Active Subscription Version - Field-level Data Validation

NPAC SMS shall perform field-level data validations to ensure that the value formats for the following input data, if supplied, is valid according to the formats specified in Table 3-4 upon Subscription Version modification of an active version:

LRN

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC

WSMSC SSN

Billing Service Provider ID

End-User Location – Value

End-User Location - Type

R5-74.3	Query Subscription Version - Output Data

R5-74.3	Query Subscription Version - Output Data

NPAC SMS shall return the following output data for a Subscription Version query request initiated by NPAC personnel or a SOA to NPAC SMS interface user:

Subscription Version ID

Subscription Version Status

Local Number Portability Type

Ported Telephone Number

Old facilities-based Service Provider Due Date

New facilities-based Service Provider Due Date

New facilities-based Service Provider ID

Old facilities-based Service Provider ID

Authorization from old facilities-based Service Provider

Status Change Cause Code

Location Routing Number (LRN)

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC (for SOAs that support WSMSC data)

WSMSC SSN (for SOAs that support WSMSC data)

Billing Service Provider ID

End-User Location Value

End User Location Type

Customer Disconnect Date

Effective Release Date

Disconnect Broadcast Complete Time Stamp

Conflict Time Stamp

Activation Time Stamp

Cancellation Time Stamp (Status Modified to Canceled Time Stamp)

New Service Provider Creation Time Stamp

Old Service Provider Authorization Time Stamp

Pre-cancellation Status

Old Service Provider Cancellation Time Stamp

New Service Provider Cancellation Time Stamp

Old Time Stamp (Status Modified to Old Time Stamp)

New Service Provider Conflict Resolution Time Stamp

Create Time Stamp

Modified Time Stamp

Porting to Original

List of all Local SMSs that failed activation, modification, or disconnect.

R5-74.4	Query Subscription Version - Output Data

R5-74.4	Query Subscription Version - Output Data

NPAC SMS shall return the following output data for a Subscription Version query request initiated over the NPAC SMS to Local SMS interface:

Subscription Version ID

Ported Telephone Number

Location Routing Number (LRN)

New facilities-based Service Provider ID

Activation Time Stamp

Customer Disconnect Date

Class DPC

Class SSN

LIDB DPC

LIDB SSN

CNAM DPC

CNAM SSN

ISVM DPC

ISVM SSN

WSMSC DPC (for Local SMS’s that support WSMSC data)

WSMSC SSN (for Local SMS’s that support WSMSC data)

End-User Location Value

End-User Location Type

Billing Service Provider ID

Local Number Portability Type

The service provider profile would be updated as follows:

Table 3-2 would be modified to add:

| NPAC New Functionality Support | M | ( |
| --- | --- | --- |

Each bit in the mask represents a Boolean indicator is set to true if a service provider does NOT support the functionality defined below.  This bit mask is used to support backward compatibility.

LSMS WSMSC DPC SSN Data – True if the LSMS and SOA systems does not support WSMSC DPC and SSN Data in subscription versions.

SOA WSMSC DPC SSN Data – True if the SOA system does not support WSMSC DPC and SSN Data in subscription versions.

Requirement 4-15 would be modified to add the bold italicized text.

R4-15.2	Modify restrictions on Service Provider data - NPAC Operations Personnel

NPAC SMS shall allow NPAC Operations personnel to modify the data in Table 3-2, with the exception of the NPAC Customer ID and NPAC New Functionality Support.

ISSUE:  Should the SOA get the WSMSC information on query?  I think the SOA needs the support flag for this information.

GDMO Modifications

Conditional PackagesWSMSC attributes would need to be added to the subscriptionVersion managed object class.

-- 20.0 LNP subscription Version Managed Object Class

subscriptionVersion MANAGED OBJECT CLASS

DERIVED FROM "CCITT Rec. X.721 (1992) | ISO/IEC 10165-2 : 1992":top;

CHARACTERIZED BY

subscriptionVersionPkg;

CONDITIONAL PACKAGES

WSMSC-DPC-Pkg PRESENT IF

!the WSMCS DPC is present in the new SP Create!,

WSMSC-SSN-Pkg PRESENT IF

!the WSMCS SSN is present in the new SP Create!;

subscriptionWSMSC-DPC GET-REPLACE

subscriptionWSMSC-SSN GET-REPLACE   REGISTERED AS {LNP-OIDS.lnp-objectClass 20};

Behavior in the subscriptionVersion NPAC managed object class behavior should be modified to as follows:

New service provider SOAs can only modify the following

attributes:

subscriptionLRN

subscriptionNewSP-DueDate

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

subscriptionWSMSC-DPC

subscriptionWSMSC-SSN

The following attributes need to be added to the GDMO:

Subscription Version WSMSC Destination Point Code

subscriptionWSMSC-DPC ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.DPC;

MATCHES FOR EQUALITY, ORDERING;

BEHAVIOUR subscriptionWSMSC-DPCBehavior;

REGISTERED AS {LNP-OIDS.lnp-attribute ?};

subscriptionWSMSC-DPCBehavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the subscription version

WSMSC Destination Point Code.

The data is stored in BCD (e.g. a value of FFF would be

displayed as 255.255.255).

!;

LNP Subscription Version WSMSC SSN

subscriptionWSMSC-SSN ATTRIBUTE

WITH ATTRIBUTE SYNTAX LNP-ASN1.SSN;

MATCHES FOR EQUALITY, ORDERING;

BEHAVIOUR subscriptionWSMSC-SSN-Behavior;

REGISTERED AS {LNP-OIDS.lnp-attribute ?};

subscriptionWSMSC-SSN-Behavior BEHAVIOUR

DEFINED AS !

This attribute is used to specify the subscription version

WSMSC SSN.

!;

The following package definitions need to be added:

-- WSMCS DPC Package

WSMCS-DPC-Pkg PACKAGE

BEHAVIOUR WSMCS-DPC-PkgBehavior;

ATTRIBUTES

WSMCS-DPC GET-REPLACE;

REGISTERED AS {LNP-OIDS.lnp-package ?};

WSMCS-DPC-PkgBehavior BEHAVIOUR

DEFINED AS !

This package provides for conditionally including the

WSMCS-DPC attribute.

!;

-- WSMCS SSN Package

WSMCS-SSN-Pkg PACKAGE

BEHAVIOUR WSMCS-SSN-PkgBehavior;

ATTRIBUTES

WSMCS-SSN GET-REPLACE;

REGISTERED AS {LNP-OIDS.lnp-package ?};

WSMCS-SSN-PkgBehavior BEHAVIOUR

DEFINED AS !

This package provides for conditionally including the

WSMCS-SSN attribute.

!;

The following behavior needs to be modified in the subscriptionVersionModify action.

New service providers can only modify the following attributes

for pending, cancel-pending, or conflict subscription versions:

subscriptionLRN

subscriptionNewSP-DueDate

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionEndUserLocationValue

subscriptionEndUserLocationType

subscriptionBillingId

subscriptionWSMCS-DPC

subscriptionWSMCS-SSN

The following behavior needs to be modified in the subscriptionVerionsNewSP-Create Action

The new service provider must specify valid values for the

following attributes:

subscriptionTN or a valid subscriptionVersionTN-Range

subscriptionLRN

subscriptionNewCurrentSP

subscriptionOldSP

subscriptionNewSP-DueDate

subscriptionCLASS-DPC

subscriptionCLASS-SSN

subscriptionLIDB-DPC

subscriptionLIDB-SSN

subscriptionCNAM-DPC

subscriptionCNAM-SSN

subscriptionISVM-DPC

subscriptionISVM-SSN

subscriptionLNPType

subscriptionPortingToOriginal-SPSwitch

subscriptionWSMCS-DPC

subscriptionWSMCS-SSN

ASN.1 Modifications

NewSP-CreateData ::= SEQUENCE {

chc1 [0] EXPLICIT CHOICE {

subscription-version-tn [0] PhoneNumber,

subscription-version-tn-range [1] TN-Range

},

subscription-lrn [1] LRN OPTIONAL,

subscription-new-current-sp [2] ServiceProvId,

subscription-old-sp [3] ServiceProvId,

subscription-new-sp-due-date [4] GeneralizedTime,

subscription-class-dpc [6] EXPLICIT DPC OPTIONAL,

subscription-class-ssn [7] EXPLICIT SSN OPTIONAL,

subscription-lidb-dpc [8] EXPLICIT DPC OPTIONAL,

subscription-lidb-ssn [9] EXPLICIT SSN OPTIONAL,

subscription-isvm-dpc [10] EXPLICIT DPC OPTIONAL,

subscription-isvm-ssn [11] EXPLICIT SSN OPTIONAL,

subscription-cnam-dpc [12] EXPLICIT DPC OPTIONAL,

subscription-cnam-ssn [13] EXPLICIT SSN OPTIONAL,

subscription-end-user-location-value [14]

EndUserLocationValue OPTIONAL,

subscription-end-user-location-type [15] EndUserLocationType OPTIONAL,

subscription-billing-id [16] BillingId OPTIONAL,

subscription-lnp-type [17] LNPType,

subscription-porting-to-original-sp-switch [18]

SubscriptionPortingToOriginal-SPSwitch,

subscription-wsmsc-dpc [19] EXPLICIT DPC OPTIONAL,

subscription-wsmcs-ssn [20] EXPLICIT SSN OPTIONAL

}

NewSP-CreateInvalidData ::= CHOICE {

subscription-version-tn [0] EXPLICIT PhoneNumber,

subscription-version-tn-range [1] EXPLICIT TN-Range,

subscription-lrn [2] EXPLICIT LRN,

subscription-new-current-sp [3] EXPLICIT ServiceProvId,

subscription-old-sp [4] EXPLICIT ServiceProvId,

subscription-new-sp-due-date [5] EXPLICIT GeneralizedTime,

subscription-class-dpc [6] EXPLICIT DPC,

subscription-class-ssn [7] EXPLICIT SSN,

subscription-lidb-dpc [8] EXPLICIT DPC,

subscription-lidb-ssn [9] EXPLICIT SSN,

subscription-isvm-dpc [10] EXPLICIT DPC,

subscription-isvm-ssn [11] EXPLICIT SSN,

subscription-cnam-dpc [12] EXPLICIT DPC,

subscription-cnam-ssn [13] EXPLICIT SSN,

subscription-end-user-location-value [14] EXPLICIT EndUserLocationValue,

subscription-end-user-location-type [15] EXPLICIT EndUserLocationType,

subscription-billing-id [16] EXPLICIT BillingId,

subscription-lnp-type [17] EXPLICIT LNPType,

subscription-porting-to-original-sp-switch [18]

EXPLICIT SubscriptionPortingToOriginal-SPSwitch,

subscription-wsmsc-dpc [19] EXPLICIT DPC,

subscription-wsmcs-ssn [20] EXPLICIT SSN

}

SubscriptionData ::= SEQUENCE {

subscription-lrn [1] LRN OPTIONAL,

subscription-new-current-sp [2] ServiceProvId OPTIONAL,

subscription-activation-timestamp [3] GeneralizedTime OPTIONAL,

subscription-class-dpc [4] EXPLICIT DPC,

subscription-class-ssn [5] EXPLICIT SSN,

subscription-lidb-dpc [6] EXPLICIT DPC,

subscription-lidb-ssn [7] EXPLICIT SSN,

subscription-isvm-dpc [8] EXPLICIT DPC,

subscription-isvm-ssn [9] EXPLICIT SSN,

subscription-cnam-dpc [10] EXPLICIT DPC,

subscription-cnam-ssn [11] EXPLICIT SSN,

subscription-end-user-location-value [12]

EndUserLocationValue OPTIONAL,

subscription-end-user-location-type [13] EndUserLocationType OPTIONAL,

subscription-billing-id [14] BillingId OPTIONAL,

subscription-lnp-type [15] LNPType,

subscription-download-reason [16] DownloadReason,

subscription-wsmsc-dpc [17] EXPLICIT DPC OPTIONAL,

subscription-wsmcs-ssn [18] EXPLICIT SSN OPTIONAL

}

SubscriptionModifyData ::= SEQUENCE {

subscription-lrn [0] LRN OPTIONAL,

subscription-new-sp-due-date [1] GeneralizedTime OPTIONAL,

subscription-old-sp-due-date [2] GeneralizedTime OPTIONAL,

subscription-old-sp-authorization [3] ServiceProvAuthorization OPTIONAL,

subscription-class-dpc [4] EXPLICIT DPC OPTIONAL,

subscription-class-ssn [5] EXPLICIT SSN OPTIONAL,

subscription-lidb-dpc [6] EXPLICIT DPC OPTIONAL,

subscription-lidb-ssn [7] EXPLICIT SSN OPTIONAL,

subscription-isvm-dpc [8] EXPLICIT DPC OPTIONAL,

subscription-isvm-ssn [9] EXPLICIT SSN OPTIONAL,

subscription-cnam-dpc [10] EXPLICIT DPC OPTIONAL,

subscription-cnam-ssn [11] EXPLICIT SSN OPTIONAL,

subscription-end-user-location-value [12] EndUserLocationValue OPTIONAL,

subscription-end-user-location-type [13] EndUserLocationType OPTIONAL,

subscription-billing-id [14] BillingId OPTIONAL,

subscription-status-change-cause-code [15]

SubscriptionStatusChangeCauseCode OPTIONAL,

subscription-wsmsc-dpc [19] EXPLICIT DPC OPTIONAL,

subscription-wsmcs-ssn [20] EXPLICIT SSN OPTIONAL

}

SubscriptionModifyInvalidData ::= CHOICE {

subscription-lrn [0] EXPLICIT LRN,

subscription-new-sp-due-date [1] EXPLICIT GeneralizedTime,

subscription-old-sp-due-date [2] EXPLICIT GeneralizedTime,

subscription-old-sp-authorization [3] EXPLICIT ServiceProvAuthorization,

subscription-class-dpc [4] EXPLICIT DPC,

subscription-class-ssn [5] EXPLICIT SSN,

subscription-lidb-dpc [6] EXPLICIT DPC,

subscription-lidb-ssn [7] EXPLICIT SSN,

subscription-isvm-dpc [8] EXPLICIT DPC,

subscription-isvm-ssn [9] EXPLICIT SSN,

subscription-cnam-dpc [10] EXPLICIT DPC,

subscription-cnam-ssn [11] EXPLICIT SSN,

subscription-end-user-location-value [12] EXPLICIT EndUserLocationValue,

subscription-end-user-location-type [13] EXPLICIT EndUserLocationType,

subscription-billing-id [14] EXPLICIT BillingId,

subscription-status-change-cause-code [15]

EXPLICIT SubscriptionStatusChangeCauseCode,

subscription-wsmsc-dpc [16] EXPLICIT DPC OPTIONAL,

subscription-wsmcs-ssn [17] EXPLICIT SSN OPTIONAL

}

Auditing of new DPC and SSN Values

R8-3	Service Providers Specify Audit Scope

NPAC SMS shall allow Service Providers to specify the scope of an audit by specifying one or more of the following parameters:

Specific Service provider network or ALL Service Providers networks

Full audit for all LNP attributes or a partial audit where the Service Provider can specify one or more of the following LNP attributes:

LIDB data

CLASS data

LRN data

CNAM data

ISVM data

WSMSC data (only Service Provider Local SMS systems that support this attribute will be audited on this attribute)

Default:  Full audit

R8-9	NPAC Personnel Specify Audit Scope

NPAC SMS shall allow NPAC SMS Personnel to specify the scope of an audit by specifying one or more of the following parameters:

Specific Service Provider  network or ALL Service Providers networks.

Full audit for all LNP attributes or a partial audit where the Service Provider can specify one or more of the following LNP attributes:

LIDB data

CLASS data

LRN data

CNAM data

ISVM data

WSMSC data

Default:  Full audit

AuditAttributes ::= CHOICE {

specific-audit [0] SEQUENCE {

lidb-data BOOLEAN,

class-data BOOLEAN,

cnam-data BOOLEAN,

isvm-data BOOLEAN,

lrn-data BOOLEAN,

wsmsc-data BOOLEAN OPTIONAL  -- OPTIONAL for backward

-- compatibility

},

all-data [1] NULL

}

MismatchAttributes ::= SEQUENCE {

seq0 [0] SEQUENCE {

lsms-subscriptionLRN LRN,

npac-subscriptionLRN LRN

} OPTIONAL,

seq1 [1] SEQUENCE {

lsms-subscriptionNewCurrentSP ServiceProvId,

npac-subscriptionNewCurrentSP ServiceProvId

} OPTIONAL,

seq2 [2] SEQUENCE {

lsms-subscriptionActivationTimeStamp GeneralizedTime,

npac-subscriptionActivationTimeStamp GeneralizedTime

} OPTIONAL,

seq3 [3] SEQUENCE {

lsms-subscriptionCLASS-DPC DPC,

npac-subscriptionCLASS-DPC DPC

} OPTIONAL,

seq4 [4] SEQUENCE {

lsms-subscriptionCLASS-SSN SSN,

npac-subscriptionCLASS-SSN SSN

} OPTIONAL,

seq5 [5] SEQUENCE {

lsms-subscriptionLIDB-DPC DPC,

npac-subscriptionLIDB-DPC DPC

} OPTIONAL,

seq6 [6] SEQUENCE {

lsms-subscriptionLIDB-SSN SSN,

npac-subscriptionLIDB-SSN SSN

} OPTIONAL,

seq7 [7] SEQUENCE {

lsms-subscriptionISVM-DPC DPC,

npac-subscriptionISVM-DPC DPC

} OPTIONAL,

seq8 [8] SEQUENCE {

lsms-subscriptionISVM-SSN SSN,

npac-subscriptionISVM-SSN SSN

} OPTIONAL,

seq9 [9] SEQUENCE {

lsms-subscriptionCNAM-DPC DPC,

npac-subscriptionCNAM-DPC DPC

} OPTIONAL,

seq10 [10] SEQUENCE {

lsms-subscriptionCNAM-SSN SSN,

npac-subscriptionCNAM-SSN SSN

} OPTIONAL,

seq11 [11] SEQUENCE {

lsms-subscriptionEndUserLocationValue EndUserLocationValue,

npac-subscriptionEndUserLocationValue EndUserLocationValue

} OPTIONAL,

seq12 [12] SEQUENCE {

lsms-subscriptionEndUserLocationType EndUserLocationType,

npac-subscriptionEndUserLocationType EndUserLocationType

} OPTIONAL,

seq13 [13] SEQUENCE {

lsms-subscriptionBillingId BillingId,

npac-subscriptionBillingId BillingId

} OPTIONAL,

seq14 [14] SEQUENCE {

lsms-subscriptionLNPType LNPType,

npac-subscriptionLNPType LNPType

} OPTIONAL,

seq15 [10] SEQUENCE {

lsms-subscriptionWSMCS-DPC DPC,

npac-subscriptionWSMCS-DPC DPC

} OPTIONAL,

seq16 [10] SEQUENCE {

lsms-subscriptionWSMCS-SSN SSN,

npac-subscriptionWSMCS-SSN SSN

} OPTIONAL

}

Change Order Number: NANC 204

IMPACT/CHANGE ASSESSMENT

| FRS | IIS | ASN.1 | GDMO | NPAC | SOA | LSMS |
| --- | --- | --- | --- | --- | --- | --- |
| TBD | TBD | TBD | TBD | TBD | TBD | TBD |

Inter Service Provider Communication Process

Subscriber Name, Address, City, State, Zip have been requested as information to be exchanged between old and new SP’s when creating a pending port.  This information originates from the new service provider only.  This data would not remain in the NPAC SMS after the port has been activated or cancelled. Data would be needed in the Create Subscription Version Initial Concurrence Window (T1 Timer), Create Subscription Version Final Concurrence Window (T2 Timer), and object creation notifications to service providers that support Inter Service Provider processing. It is believed at this time that the address information definition in the NANC IIS for the NPAC SMS customer contact data is sufficient for wireless use.   The current definition is as follows:

| Field | Size/Type |
| --- | --- |
| Name | 40 character |
| Address Line 1 | 40 character |
| Address Line 2 | 40 character |
| City | 20 character |
| State | 2 character |
| Zip | 9 character |
| Country | 20 character |
| Province | 2 character |

Issue:  A question was raised as to whether social security number and tax ids were also needed in this information.

Backward Compatibility

The following table indicates if a change order is Backward Compatible (BC) and gives further detail if the change order is not backwards compatible or if there is a question about backwards compatibility.

| Change Order Description | BC? | Notes |
| --- | --- | --- |
| NANC 201- Unique Sets of Timers | TBD |
|  | NANC 202- Unique Sets of Business Days/Hours | TBD |
|  | NANC 203- Wireless Addition of WSMSC DPC and SSN Information | TBD | If a SOA does not send this information it will not be impacted. If an LSMS does not indicate to the NPAC SMS that it does not want to receive the information then it will not receive it in subscription version downloads, in the download files or in audit processing. Query is still an issue for the SOA and LSMS. |
| NANC 204 – Inter Service Provider Communication | TBD |