NANC 314 Subscription and Block Download File section in Appendix E have incorrect DPC data examples.

FRS Document Only Change

Below are the details of how the text currently appears in the FRS and how it should by modified.

Download File Examples as they currently exist in the FRS

All fields within files discussed in the following section are variable length.  The download reason in all download files is always set to new.  ASCII 13 is the value used as the value for carriage return (CR) in the download files.

Subscription Download File

The following table describes each field of the sample subscription download file. This download file example contains data for three subscriptions, with three lines for each subscription. Each subscription is one record in the file, pipe delimited, with a carriage return (CR) between each subscription. The breaks in the lines and the parenthesized comments are solely for ease of reading and understanding.

Table E-1 describes the entries for subscription 1: The “Value in Example” column directly correlates to the values for subscription 1 in the download file example, as seen in Figure E-1.

Subscription versions in the download file are selected by an NPA-NXX begin and end range.  The file name for the Subscriptions download file will be in the format:

NPANXX-NPANXX.DD-MM-YYYYHH24MISS

The NPANXX-NPANXX values map to the selection criteria and the time stamp maps to the current time.

The Subscriptions file given in the example would be named:

303123-303125.10-13-1996081122

Figure E- 1 -- Subscription Download File Example

| Explanation of the fields in the subscription download file |
| --- |
| Field Number | Field Name | Value in Example |
| 1 | Version Id | 0000000001 |
| 2 | Version TN | 3031231000 |
| 3 | LRN | 1234567890 |
| 4 | New Current Service Provider Id | 0001 |
| 5 | Activation Timestamp | 19960916152337 (yyyymmddhhmmss) |
| 7 | CLASS DPC | 123456789 |
| 8 | CLASS SSN | 123 |
| 9 | LIDB DPC | 123456789 |
| 10 | LIDB SSN | 123 |
| 11 | ISVM DPC | 123456789 |
| 12 | ISVM SSN | 123 |
| 13 | CNAM DPC | 123456789 |
| 14 | CNAM SSN | 123 |
| 15 | End user Location Value | 123456789012 |
| 16 | End User Location Type | 12 |
| 17 | Billing Id | 0001 |
| 18 | LNP Type | 0 |
| 19 | Download Reason | 0 |
| 20 | WSMSC DPC | Not present if LSMS or SOA does not support the WSMSC DPC as shown in this example. If it were present the value would be in the same format as other DPC data. |
| 21 | WSMSC SSN | Not present if LSMS or SOA does not support the WSMSC SSN as shown in this example. If it were present the value would be in the same format as other DPC data. |

Table E- 1 -- Explanation of the Fields in The Subscription Download File

Block Download File

The following table describes each field of the sample Block download file. This download file example contains data for three Blocks, with three lines for each Block. Each Block is one record in the file, pipe delimited, with a carriage return(CR) between each Block. The breaks in the lines and the parenthesized comments are solely for ease of reading and understanding.

Table E-6 describes the entries for Block 1: The “Value in Example” column directly correlates to the values for Block 1 in the download file example, as seen in Figure E-6.

Blocks in the download file are selected by a combination of NPA-NXX-X begin and end range (with a default value of 000-000-0 through 999-999-9), as well as TIME begin and end range (with a default value of 00-00-000000000000 through 99-99-999999999999).  The TIME Range is keyed off the Activation Broadcast Timestamp, Modify Broadcast Timestamp, and Disconnect Broadcast Timestamp.  The file name for the Block download file will be in the format:

NPANXXX-NPANXXX.DD-MM-YYYYHH24MISS.DD-MM-YYYYHH24MISS.DD-MM-YYYYHH24MISS

The NPANXXX-NPANXXX values map to the NPA-NXX-X selection criteria, the first stamp maps to the current time (when the file is generated), the second time stamp maps to the begin time range, and the third time stamp maps to the end time range.  All three time stamps are represented in Central Time (standard/daylight), even though the Blocks are stored in the NPAC in Greenwich Mean Time.

The Block file given in the example would be named:

3031235-3031252.09-17-1996153344.07-11-1996091222.09-17-1996153344

The files available for LSMS compares will be defined as one or more NPA-NXX-Xs per file.

Figure E- 2 -- Block Download File Example

| Explanation of the fields in the BLOCK download file |
| --- |
| Field Number | Field Name | Value in Example |
| 1 | Block Id | 1 |
| 2 | NPA-NXX-X | 3031231 |
| 3 | LRN | 1234567890 |
| 4 | New Current Service Provider Id | 0001 |
| 5 | Activation Timestamp | 19960916152337 (yyyymmddhhmmss) |
| 6 | CLASS DPC | 123456789 |
| 7 | CLASS SSN | 123 |
| 8 | LIDB DPC | 123456789 |
| 9 | LIDB SSN | 123 |
| 10 | ISVM DPC | 123456789 |
| 11 | ISVM SSN | 123 |
| 12 | CNAM DPC | 123456789 |
| 13 | CNAM SSN | 123 |
| 14 | WSMSC DPC | Not present if LSMS or SOA does not support the WSMSC DPC as shown in this example. If it were present the value would be in the same format as other DPC data. |
| 15 | WSMSC SSN | Not present if LSMS or SOA does not support the WSMSC DPC as shown in this example. If it were present the value would be in the same format as other SSN data. |
| 16 | Download Reason | 0 |

Table E- 2 -- Explanation of the Fields in The Block Download File

Download File Examples with the edits.

Note:  Edits are in larger font and italized.

All fields within files discussed in the following section are variable length.  The download reason in all download files is always set to new.  ASCII 13 is the value used as the value for carriage return (CR) in the download files.

Subscription Download File

The following table describes each field of the sample subscription download file. This download file example contains data for three subscriptions, with three lines for each subscription. Each subscription is one record in the file, pipe delimited, with a carriage return (CR) between each subscription. The breaks in the lines and the parenthesized comments are solely for ease of reading and understanding.

Table E-1 describes the entries for subscription 1: The “Value in Example” column directly correlates to the values for subscription 1 in the download file example, as seen in Figure E-1.

Subscription versions in the download file are selected by an NPA-NXX begin and end range.  The file name for the Subscriptions download file will be in the format:

NPANXX-NPANXX.DD-MM-YYYYHH24MISS

The NPANXX-NPANXX values map to the selection criteria and the time stamp maps to the current time.

The Subscriptions file given in the example would be named:

303123-303125.10-13-1996081122

Figure E- 3 -- Subscription Download File Example

| Explanation of the fields in the subscription download file |
| --- |
| Field Number | Field Name | Value in Example |
| 1 | Version Id | 0000000001 |
| 2 | Version TN | 3031231000 |
| 3 | LRN | 1234567890 |
| 4 | New Current Service Provider Id | 0001 |
| 5 | Activation Timestamp | 19960916152337 (yyyymmddhhmmss) |
| 6 | CLASS DPC | 123123123 |
| 7 | CLASS SSN | 123 |
| 8 | LIDB DPC | 123123123 |
| 9 | LIDB SSN | 123 |
| 10 | ISVM DPC | 123123123 |
| 11 | ISVM SSN | 123 |
| 12 | CNAM DPC | 123123123 |
| 13 | CNAM SSN | 123 |
| 14 | End user Location Value | 123456789012 |
| 15 | End User Location Type | 12 |
| 16 | Billing Id | 0001 |
| 17 | LNP Type | 0 |
| 18 | Download Reason | 0 |
| 19 | WSMSC DPC | Not present if LSMS or SOA does not support the WSMSC DPC as shown in this example. If it were present the value would be in the same format as other DPC data. |
| 20 | WSMSC SSN | Not present if LSMS or SOA does not support the WSMSC SSN as shown in this example. If it were present the value would be in the same format as other DPC data. |

Table E- 3 -- Explanation of the Fields in The Subscription Download File

Block Download File

The following table describes each field of the sample Block download file. This download file example contains data for three Blocks, with three lines for each Block. Each Block is one record in the file, pipe delimited, with a carriage return(CR) between each Block. The breaks in the lines and the parenthesized comments are solely for ease of reading and understanding.

Table E-6 describes the entries for Block 1: The “Value in Example” column directly correlates to the values for Block 1 in the download file example, as seen in Figure E-6.

Blocks in the download file are selected by a combination of NPA-NXX-X begin and end range (with a default value of 000-000-0 through 999-999-9), as well as TIME begin and end range (with a default value of 00-00-000000000000 through 99-99-999999999999).  The TIME Range is keyed off the Activation Broadcast Timestamp, Modify Broadcast Timestamp, and Disconnect Broadcast Timestamp.  The file name for the Block download file will be in the format:

NPANXXX-NPANXXX.DD-MM-YYYYHH24MISS.DD-MM-YYYYHH24MISS.DD-MM-YYYYHH24MISS

The NPANXXX-NPANXXX values map to the NPA-NXX-X selection criteria, the first stamp maps to the current time (when the file is generated), the second time stamp maps to the begin time range, and the third time stamp maps to the end time range.  All three time stamps are represented in UTC.

The Block file given in the example would be named:

3031235-3031252.09-17-1996153344.07-11-1996091222.09-17-1996153344

The files available for LSMS compares will be defined as one or more NPA-NXX-Xs per file.

Figure E- 4 -- Block Download File Example

| Explanation of the fields in the BLOCK download file |
| --- |
| Field Number | Field Name | Value in Example |
| 1 | Block Id | 1 |
| 2 | NPA-NXX-X | 3031231 |
| 3 | LRN | 1234567890 |
| 4 | New Current Service Provider Id | 0001 |
| 5 | Activation Timestamp | 19960916152337 (yyyymmddhhmmss) |
| 6 | CLASS DPC | 123123123 |
| 7 | CLASS SSN | 123 |
| 8 | LIDB DPC | 123123123 |
| 9 | LIDB SSN | 123 |
| 10 | ISVM DPC | 123123123 |
| 11 | ISVM SSN | 123 |
| 12 | CNAM DPC | 123123123 |
| 13 | CNAM SSN | 123 |
| 14 | WSMSC DPC | Not present if LSMS or SOA does not support the WSMSC DPC as shown in this example. If it were present the value would be in the same format as other DPC data. |
| 15 | WSMSC SSN | Not present if LSMS or SOA does not support the WSMSC DPC as shown in this example. If it were present the value would be in the same format as other SSN data. |
| 16 | Download Reason | 0 |

Table E- 4 -- Explanation of the Fields in The Block Download File

# Text boxes

0001|3031231000|1234567890|0001|19960916152337|

123456789|123|123456789|123|123456789|123|123456789|123|

123456789012|12|0001||0|0(CR) 		(end of subscription 1)

0002|3031241000|1234567891|0001|19960825011010||

123456789|123|123456789|123|123456789|123|123456789|123|

123456789013|13|0001|0|0(CR) 		(end of subscription 2)

0003|3031251000|1234567892|19960713104923|

123456789|123|123456789|123|123456789|123|123456789|123|

123456789014|13|0001|0|0(CR) 		(end of subscription 3)

0001|3031231000|1234567890|0001|19960916152337|

123123123|123|123123123|123|123123123|123|123123123|123|

123456789012|12|0001||0|0(CR) 		(end of subscription 1)

0002|3031241000|1234567891|0001|19960825011010||

123123123|123|123123123|123|123123123|123|123123123|123|

123456789013|13|0001|0|0(CR) 		(end of subscription 2)

0003|3031251000|1234567892|19960713104923|

123123123|123|123123123|123|123123123|123|123123123|123|

123456789014|13|0001|0|0(CR) 		(end of subscription 3)

1|3031231|1234567890|0001|19960916152337|

123456789|123|123456789|123|123456789|123|123456789|123|

||0(CR) 		(end of Block 1)

2|3031241|1234567891|0001|19960825011010|

123456789|123|123456789|123|123456789|123|123456789|123|

123456789|123|0(CR) 		(end of Block 2)

3|3031251|1234567892|19960713104923|

123456789|123|123456789|123|123456789|123|123456789|123|

123456789|123|0(CR) 		(end of Block 3)

1|3031231|1234567890|0001|19960916152337|

123123123|123|123123123|123|123123123|123|123123123|123|||0(CR) 		(end of Block 1)

2|3031241|1234567891|0001|19960825011010|

123123123|123|123123123|123|123123123|123|123123123|123|123456789|123|0(CR) 		(end of Block 2)

3|3031251|1234567892|19960713104923|

123123123|123|123123123|123|123123123|123|123123123|123|123456789|123|0(CR) 		(end of Block 3)