DELTA DOCUMENT

NPAC SMS

Interoperability Test Plan

Release 3.2.0

Draft #2

Supporting NANC IIS Version 3.2.0a

November 1, 2002

Table of Contents

1	MOC Test Cases	1-1

1.1	NANC 187	1-1

1.1.1	MOC.SOA.CAP.ACT.LINK.lnpNetwork.lnpDownload	1-1

1.1.2	MOC.SOA.INV.ACT.LINK.lnpNetwork.lnpDownload	1-1

1.1.3	MOC.SOA.VAL.LINK.lnpDownload-NPA-NXX-X	1-2

1.1.4	MOC.SOA.CAP.ACT.LINK.lnpNotificationRecovery	1-2

1.1.5	MOC.SOA.INV.ACT.LINK.lnpNotificationRecovery	1-3

1.1.6	MOC.LSMS.CAP.ACT.LINK.lnpNetwork.lnpDownload	1-4

1.1.7	MOC.LSMS.INV.ACT.LINK.lnpNetwork.lnpDownload	1-4

1.1.8	MOC.LSMS.CAP.ACT.LINK.lnpSubscriptions.lnpDownload	1-5

1.1.9	MOC.LSMS.INV.ACT.LINK.lnpSubscriptions.lnpDownload	1-5

1.1.10	MOC.LSMS.VAL.LINK.lnpDownload-NPA-NXX-X	1-6

1.1.11	MOC.LSMS.VAL.LINK.lnpDownload-NumberPoolBlock	1-6

1.1.12	MOC.LSMS.CAP.ACT.LINK.lnpNotificationRecovery	1-6

1.1.13	MOC.LSMS.INV.ACT.LINK.lnpNotificationRecovery	1-7

1.2	NANC 218	1-7

1.2.1	MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOldSP-Create-Initial	1-7

1.2.2	MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOldSP-Create-Second	1-8

1.2.3	MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionModify	1-8

1.2.4	MOC.SOA.CAP.NOT.RANGE.CONFLICT.subscriptionVersionRangeObjectCreation	1-9

1.2.5	MOC.SOA.CAP.NOT.RANGE.CONFLICT.subscriptionVersionRangeAttributeValueChange	1-9

1.2.6	MOC.SOA.CAP.NOT.LIST.CONFLICT.subscriptionVersionRangeObjectCreation	1-10

1.2.7	MOC.SOA.CAP.NOT.LIST.CONFLICT.subscriptionVersionRangeAttributeValueChange	1-10

1.3	NANC 230	1-11

1.3.1	MOC.SOA.CAP.ACT.PTOLISP.subscriptionVersionNewSP-Create-Initial	1-11

1.3.2	MOC.SOA.INV.ACT.PTOLISP.subscriptionVersionNewSP-Create	1-11

1.3.3	MOC.SOA.CAP.NOT.RANGE.PTOLISP.subscriptionVersionRangeObjectCreation	1-12

1.3.4	MOC.SOA.CAP.NOT.LIST.PTOLISP.subscriptionVersionRangeObjectCreation	1-12

1.3.5	MOC.SOA.INV.NOT.RANGE.PTOLISP.subscriptionVersionRangeObjectCreation	1-13

1.4	NANC 249	1-13

1.4.1	MOC.SOA.CAP.ACT.DISCONPEND.subscriptionVersionModify	1-13

1.4.2	MOC.SOA.INV.ACT.DISCONPEND.subscriptionVersionModify	1-13

1.5	NANC 319	1-14

1.5.1	MOC.SOA.INV.CRE.LATA.serviceProvNPA-NXX	1-14

1.5.2	MOC.SOA.INV.CRE.LATA.serviceProvLRN	1-14

2	A2A Test Cases	2-16

2.1	NANC 187	2-16

2.1.1	A2A.SOA.VAL.MISC.ACTION.LINK.resync	2-16

2.1.2	A2A.SOA.INV.MISC.ACTION.LINK.resync	2-17

2.1.3	A2A.SOA.VAL.MISC.ACTION.LINK.ASSOCSP.resync	2-17

2.1.4	A2A.SOA.VAL.MISC.ACTION.LINK.resync_3_1	2-18

2.1.5	A2A.LSMS.VAL.MISC.ACTION.LINK.resync	2-19

2.1.6	A2A.LSMS.INV.MISC.ACTION.LINK.resync	2-20

2.2	NANC 218	2-20

2.2.1	A2A.SOA.CAP.OP.SET.PEND.CONFLICT.subscriptionVersion	2-20

2.2.2	A2A.NSOA.VAL.CREATE.CONFLICT.SubscriptionVersion	2-21

2.2.3	A2A.OSOA.VAL.CREATE.CONFLICT.SubscriptionVersion	2-21

2.2.4	A2A.NSOA.INV.CANCEL.CONFLICT.SubscriptionVersion	2-21

2.2.5	A2A.OSOA.INV.CANCEL.CONFLICT.SubscriptionVersion	2-21

2.2.6	A2A.OSOA.VAL.MODIFY.PEND.subscriptionVersion	2-21

2.3	NANC 230	2-21

2.3.1	A2A.DSOA.VAL.PORT-TO-ORIG.PTOLISP.SubscriptionVersion	2-21

2.3.2	A2A.SOA.VAL.PORT-TO-ORIG.ASSOCSP.PTOLISP.SubscriptionVersion	2-22

2.4	NANC 249	2-23

2.4.1	A2A.SOA.VAL.MODIFY.DISCONPEND.SubscriptionVersion	2-23

2.4.2	A2A.SOA.INV.MODIFY.DISCONPEND.SubscriptionVersion	2-24

2.4.3	A2A.SOA.VAL.MODIFY.TN-RANGE.DISCONPEND.SubscriptionVersion	2-24

2.4.4	A2A.SOA.INV.MODIFY.TN-RANGE.DISCONPEND.SubscriptionVersion	2-25

2.4.5	A2A.SOA.VAL.MODIFY.ASSOCSP.DISCONPEND.SubscriptionVersion	2-25

2.4.6	A2A.SOA.INV.MODIFY.ASSOCSP.DISCONPEND.SubscriptionVersion	2-26

3	Large, Single PDU Recovery Test Cases	3-27

3.1	SOA Recovery, Object Creation Notification	3-27

3.1.1	A2A.SOA.VAL.MISC.ACTION.resync_500_ocn	3-27

3.1.2	A2A.SOA.VAL.MISC.ACTION.resync_1000_ocn	3-27

3.1.3	A2A.SOA.VAL.MISC.ACTION.resync_2000_ocn	3-28

3.2	SOA Recovery, Status Attribute Value Change Notification	3-28

3.2.1	A2A.SOA.VAL.MISC.ACTION.resync_1failed_500_savc	3-28

3.2.2	A2A.SOA.VAL.MISC.ACTION.resync_1failed_1000_savc	3-29

3.2.3	A2A.SOA.VAL.MISC.ACTION.resync_1failed_2000_savc	3-29

3.2.4	A2A.SOA.VAL.MISC.ACTION.resync_20failed_500_savc	3-30

3.2.5	A2A.SOA.VAL.MISC.ACTION.resync_20failed_1000_savc	3-30

3.2.6	A2A.SOA.VAL.MISC.ACTION.resync_20failed_2000_savc	3-31

3.3	LSMS Recovery, NPA-NXX First Usage Notification	3-31

3.3.1	A2A.LSMS.VAL.MISC.ACTION.resync_500_firstusage	3-31

3.3.2	A2A.LSMS.VAL.MISC.ACTION.resync_1000_firstusage	3-32

3.3.3	A2A.LSMS.VAL.MISC.ACTION.resync_2000_firstusage	3-32

3.4	LSMS Recovery, Subscription Data, M-CREATE	3-32

3.4.1	A2A.LSMS.VAL.MISC.ACTION.resync_500_sv	3-32

3.4.2	A2A.LSMS.VAL.MISC.ACTION.resync_1000_sv	3-33

3.4.3	A2A.LSMS.VAL.MISC.ACTION.resync_2000_sv	3-33

3.4.4	A2A.LSMS.VAL.MISC.ACTION.resync_5000_sv	3-34

3.4.5	A2A.LSMS.VAL.MISC.ACTION.resync_10000_sv	3-34

Appendix B Test Case Nomenclature	B-1

Appendix E Release 3.2 Test Case Checklist	E-1

# MOC Test Cases

## NANC 187

For each test case related to NANC 187, Blocking Factors should be set to the maximum allowable number to verify that all systems are capable of supporting the maximum amount.

### MOC.SOA.CAP.ACT.LINK.lnpNetwork.lnpDownload

| Purpose | To test the SOA's ability to download the serviceProvNPA-NXX, serviceProvNPA-NXX-X (optional data recovered by EDR Service Providers), and serviceProvLRN objects instantiated on the NPAC SMS Simulator and receive them using linked replies. This will be accomplished by the SOA issuing the confirmed M-ACTION request for lnpDownload via the lnpNetwork object and subsequently handling the NPAC SMS Simulator M-ACTION response(s). This test case must be executed three times, once for no objects (a no data selected response will be returned), once where the number of objects is less than or equal to the associated Blocking Factor (a single non-linked response will be returned), and once where the number of objects is greater than the associated Blocking Factor (two or more linked replies will be returned, followed by an empty non-linked response at the end). |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the SOA is to support network data recovery using linked replies. |
| Prerequisites | Network data to be recovered exists. The data to be recovered includes data to be added, modified, or deleted for each type of network data to be recovered. |
| Procedure | SOA sends an lnpDownload M-ACTION request with criteria as supported by the product. NPAC SMS Simulator responds with an lnpDownload M-ACTION response using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. |
| Expected Results | The SOA sends a valid M-ACTION request and receives the NPAC SMS Simulator M-ACTION response properly using linked replies. |

This test case, 1.1.2, (MOC.SOA.INV.ACT.LINK.lnpNetwork.lnpDownload) is a duplicate of 11.5.4 (MOC.SOA.INV.ACT.lnpNetwork.lnpDownload).  Delete this one and make 11.5.4 a required test case for R3.2.  Since it is an error scenario, the tested functionality handles non-linked response.

### This test case, 1.1.3, (MOC.SOA.VAL.LINK.lnpDownload-NPA-NXX-X) should be part of the general recovery test case (MOC.SOA.CAP.ACT.LINK.lnpNetwork.lnpDownload).  It is optional functionality that is specific only to EDR Service Providers.  Delete this test case.MOC.SOA.CAP.ACT.LINK.lnpNotificationRecovery

| Purpose | Verify SOA can successfully process the lnpNotificationRecovery action when the SOA supports linked replies. This test case must be executed three times, once for no objects (a no data selected response will be returned), once where the number of objects is less than or equal to the associated Blocking Factor (a single non-linked response will be returned), and once where the number of objects is greater than the associated Blocking Factor (two or more linked replies will be returned, followed by an empty non-linked response at the end). This test case must be executed an additional three times if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider SOA supports notification recovery using linked replies. The SOA will recover either the “individual” notifications or the “range/list” version of the notifications, and they will be sent using linked replies. |
| Prerequisites | Notifications exist of each type of notification that can be recovered for the requesting service provider. If the “range/list” version of the notifications is being recovered, there must be notifications for each type that use both the “list-data” and “range-data”. There are a number of notifications to be recovered for both “individual” subscription version notifications and “range/list” subscription version notifications. |
| Procedure | SOA sends the lnpNotificationRecovery action to the NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with an M-ACTION lnpNotificationRecovery response using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. |
| Expected Results | SOA sends the M-ACTION and receives action response using linked replies with the notification data. |

This test case 1.1.5, (MOC.SOA.INV.ACT.LINK.lnpNotificationRecovery) is a duplicate of 11.1.8 (MOC.SOA.INV.ACT.lnpNotificationRecovery).  Delete this one and make 11.1.8 a required test case for R3.2.  Since it is an error scenario, the tested functionality handles non-linked response.

### MOC.LSMS.CAP.ACT.LINK.lnpNetwork.lnpDownload

| Purpose | To test the LSMS's ability to download the serviceProvNPA-NXX, serviceProvNPA-NXX-X (optional data recovered by EDR Service Providers), and serviceProvLRN objects instantiated on the NPAC SMS Simulator and receive them using linked replies. This will be accomplished by the LSMS issuing the confirmed M-ACTION request for lnpDownload via the lnpNetwork object and subsequently handling the NPAC SMS Simulator M-ACTION response(s). This test case must be executed three times, once for no objects (a no data selected response will be returned), once where the number of objects is less than or equal to the associated Blocking Factor (a single non-linked response will be returned), and once where the number of objects is greater than the associated Blocking Factor (two or more linked replies will be returned, followed by an empty non-linked response at the end). |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the LSMS is to support network data recovery using linked replies. |
| Prerequisites | Network data to be recovered exists. The data to be recovered includes data to be added, modified, or deleted for each type of network data to be recovered. |
| Procedure | LSMS sends an lnpDownload M-ACTION request with criteria as supported by the product. NPAC SMS Simulator responds with an lnpDownload M-ACTION response using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. |
| Expected Results | The LSMS sends a valid M-ACTION request and receives the NPAC SMS Simulator M-ACTION response properly using linked replies. |

This test case, 1.1.7, (MOC.LSMS.INV.ACT.LINK.lnpNetwork.lnpDownload) is a duplicate of 13.4.4 (MOC.LSMS.INV.ACT.lnpNetwork.lnpDownload).  Delete this one and make 13.4.4 a required test case for R3.2.  Since it is an error scenario, the tested functionality handles non-linked response.

### MOC.LSMS.CAP.ACT.LINK.lnpSubscriptions.lnpDownload

| Purpose | To test the LSMS's ability to download the subscriptionVersionNPAC objects instantiated on the NPAC SMS Simulator when the LSMS supports linked replies. This will be accomplished by the LSMS issuing the confirmed M-ACTION request for lnpDownload via the lnpSubscription object and subsequently handling the NPAC SMS Simulator M-ACTION response(s). This test case must be executed three times, once for no objects (a no data selected response will be returned), once where the number of objects is less than or equal to the associated Blocking Factor (a single non-linked response will be returned), and once where the number of objects is greater than the associated Blocking Factor (two or more linked replies will be returned, followed by an empty non-linked response at the end). |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the LSMS supports subscription data recovery using linked replies. |
| Prerequisites | A lnpSubscriptions managed object instance has been inherently created. |
| Procedure | LSMS sends a valid lnpDownload M-ACTION request. NPAC SMS Simulator responds with a successful M-ACTION response using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. |
| Expected Results | The LSMS sends a valid M-ACTION request, and receives the NPAC SMS Simulator's M-ACTION response properly using linked replies. |

### MOC.LSMS.INV.ACT.LINK.lnpSubscriptions.lnpDownload

| Purpose | To test the LSMS's ability to handle an error response for the lnpDownload action when the LSMS supports linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the LSMS supports subscription data recovery using linked replies. |
| Prerequisites |  |
| Procedure | LSMS sends an lnpDownload M-ACTION request for subscription data with criteria as supported by the product. NPAC SMS Simulator responds with error status ‘failed’. |
| Expected Results | The LSMS will correctly handle the error response received from the NPAC SMS Simulator. |

This test case, 1.1.3, (MOC.SOA.VAL.LINK.lnpDownload-NPA-NXX-X) should be part of the general recovery test case (MOC.LSMS.CAP.ACT.LINK.lnpNetwork.lnpDownload).  It is optional functionality that is specific only to EDR Service Providers.  Delete this test case.

### MOC.LSMS.VAL.LINK.lnpDownload-NumberPoolBlock

| Purpose | Verify the LSMS’s ability to issue the lnpDownload action for numberPoolBlock data when the LSMS supports linked replies. This test case must be executed three times, once for no objects (a no data selected response will be returned), once where the number of objects is less than or equal to the associated Blocking Factor (a single non-linked response will be returned), and once where the number of objects is greater than the associated Blocking Factor (two or more linked replies will be returned, followed by an empty non-linked response at the end). |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if LSMS will be supporting numberPoolBlock data using linked replies. |
| Prerequisites | NumberPoolBlock objects exist on the NPAC SMS Simulator. |
| Procedure | LSMS issues a valid lnpDownload M-ACTION request for all or specific numberPoolBlock objects. NPAC SMS Simulator responds with a successful M-ACTION response using linked replies containing the requested data. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. |
| Expected Results | LSMS issues a valid M-ACTION request and receives the data successfully using linked replies from the NPAC SMS Simulator. |

### MOC.LSMS.CAP.ACT.LINK.lnpNotificationRecovery

| Purpose | Verify LSMS can successfully process the lnpNotificationRecovery action when the LSMS supports linked replies. This test case must be executed three times, once for no objects (a no data selected response will be returned), once where the number of objects is less than or equal to the associated Blocking Factor (a single non-linked response will be returned), and once where the number of objects is greater than the associated Blocking Factor (two or more linked replies will be returned, followed by an empty non-linked response at the end). |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider LSMS supports notification recovery using linked replies. |
| Prerequisites | Notifications exist of each type of notification that can be recovered for the requesting service provider. There are a number of notifications to be recovered for “individual” subscription version notifications. |
| Procedure | LSMS sends the lnpNotificationRecovery action to the NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with an M-ACTION lnpNotificationRecovery response using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. |
| Expected Results | LSMS sends the M-ACTION and receives action response using linked replies with the notification data. |

This test case, 1.1.13, (MOC.LSMS.INV.ACT.LINK.lnpNotificationRecovery) is a duplicate of 13.1.10 (MOC.LSMS.INV.ACT.lnpNotificationRecovery).  Delete this one and make 13.1.10 a required test case for R3.2.  Since it is an error scenario, the tested functionality handles non-linked response.

### MOC.SOA.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNetwork.lnpDownload

| Purpose | To test the SOA 's ability to handle a criteria-too-large error response for the lnpDownload action when the SOA supports linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the SOA supports network data recovery using linked replies. |
| Prerequisites |  |
| Procedure | SOA sends an lnpDownload M-ACTION request for network data with criteria as supported by the product. NPAC SMS Simulator responds with error status ‘criteria-too-large’. |
| Expected Results | The SOA will correctly handle the error response received from the NPAC SMS Simulator. |

### MOC.SOA.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNotificationRecovery

| Purpose | Verify SOA can successfully process a criteria-too-large error response to the lnpNotificationRecovery action when the SOA supports linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider SOA supports notification recovery using linked replies. |
| Prerequisites |  |
| Procedure | SOA sends the lnpNotificationRecovery action to the NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with error status ‘criteria-too-large’. |
| Expected Results | SOA sends the M-ACTION request and receives the action response with the error successfully. |

### MOC.LSMS.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNetwork.lnpDownload

| Purpose | To test the LSMS's ability to handle a criteria-too-large error response for the lnpDownload action when the LSMS supports linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the LSMS supports network data recovery using linked replies. |
| Prerequisites |  |
| Procedure | LSMS sends an lnpDownload M-ACTION request for network data with criteria as supported by the product. NPAC SMS Simulator responds with error status ‘criteria-too-large’. |
| Expected Results | The LSMS will correctly handle the error response received from the NPAC SMS Simulator. |

### MOC.LSMS.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNotificationRecovery

| Purpose | Verify LSMS can successfully process a criteria-too-large error response to the lnpNotificationRecovery action when the LSMS supports linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider LSMS supports notification recovery using linked replies. |
| Prerequisites |  |
| Procedure | LSMS sends the lnpNotificationRecovery action to the NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with error status ‘criteria-too-large’. |
| Expected Results | LSMS sends the M-ACTION request and receives the action response with the error successfully. |

### MOC.LSMS.INV.ACT.LINK.CRIT.TOO.LARGE.lnpSubscriptions.lnpDownload

| Purpose | Verify LSMS can successfully process a criteria-too-large error response to the lnpDownload action for subscription data when the LSMS supports linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider LSMS supports subscription data recovery using linked replies. |
| Prerequisites |  |
| Procedure | LSMS sends the lnpDownload action for subscription data to the NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with error status ‘criteria-too-large’. |
| Expected Results | LSMS sends the M-ACTION request and receives the action response with the error successfully. |

## NANC 218

### MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOldSP-Create-Initial

| Purpose | To test the SOA’s ability to do the initial create with an authorization set to FALSE of a subscriptionVersionNPAC object, as the old service provider, and the subsequent objectCreationNotification that contains the conflict timestamp. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider SOA supports an old service provider create with authorization set to FALSE. |
| Prerequisites | An lnpSubscriptions managed object instance has been inherently created. |
| Procedure | SOA issues the M-ACTION subscriptionVersionOldSP-Create action with authorization set to FALSE. NPAC SMS Simulator responds with a successful M-ACTION reply. NPAC SMS Simulator issues the objectCreation or subscriptionVersionRangeObjectCreation M-EVENT-REPORT that contains the conflict timestamp. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA sends a valid M-ACTION request and receives the NPAC SMS Simulator's M-ACTION response and M-EVENT-REPORT properly that contains the conflict timestamp. |

### MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOldSP-Create-Second

| Purpose | To test the SOA’s ability to do the second create of a subscriptionVersionNPAC object with an authorization set to FALSE, as the old service provider, and the subsequent attributeValueChange that contains the conflict timestamp. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | This test case must be executed if the service provider SOA supports an old service provider create with authorization set to FALSE. |
| Prerequisites | MOC.SOA.CAP.ACT.subscriptionVersionNewSP-Create-Initial |
| Procedure | SOA issues the M-ACTION subscriptionVersionOldSP-Create action with authorization set to FALSE. NPAC SMS Simulator responds with a successful M-ACTION reply. NPAC SMS Simulator issues the attributeValueChange or subscriptionVersionRangeAttributeValueChange M-EVENT-REPORT that contains the conflict timestamp. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA sends a valid M-ACTION request and receives the NPAC SMS Simulator's M-ACTION response and M-EVENT-REPORT properly that contains the conflict timestamp. |

This test case, 1.2.3, (MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionModify) is the same as the previous test case from a MOC perspective (MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOld SP-Create-Second).  Delete this test case.

### MOC.SOA.CAP.NOT.RANGE.CONFLICT.subscriptionVersionRangeObjectCreation

| Purpose | To test the SOA’s ability to accept a subscriptionVersionRangeObjectCreation M-EVENT-REPORT, including the conflict timestamp. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting the subscriptionVersionRangeObjectCreation notification. |
| Prerequisites | A lnpSubscriptions managed object instance has been inherently created. |
| Procedure | NPAC SMS Simulator issues the subscriptionVersionRangeObjectCreation M-EVENT-REPORT for 1 or more subscription versions with consecutive TNs and subscription version Ids, along with the conflict timestamp. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA receives the NPAC SMS Simulator's M-EVENT-REPORT that contains the conflict timestamp and acknowledges it correctly. |

### MOC.SOA.CAP.NOT.RANGE.CONFLICT.subscriptionVersionRangeAttributeValueChange

| Purpose | To test the SOA’s ability to accept a subscriptionVersionRangeAttributeValueChange M-EVENT-REPORT, including the conflict timestamp. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting the subscriptionVersionRangeAttributeValueChange M-EVENT-REPORT. |
| Prerequisites | The service provider SOA has issued a subscriptionVersionNewSP-Create action and created 1 or more ‘pending’ subscription versions on the NPAC SMS Simulator. |
| Procedure | NPAC SMS Simulator issues the subscriptionVersionRangeAttributeValueChange M-EVENT-REPORT, simulating the Old Service Provider create, for 1 or more ‘pending’ subscription versions with consecutive TNs and subscription version Ids, with authorization set to FALSE, along with the conflict timestamp. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA receives the NPAC SMS Simulator's M-EVENT-REPORT that contains the conflict timestamp and acknowledges it correctly. |

### MOC.SOA.CAP.NOT.LIST.CONFLICT.subscriptionVersionRangeObjectCreation

| Purpose | To test the SOA’s ability to accept a subscriptionVersionRangeObjectCreation M-EVENT-REPORT, including the conflict timestamp. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting the subscriptionVersionRangeObjectCreation notification. |
| Prerequisites | An lnpSubscriptions managed object instance has been inherently created. |
| Procedure | NPAC SMS Simulator issues the subscriptionVersionRangeObjectCreation M-EVENT-REPORT for 2 or more subscription versions with consecutive TNs and non-consecutive subscription version Ids, with authorization set to FALSE, along with the conflict timestamp. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA receives the NPAC SMS Simulator's M-EVENT-REPORT that contains the conflict timestamp and acknowledges it correctly. |

### MOC.SOA.CAP.NOT.LIST.CONFLICT.subscriptionVersionRangeAttributeValueChange

| Purpose | To test the SOA’s ability to accept a subscriptionVersionRangeAttributeValueChange M-EVENT-REPORT, including the conflict timestamp. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting the subscriptionVersionRangeAttributeValueChange M-EVENT-REPORT. |
| Prerequisites | The service provider SOA has issued a subscriptionVersionNewSP-Create action and created 2 or more ‘pending’ subscription versions on the NPAC SMS Simulator with consecutive TNs and non-consecutive subscription version Ids. |
| Procedure | NPAC SMS Simulator issues the subscriptionVersionRangeRangeAttributeValueChange M-EVENT-REPORT, simulating the Old Service Provider, with authorization set to FALSE, along with the conflict timestamp. SOA confirms the M-EVENT-REPORT for 2 or more subscription versions with consecutive TNs and non-consecutive subscription version Ids. |
| Expected Results | The SOA receives the NPAC SMS Simulator's M-EVENT-REPORT that contains the conflict timestamp and acknowledges it correctly. |

## NANC 230

### MOC.SOA.CAP.ACT.PTOLISP.subscriptionVersionNewSP-Create-Initial

| Purpose | To test the SOA’s ability to do the initial create of a port-to-original intra-port subscriptionVersionNPAC object as the new service provider. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting a PTO LISP. |
| Prerequisites | An lnpSubscriptions managed object instance has been inherently created. |
| Procedure | SOA issues the M-ACTION subscriptionVersionNewSP-Create action for a PTO LISP port. NPAC SMS Simulator responds with a successful M-ACTION reply. NPAC SMS Simulator issues the objectCreation or subscriptionVersionRangeObjectCreation M-EVENT-REPORT. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA sends a valid M-ACTION request for a PTO LISP port, and receives the NPAC SMS Simulator's M-ACTION response and M-EVENT-REPORT properly. |

This test case, 1.3.2, (MOC.SOA.INV.ACT.PTOLISP.subscriptionVersionNewSP-Create) is a duplicate of 11.4.16 (MOC.SOA.INV.ACT.subscriptionVersionNewSP-Create).  Delete this one and make 11.4.16 a required test case for R3.2.

### MOC.SOA.CAP.NOT.RANGE.PTOLISP.subscriptionVersionRangeObjectCreation

| Purpose | To test the SOA’s ability to accept a subscriptionVersionRangeObjectCreation M-EVENT-REPORT, for a PTO LISP port. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting a PTO LISP port. |
| Prerequisites | An lnpSubscriptions managed object instance has been inherently created. |
| Procedure | NPAC SMS Simulator issues the subscriptionVersionRangeObjectCreation M-EVENT-REPORT for 1 or more subscription versions with consecutive TNs and subscription version Id for a PTO LISP port. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA receives the NPAC SMS Simulator's M-EVENT-REPORT for a PTO LISP port and acknowledges it correctly. |

### MOC.SOA.CAP.NOT.LIST.PTOLISP.subscriptionVersionRangeObjectCreation

| Purpose | To test the SOA’s ability to accept a subscriptionVersionRangeObjectCreation M-EVENT-REPORT, for a PTO LISP port. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting a PTO LISP port. |
| Prerequisites | An lnpSubscriptions managed object instance has been inherently created. |
| Procedure | NPAC SMS Simulator issues the subscriptionVersionRangeObjectCreation M-EVENT-REPORT for 2 or more subscription versions with consecutive TNs and non-consecutive subscription version Ids for a PTO LISP port. SOA confirms the M-EVENT-REPORT. |
| Expected Results | The SOA receives the NPAC SMS Simulator's M-EVENT-REPORT for a PTO LISP port and acknowledges it correctly. |

This test case, 1.3.5, (MOC.SOA.INV.NOT.RANGE.PTOLISP.subscriptionVersionRangeObject Creation) is a duplicate of 11.4.47 (MOC.SOA.INV.NOT.RANGE.subscriptionVersionRangeObjectCreation).  Delete this one and make 11.4.47 a required test case for R3.2.

## NANC 249

### MOC.SOA.CAP.ACT.DISCONPEND.subscriptionVersionModify

| Purpose | To test the SOA’s ability to modify a disconnect-pending subscription version. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if SOA will be supporting the subscriptionVersionModify notification of a disconnect-pending port. |
| Prerequisites |  |
| Procedure | SOA issues a valid subscriptionVersionModify M-ACTION and specifies either the subscriptionVersionId or subscriptionVersionTN and status, along with the Customer Disconnect Date, and optionally the Effective Release Date. NPAC SMS Simulator responds with a successful M-ACTION response. |
| Expected Results | The SOA issues a valid M-ACTION request and receives the NPAC SMS Simulator's M-ACTION response and M-EVENT-REPORT properly. |

This test case, 1.4.2, (MOC.SOA.INV.ACT.DISCONPEND.subscriptionVersionModify) is a duplicate of 11.4.19 (MOC.SOA.INV.ACT.subscriptionVersionModify).  Delete this one and make 11.4.19 a required test case for R3.2.

## NANC 319

This test case, 1.5.1, (MOC.SOA.INV.CRE.LATA.serviceProvNPA-NXX) is a duplicate of 11.10.6 (MOC.SOA.INV.CRE.serviceProvNPA-NXX).  Delete this one and make 11.10.6 a required test case for R3.2.

This test case, 1.5.2, (MOC.SOA.INV.CRE.LATA.serviceProvLRN) is a duplicate of 11.11.6 (MOC.SOA.INV.CRE.serviceProvLRN).  Delete this one and make 11.11.6 a required test case for R3.2.

### MOC.LSMS.INV.CRE.LATA.serviceProvNPA-NXX

| Purpose | To test the LSMS’s ability to handle the M-CREATE error response for a previously initiated and valid M-CREATE request for a serviceProvNPA-NXX, when that NPA-NXX does NOT have a corresponding entry in the NPAC’s LATA ID lookup table. |
| --- | --- |
| Severity | C |
| Severity Explanation | Must be performed if prerequisite is performed. |
| Prerequisites | MOC.LSMS.VAL.CRE.AUTO.serviceProvNPA-NXX |
| Procedure | LSMS issues an M-CREATE request for the serviceProvNPA-NXX object. NPAC SMS Simulator responds with a processing failure error. |
| Expected Results | The LSMS correctly handles the error response from the NPAC SMS Simulator. |

### MOC.LSMS.INV.CRE.LATA.serviceProvLRN

| Purpose | To test the LSMS’s ability to handle the M-CREATE error response for a previously initiated and valid M-CREATE request for a serviceProvLRN, when the first 6-digits (NPA-NXX) of that LRN does NOT have acorresponding entry in the NPAC’s LATA ID lookup table. |
| --- | --- |
| Severity | C |
| Severity Explanation | Must be performed if prerequisite is performed. |
| Prerequisites | MOC.LSMS.VAL.CRE.AUTO.serviceProvLRN |
| Procedure | LSMS issues a valid M-CREATE request a serviceProvLRN. NPAC SMS Simulator responds with a processing failure error. |
| Expected Results | The LSMS correctly handles the error response from the NPAC SMS Simulator. |

# A2A Test Cases

## NANC 187

For each test case related to NANC 187, Blocking Factors should be set to the maximum allowable number to verify that all systems are capable of supporting the maximum amount.

### A2A.SOA.VAL.MISC.ACTION.LINK.resync

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator using linked replies. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support network and/or notification data recovery using linked replies. |
| Prerequisites | Network and notification data exist to recover. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting network data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start network data download for a specified period of time. NPAC SMS Simulator responds with network data updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues data download and/or notification recovery actions, and receives action responses containing network and/or notification data updates using linked replies. Test case must be executed twice for each type of recovery if both recovery requests cannot be issued sequentially. |

### A2A.SOA.INV.MISC.ACTION.LINK.resync

| Purpose | Verify SOA can process resynchronization update errors from NPAC SMS Simulator. The purpose of this scenario is to test the behavior of the SOA under the following conditions with the SOA having established association with NPAC SMS Simulator, with resynchronization flag on, when the SOA supports linked replies: SOA, if supporting network data, sends the lnpDownload action request to start network data download for a specified period of time and the NPAC SMS Simulator responds with criteria-too-large error. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time and the NPAC SMS Simulator responds with criteria-too-large error. The procedure and behavior responses for this scenario should be agreed upon between the test engineer and vendor. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support network and/or notification data recovery using linked replies. |
| Prerequisites | Network and notification data exists to be recovered. |
| Procedure | To be determined by vendor and test engineer. Note: This test case may need to be executed more than once to complete the testing requirements. |
| Expected Results | SOA associates in recovery mode, issues data download and/or notification recovery actions, and receives action and handles error conditions. |

### A2A.SOA.VAL.MISC.ACTION.LINK.ASSOCSP.resync

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator using linked replies for an associated service provider. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support network and/or notification data recovery using linked replies for an associated service provider. |
| Prerequisites | Network and notification data exist to recover for the associated service provider. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting network data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start network data download at a specified period of time for the associated service provider. NPAC SMS Simulator responds with network data updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time for the associated service provider. NPAC SMS Simulator responds with notification updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. SOA sends the lnpRecoveryComplete action request to the NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator responds to the action. |
| Expected Results | SOA associates in recovery mode, issues data download and notification recovery actions, and receives action responses containing network and notification data updates using linked replies for the associated service. Test case must be executed twice for each type of recovery if both recovery requests cannot be issued sequentially. |

This test case, 2.1.4, (A2A.SOA.VAL.MISC.ACTION.LINK.resync_3_1) covers the same functionality as 2.1.1 (A2A.SOA.VAL.MISC.ACTION.LINK.resync).  Delete this test case.

### A2A.LSMS.VAL.MISC.ACTION.LINK.resync

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator using linked replies. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support notification data recovery using linked replies. |
| Prerequisites | Network, subscription, and notification data exist to recover. Test case must be executed independently for each type of recovery supported if the recovery requests can not be issued sequentially. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supported, sends the lnpDownload action request to NPAC SMS Simulator to start network data download at a specified period of time. NPAC SMS Simulator responds with network data updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. LSMS, if supported, sends the lnpDownload action request to NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with subscription data updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. LSMS, if supported, sends the lnpDownload action request to NPAC SMS Simulator to start number pool block data download for a specified period of time. NPAC SMS Simulator responds with number pool block updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. LSMS, if supported, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. |
| Procedure (con’t) | NPAC SMS Simulator responds with notification data updates using linked replies. In the case of no objects, the NPAC SMS Simulator responds with a no data selected response. In the case where the number of objects is less than or equal to the associated Blocking Factor, the NPAC SMS Simulator responds with a single non-linked response. In the case where the number of objects is greater than the associated Blocking Factor, the NPAC SMS Simulator responds with two or more linked replies, followed by an empty non-linked response. LSMS sends the lnpRecoveryComplete action request to NPAC to set resynchronization flag off. NPAC SMS Simulator responds to the action. |
| Expected Results | LSMS associates in recovery mode, issues data download and notification recovery actions, and receives action responses containing network, subscription and notification data updates using linked replies, and takes appropriate action to update its databases. |

This test case, 2.1.6, (A2A.LSMS.INV.MISC.ACTION.LINK.resync) is a duplicate of 16.15.5 (A2A.LSMS.INV.MISC.ACTION.resync).  Delete this one and make 11.15.5 a required test case for R3.2.  Since it is an error scenario, the tested functionality handles non-linked response.

## NANC 218

This test case, 2.2.1, (A2A.SOA.CAP.OP.SET.PEND.CONMFLICT.subscriptionVersion) is not needed, since the functionality is covered in the existing test cases below.

### A2A.NSOA.VAL.CREATE.CONFLICT.SubscriptionVersion

Existing Test Case, verify conflict timestamp is sent in attribute value change notification.

### A2A.OSOA.VAL.CREATE.CONFLICT.SubscriptionVersion

Existing Test Case, verify conflict timestamp is sent in attribute value change notification.

### A2A.NSOA.INV.CANCEL.CONFLICT.SubscriptionVersion

Existing Test Case, verify conflict timestamp is sent in attribute value change notification.

### A2A.OSOA.INV.CANCEL.CONFLICT.SubscriptionVersion

Existing Test Case, verify conflict timestamp is sent in attribute value change notification.

### A2A.OSOA.VAL.MODIFY.PEND.subscriptionVersion

Existing Test Case, verify conflict timestamp is sent in attribute value change notification.

## NANC 230

### A2A.DONORSOA.VAL.PORT-TO-ORIG.PTOLISP.SubscriptionVersion

| Purpose | To verify a New Service Provider SOA (Donor SOA) can perform a port-to-original of an intra-service provider port. The Old Service Provider SOA is simulated. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a Donor SOA is to support subscription version PTO of intra-service provider port. |
| Prerequisites | All subscription version create, activate and disconnect test cases. |
| Procedure | The New Service Provider SOA (Donor SOA) issues the subscriptionVersionCreate action specifying a port-to-original by setting the subscriptionPortingToOriginal-Service ProviderSwitch attribute to ‘true’, and LNP Type of LISP. The NPAC SMS Simulator locally creates the ‘pending’ subscription version, responds to the M-ACTION and issues the objectCreation or subscriptionVersionRangeObjectCreation notification. The SOA (Donor SOA) confirms the objectCreation notification sent by the NPAC SMS Simulator. The SOA (Donor SOA) issues the M-ACTION subscriptionVersionActivate for the newly created and ‘pending’ subscriptionVersionNPAC instance. The NPAC SMS Simulator locally sets the subscriptionVersionStatus of the ‘pending’ instance to ‘sending’, and responds to the M-ACTION. The NPAC SMS Simulator emulates deleting the version from all the LSMSs, locally sets the subscriptionVersionStatus to ‘old’, and sends the subscriptionVersionStatusAttributeValueChange or subscriptionVersionRangeStatusAttributeValueChange notification to the SOA. The New Service Provider SOA (Donor SOA) confirms the notification. |
| Expected Results | The SOA (Donor SOA) successfully initiates the transaction and handles the subsequent interactions with the NPAC SMS Simulator. The created subscriptionVersionNPAC instance will have a final status of ‘old’. |

### A2A.SOA.VAL.PORT-TO-ORIG.ASSOCSP.PTOLISP.SubscriptionVersion

| Purpose | To verify that the SOA can, for an associated service provider, create a port-to-original intra-service provider port. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a SOA is to support intra-service provider subscription version processing for port-to-original porting. |
| Prerequisites |  |
| Procedure | The SOA issues the subscriptionVersionCreate action for a port-to-original by setting the subscriptionPortingToOriginal-SPSwitch attribute to TRUE, and LNP Type of LISP. The SOA handles the M-ACTION response. The NPAC SMS Simulator locally creates the ‘pending’ subscription version and emits the objectCreation or subscriptionVersionRangeObjectCreation notification. The SOA handles the notification sent by the NPAC SMS Simulator, and confirms it. The SOA issues the M-ACTION subscriptionVersionActivate for the newly created and ‘pending’ subscriptionVersionNPAC instance. The SOA handles the action response message sent by the NPAC simulator. The NPAC SMS Simulator locally sets the subscriptionVersionStatus of the ‘pending’ instance to ‘sending’. The NPAC SMS Simulator emulates deleting that version from all the LSMSs, locally sets the subscriptionVersionStatus to ‘old’, and sends the subscriptionVersionStatusAttributeValueChange or subscriptionVersionRangeStatusAttributeValueChange notification to the SOA for the ‘old’ status. The SOA handles the notification for the ‘old’ Status, and responds with confirmation. |
| Expected Results | The SOA successfully initiates the port to original intra-service provider port and handles the subsequent interactions with the NPAC SMS simulator. |

## NANC 249

### A2A.SOA.VAL.MODIFY.DISCONPEND.SubscriptionVersion

| Purpose | To test that a SOA can modify a disconnect pending subscription version. The LSMSs are simulated. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a SOA is to support subscription version modification of disconnect pending status. |
| Prerequisites | A subscription version had been created, activated, and set to future-dated disconnect. |
| Procedure | The SOA issues an M-ACTION subscriptionVersionModify to NPAC SMS Simulator. The NPAC SMS Simulator locally sets the subscriptionVersionNPAC attributes values for the instance to be modified, and responds to the M-ACTION. The NPAC SMS Simulator sends the subscriptionVersionStatusAttributeValueChange or subscriptionVersionRangeStatusAttributeValueChange notification to the SOA. The SOA confirms the notification. |
| Expected Results | The SOA successfully initiate the transaction and handles the subsequent interactions with the NPAC SMS Simulator. The subscriptionVersionNPAC attributes are modified. |

### A2A.SOA.INV.MODIFY.DISCONPEND.SubscriptionVersion

| Purpose | To verify a SOA can handle the error condition for the modification of future-dated disconnect dates, and the subscription version is not updated in response to a modify disconnect pending version scenario. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a SOA is to support subscription version modification of disconnect pending status. |
| Prerequisites | A subscription version had been created, activated, and set to future-dated disconnect. |
| Procedure | The SOA issues an M-ACTION subscriptionVersionModify to NPAC SMS Simulator. NPAC SMS Simulator responds with error status ‘failed’. |
| Expected Results | The SOA will correctly handle the error response received from the NPAC SMS Simulator. |

### A2A.SOA.VAL.MODIFY.TN-RANGE.DISCONPEND.SubscriptionVersion

| Purpose | Verify a SOA can modify disconnect pending subscription versions on the NPAC SMS Simulator using a TN range. The LSMSs are simulated. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | SOA must execute if supporting range modifications using the subscriptionVersionModify action. |
| Prerequisites | A2A.SOA.VAL.MODIFY.DISCONPEND.SubscriptionVersion A range of disconnect pending subscription versions exists. |
| Procedure | The SOA issues an M-ACTION subscriptionVersionModify to NPAC SMS Simulator, using a TN-Range. The NPAC SMS Simulator locally sets the subscriptionVersionNPAC attributes values for the instances to be modified, and responds to the M-ACTION. The NPAC SMS Simulator sends the subscriptionVersionStatusAttributeValueChange or subscriptionVersionRangeStatusAttributeValueChange notification. The SOA confirms the notifications. |
| Expected Results | The SOA successfully initiate the transaction and handles the subsequent interactions with the NPAC SMS Simulator. The subscriptionVersionNPAC attributes for all the instances in the TN range are modified. |

### A2A.SOA.INV.MODIFY.TN-RANGE.DISCONPEND.SubscriptionVersion

| Purpose | To verify a SOA can handle the error condition for the modification of future-dated disconnect dates using a TN range, and the subscription versions are not updated in response to a modify disconnect pending version scenario. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a SOA is to support subscription version modification of disconnect pending status using a TN range. |
| Prerequisites | A range of subscription versions has been created, activated, and set to future-dated disconnect. |
| Procedure | The SOA issues an M-ACTION subscriptionVersionModify to NPAC SMS Simulator. NPAC SMS Simulator responds with error status ‘failed’. |
| Expected Results | The SOA will correctly handle the error response received from the NPAC SMS Simulator. |

### A2A.SOA.VAL.MODIFY.ASSOCSP.DISCONPEND.SubscriptionVersion

| Purpose | To test that a SOA, for an associated service provider, can modify a disconnect pending subscription version. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a SOA is to support associated service provider subscription version processing for modify of disconnect pending status. |
| Prerequisites | A disconnect pending subscription version exists for the service provider. |
| Procedure | The SOA, for an associated service provider, issues an M-ACTION subscriptionVersionModify to NPAC SMS Simulator to modify routing data with an associated service provider is specified in the access control SystemId and handles the action response message from the NPAC SMS Simulator. The NPAC SMS Simulator locally sets the subscriptionVersionNPAC attributes values for the instance to be modified. The NPAC SMS Simulator sends a subscriptionVersionStatusAttributeValueChange or subscriptionVersionRangeStatusAttributeValueChange. The SOA, for an associated service provider, handles the notification sent by the NPAC SMS Simulator for the ‘disconnect pending’ status, and responds with confirmation. |
| Expected Results | The SOA, acting for an associated service provider, successfully initiate the subscriptionVersionModify M-ACTION and handles the subsequent interactions with the NPAC SMS Simulator. |

### A2A.SOA.INV.MODIFY.ASSOCSP.DISCONPEND.SubscriptionVersion

| Purpose | To verify a SOA can handle the error condition for the modification of a future-dated disconnect date, for an associated service provider, and the subscription version is not updated in response to a modify disconnect pending version scenario. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Test case must be executed if a SOA is to support associated service provider subscription version processing for modify of disconnect pending status. |
| Prerequisites | A subscription version had been created, activated, and set to future-dated disconnect. |
| Procedure | The SOA, for an associated service provider, issues an M-ACTION subscriptionVersionModify to NPAC SMS Simulator to modify routing data with an associated service provider is specified in the access control SystemId and handles the action response message from the NPAC SMS Simulator. NPAC SMS Simulator responds with error status ‘failed’. |
| Expected Results | The SOA, for an associated service provider, will correctly handle the error response received from the NPAC SMS Simulator. |

# Large, Single PDU Recovery Test Cases

During the 10/31/02 conference call, the following large PDU recovery test cases were discussed as to the benefit of requiring increasing quantities of notifications.  Participants on the call suggested that these should be limited to the current production values, and the maximum number per the tunable.  This will be discussed again during the second review of this document.

## SOA Recovery, Object Creation Notification

### A2A.SOA.VAL.MISC.ACTION.resync_500_ocn

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 500 object creation notifications. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_1000_ocn

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 1000 object creation notifications. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_2000_ocn

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 2000 object creation notifications. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

## SOA Recovery, Status Attribute Value Change Notification

### A2A.SOA.VAL.MISC.ACTION.resync_1failed_500_savc

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 500 status attribute value change notifications with one failed SP. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_1failed_1000_savc

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 1000 status attribute value change notifications with one failed SP. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_1failed_2000_savc

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 2000 status attribute value change notifications with one failed SP. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_20failed_500_savc

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 500 status attribute value change notifications with twenty failed SPs. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_20failed_1000_savc

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 1000 status attribute value change notifications with twenty failed SPs. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.SOA.VAL.MISC.ACTION.resync_20failed_2000_savc

| Purpose | Verify SOA can process resynchronization updates from NPAC SMS Simulator for 2000 status attribute value change notifications with twenty failed SPs. This test case must be executed twice if a SOA is supporting both “individual” and “range/list” notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a SOA is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | SOA established association with NPAC SMS Simulator, with resynchronization flag on. SOA, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. SOA sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | SOA associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

## LSMS Recovery, NPA-NXX First Usage Notification

### A2A.LSMS.VAL.MISC.ACTION.resync_500_firstusage

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 500 NPA-NXX first usage notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.LSMS.VAL.MISC.ACTION.resync_1000_firstusage

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 1000 NPA-NXX first usage notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

### A2A.LSMS.VAL.MISC.ACTION.resync_2000_firstusage

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 2000 NPA-NXX first usage notifications. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support notification data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required notification data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting notification data recovery, sends the lnpNotificationRecovery action request to NPAC SMS Simulator to start notification data download for a specified period of time. NPAC SMS Simulator responds with notification updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues notification recovery actions, and receives action responses containing notification data updates. |

## LSMS Recovery, Subscription Data, M-CREATE

### A2A.LSMS.VAL.MISC.ACTION.resync_500_sv

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 500 subscription data creates. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support subscription data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required subscription data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting subscription data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with subscription updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues subscription recovery actions, and receives action responses containing subscription data updates. |

### A2A.LSMS.VAL.MISC.ACTION.resync_1000_sv

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 1000 subscription data creates. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support subscription data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required subscription data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting subscription data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with subscription updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues subscription recovery actions, and receives action responses containing subscription data updates. |

### A2A.LSMS.VAL.MISC.ACTION.resync_2000_sv

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 2000 subscription data creates. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support subscription data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required subscription data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting subscription data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with subscription updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues subscription recovery actions, and receives action responses containing subscription data updates. |

### A2A.LSMS.VAL.MISC.ACTION.resync_5000_sv

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 5000 subscription data creates. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support subscription data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required subscription data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting subscription data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with subscription updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues subscription recovery actions, and receives action responses containing subscription data updates. |

### A2A.LSMS.VAL.MISC.ACTION.resync_10000_sv

| Purpose | Verify LSMS can process resynchronization updates from NPAC SMS Simulator for 10,000 subscription data creates. |
| --- | --- |
| Severity | C |
| Severity Explanation | Required if a LSMS is to support subscription data recovery. |
| Prerequisites | The NPAC SMS Simulator configuration tool is set up to build the required subscription data that needs to be recovered. |
| Procedure | LSMS established association with NPAC SMS Simulator, with resynchronization flag on. LSMS, if supporting subscription data recovery, sends the lnpDownload action request to NPAC SMS Simulator to start subscription data download for a specified period of time. NPAC SMS Simulator responds with subscription updates. LSMS sends action request to NPAC SMS Simulator to set the resynchronization flag off. NPAC SMS Simulator sends the action response. |
| Expected Results | LSMS associates in recovery mode, issues subscription recovery actions, and receives action responses containing subscription data updates. |

Appendix B Test Case Nomenclature

| stack-To-stack test-id symbols |
| --- |
| Abbreviation | Description |
| S2S | Stack-to-Stack Interoperability Testing |
| VAL | Valid Test |
| INV | Invalid Test |
| SOA | Initiating system is SOA |
| LSMS | Initiating system is LSMS |
| ASSOC | Association (A-ASSOCIATE) Request |
| RELES | Release (A-RELEASE) Request |
| ABORT | Abort (A-ABORT) Request |
| INVK | Invalid KEY |
| INVT | Invalid Time |
| ISMFU | Invalid Systems Management Functional Unit Identifier |
| ISEQ | Invalid Sequence Number |

| security test-id symbols |
| --- |
| Abbreviation | Description |
| SEC | Security Interoperability Testing |
| VAL | Valid Test |
| INV | Invalid Test |
| SOA | Initiating system is SOA |
| LSMS | Initiating system is LSMS |
| ASSOC | Association (A-ASSOCIATE) Request |
| RELES | Release (A-RELEASE) Request |
| ABORT | Abort (A-ABORT) Request |
| INVK | Invalid KEY |
| INVT | Invalid Time |
| ISMFU | Invalid Systems Management Functional Unit Identifier |
| ISEQ | Invalid Sequence Number |

| MOC test-id symbols |
| --- |
| Abbreviation | Description |
| MOC | Managed Object Conformance Interoperability Testing |
| NPAC | Initiating System is NPAC |
| SOA | Initiating system is SOA |
| LSMS | Initiating system is LSMS |
| CAP | MO Capability Test |
| OP | Operation Test |
| NOT | Notification Test |
| ACT | Action Test |
| VAL | Valid behaviour Test |
| INV | Invalid behaviour Test |
| CRE | MO Instance Create Test |
| DEL | MO Instance Delete Test |
| SET | Attribute Set Test |
| GET | Attribute Get Test |
| SING | Operation on Single Attribute Test |
| MULT | Operation on Multiple Attribute Test |
| COND | Operation on Conditional Attribute Test |
| AUTO | Automatic Object Naming |
| RO | Read Only |
| CO | Contained Objects |
| SCOP | Scoped Test |
| FILT | Filter Test |
| BND | Boundary Test |
| MIN | Lower Bound Test |
| MAX | Upper Bound Test |
| MAXQ | Maximum number of allowed queries |
| MAXB | Maximum number of allowed Bytes |
| RANGE | Tests the “range” structure of a “range/list” notification |
| LIST | Tests the “list” structure of a “range/list” notification |

| recovery test-id symbols |
| --- |
| Abbreviation | Description |
| AMG | Association Management Interoperability Testing |
| SOA | Initiating system is SOA |
| LSMS | Initiating system is LSMS |
| ASSOC | Association (A-ASSOCIATE) Request |
| REASSOC | re-establish Association |
| REQTMOT | Request Timeout Test |
| RETRY | Retry a Request |
| SWOV | Switch Over |
| BKUP | Backup NPAC |
| CMIP | CMIP requests |
| SECVIOL | Security Violation Test |
| LOSS | Association Loss Test |
| DOWN | NPAC Down test |
| SAME | Retry Same Host |
| OTHER | Retry Other Host |

| A2A test-id symbols |
| --- |
| Abbreviation | Description |
| A2A | Application to Application Test |
| LSMS | System Under Test is an LSMS |
| SOA | System Under Test is a SOA |
| NSOA | System Under Test is a New SOA |
| OSOA | System Under Test is an Old SOA |
| DSOA | System Under Test is a Donor SOA |
| VAL | Valid Transaction Test |
| INV | Invalid Transaction / Inopportune Behavior Test |
| Audit Test Cases |
| MISSVER | Missing Subscription Version Test |
| OBSVER | Old Subscription Version Test |
| ERRVER | Erroneous Subscription Version Test |
| NODIS | No Discrepancy Found Test |
| TN | Single Telephone Number Test |
| TNRNG | Telephone Number Range Test |
| ACTRNG | Activation Range Test |
| WITHDIS | Audit Discrepancy Found Test |
| NPACCNCLD | Canceled by NPAC |
| CRENOT | Object Creation Notification |
| TIMOUT | Operation/Transaction Timeout Test |
| COMP | Audit Complete Test |
| NORES | Missing Audit Results Test |
| NUMTN | Audit Number of TNs Test |
| COMPTN | Completed Number of TNs Test |
| NUMDISERR | Number of Discrepancies Error Test |
| Service Provider and Network Data Test Cases |
| SETSP | Set Service Provider Test |
| CREND | Create a Network Data Instance Test |
| DELND | Delete a Network Data Instance Test |
| Subscription Version Test Cases |
| CREATE | Subscription Version Creation Test |
| ACTIVATE | Subscription Version Activation Test |
| MODIFY | Subscription Version Modification Test |
| CANCEL | Subscription Version Cancellation Test |
| IMMDISC | Subscription Version Immediate Disconnect Test |
| DEFDISC | Subscription Version Deferred Disconnect Test |
| STATE-TRANS | State Transition Test |
| FIRST | First Create Transaction Test |
| SECOND | Second Create Transaction Test |
| TN-RANGE | Telephone Number Range Transaction Test |
| PEND | Pending Subscription Version Test |
| CONFLICT | Conflict Subscription Version Test |
| ACT, ACTIVE | Active Subscription Version Test |
| OLD | Old Subscription Version Test |
| PARTFAIL | Partially Failed Subscription Version Test |
| FAIL, FAILED | Failed Subscription Version Test |
| SENDING | Sending Subscription Version Test |
| CANCEL-PEND | Cancel-Pending Subscription Version Test |
| DISCPEND | Disconnect-Pending Subscription Version Test |
| OBJCRE | Object Creation Notification Test |
| NOTMISS | Missing Notification Test |
| ACTNOTMISS | Active Status Missing Notification Test |
| BYNPAC | Operation Performed by NPAC Test |
| BYOSOA | Operation Performed by Old SOA Test |
| BYNSOA | Operation Performed by New SOA Test |
| ATTRCHNG | Attribute is Changed Test |
| STATCHNG | Status Attribute is Changed Test |
| ATTRSAME | Attribute in Unchanged Test |
| NONONC | No Concurrence by Other SOA Test |
| ACKREQ | Acknowledge Request Test |
| RESOLV | Conflict Resolution Test |
| PORT-TO-ORIG | Port To Original SP Test |
| MULT | Multiple Versions Test |
| UNKNOWN | Unknown Instance Test |
| Miscellaneous Test Cases |
| MISC | Miscellaneous Test |
| ACTION | Action Request Test |
| EVENT | Event Report Test |
| SET | Set Request Test |

Appendix E Release 3.2 Test Case Checklist

| Test Case Number and Name | Sev | Date | Result |
| --- | --- | --- | --- |
| MOC NANC 187 |
| 1 | 1.1.1 | MOC.SOA.CAP.ACT.LINK.lnpNetwork.lnpDownload | C |  |  |
| 3 | 1.1.3 | MOC.SOA.VAL.LINK.lnpDownload-NPA-NXX-X | C |  |  |
| 4 | 1.1.4 | MOC.SOA.CAP.ACT.LINK.lnpNotificationRecovery | C |  |  |
| 6 | 1.1.6 | MOC.LSMS.CAP.ACT.LINK.lnpNetwork.lnpDownload | C |  |  |
| 8 | 1.1.8 | MOC.LSMS.CAP.ACT.LINK.lnpSubscriptions.lnpDownload | C |  |  |
| 9 | 1.1.9 | MOC.LSMS.INV.ACT.LINK.lnpSubscription.lnpDownload | C |  |  |
| 11 | 1.1.11 | MOC.LSMS.VAL.LINK.lnpDownload-NumberPoolBlock | C |  |  |
| 12 | 1.1.12 | MOC.LSMS.CAP.ACT.LINK.lnpNotificationRecovery | C |  |  |
|  | 1.1.8 | MOC.SOA.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNetwork.lnpDownload |  |  |  |
|  | 1.1.9 | MOC.SOA.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNotificationRecovery |  |  |  |
|  | 1.1.10 | MOC.LSMS.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNetwork.lnpDownload |  |  |  |
|  | 1.1.11 | MOC.LSMS.INV.ACT.LINK.CRIT.TOO.LARGE.lnpNotificationRecovery |  |  |  |
|  | 1.1.12 | MOC.LSMS.INV.ACT.LINK.CRIT.TOO.LARGE.lnpSubscriptions.lnpDownload |  |  |  |
| MOC NANC 218 |
| 1 | 1.2.1 | MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOldSP-Create-Initial | C |  |  |
| 2 | 1.2.2 | MOC.SOA.CAP.ACT.CONFLICT.subscriptionVersionOldSP-Create-Second | C |  |  |
| 4 | 1.2.4 | MOC.SOA.CAP.NOT.RANGE.CONFLICT.subscriptionVersionRangeObjectCreation | C |  |  |
| 5 | 1.2.5 | MOC.SOA.CAP.NOT.RANGE.CONFLICT.subscriptionVersionRangeAttributeValueChange | C |  |  |
| 6 | 1.2.6 | MOC.SOA.CAP.NOT.LIST.CONFLICT.subscriptionVersionRangeObjectCreation | C |  |  |
| 7 | 1.2.7 | MOC.SOA.CAP.NOT.LIST.CONFLICT.subscriptionVersionRangeAttributeValueChange | C |  |  |
| MOC NANC 230 |
| 1 | 1.3.1 | MOC.SOA.CAP.ACT.PTOLISP.subscriptionVersionNewSP-Create-Initial | C |  |  |
| 3 | 1.3.3 | MOC.SOA.CAP.NOT.RANGE.PTOLISP.subscriptionVersionRangeObjectCreation | C |  |  |
| 4 | 1.3.4 | MOC.SOA.CAP.NOT.LIST.PTOLISP.subscriptionVersionRangeObjectCreation | C |  |  |
| MOC NANC 249 |
| 1 | 1.4.1 | MOC.SOA.CAP.ACT.DISCONPEND.subscriptionVersionModify | C |  |  |
| MOC NANC 319 |
| 1 | 1.5.1 | MOC.LSMS.INV.CRE.LATA.serviceProvNPA-NXX | C |  |  |
| 2 | 1.5.2 | MOC.LSMS.INV.CRE.LATA.serviceProvLRN | C |  |  |
| A2A NANC 187 |
| 1 | 2.1.1 | A2A.SOA.VAL.MISC.ACTION.LINK.resync | C |  |  |
| 2 | 2.1.2 | A2A.SOA.INV.MISC.ACTION.LINK.resync | C |  |  |
| 3 | 2.1.3 | A2A.SOA.VAL.MISC.ACTION.LINK.ASSOCSP.resync | C |  |  |
| 5 | 2.1.5 | A2A.LSMS.VAL.MISC.ACTION.LINK.resync | C |  |  |
| A2A NANC 218 |
| 2 | 2.2.2 | A2A.NSOA.VAL.CREATE.CONFLICT.SubscriptionVersion | C |  |  |
| 3 | 2.2.3 | A2A.OSOA.VAL.CREATE.CONFLICT.SubscriptionVersion | C |  |  |
| 4 | 2.2.4 | A2A.NSOA.INV.CANCEL.CONFLICT.SubscriptionVersion | C |  |  |
| 5 | 2.2.5 | A2A.OSOA.INV.CANCEL.CONFLICT.SubscriptionVersion | C |  |  |
| 6 | 2.2.6 | A2A.OSOA.VAL.MODIFY.PEND.subscriptionVersion |  |  |  |
| A2A NANC 230 |
| 1 | 2.3.1 | A2A.DSOA.VAL.PORT-TO-ORIG.PTOLISP.SubscriptionVersion | C |  |  |
| 2 | 2.3.2 | A2A.SOA.VAL.PORT-TO-ORIG.ASSOCSP.PTOLISP.SubscriptionVersion | C |  |  |
| A2A NANC 249 |
| 1 | 2.4.1 | A2A.SOA.VAL.MODIFY.DISCONPEND.SubscriptionVersion | C |  |  |
| 2 | 2.4.2 | A2A.SOA.INV.MODIFY.DISCONPEND.SubscriptionVersion | C |  |  |
| 3 | 2.4.3 | A2A.SOA.VAL.MODIFY.TN-RANGE.DISCONPEND.SubscriptionVersion | C |  |  |
| 4 | 2.4.4 | A2A.SOA.INV.MODIFY.TN-RANGE.DISCONPEND.SubscriptionVersion | C |  |  |
| 5 | 2.4.5 | A2A.SOA.VAL.MODIFY.ASSOCSP.DISCONPEND.SubscriptionVersion | C |  |  |
| 6 | 2.4.6 | A2A.SOA.INV.MODIFY.ASSOCSP.DISCONPEND.SubscriptionVersion |  |  |  |
| LARGE, SINGLE PDU RECOVERY, SOA, OCN |
| 1 | 3.1.1 | A2A.SOA.VAL.MISC.ACTION.resync_500_ocn | C |  |  |
| 2 | 3.1.2 | A2A.SOA.VAL.MISC.ACTION.resync_1000_ocn | C |  |  |
| 3 | 3.1.3 | A2A.SOA.VAL.MISC.ACTION.resync_2000_ocn | C |  |  |
| LARGE, SINGLE PDU RECOVERY, SOA, SAVC |
| 1 | 3.2.1 | A2A.SOA.VAL.MISC.ACTION.resync_1failed_500_savc | C |  |  |
| 2 | 3.2.2 | A2A.SOA.VAL.MISC.ACTION.resync_1failed_1000_savc | C |  |  |
| 3 | 3.2.3 | A2A.SOA.VAL.MISC.ACTION.resync_1failed_2000_savc | C |  |  |
| 4 | 3.2.4 | A2A.SOA.VAL.MISC.ACTION.resync_20failed_500_savc | C |  |  |
| 5 | 3.2.5 | A2A.SOA.VAL.MISC.ACTION.resync_20failed_1000_savc | C |  |  |
| 6 | 3.2.6 | A2A.SOA.VAL.MISC.ACTION.resync_20failed_2000_savc | C |  |  |
| LARGE, SINGLE PDU RECOVERY, LSMS, FIRST USAGE |
| 1 | 3.3.1 | A2A.LSMS.VAL.MISC.ACTION.resync_500_firstusage | C |  |  |
| 2 | 3.3.2 | A2A.LSMS.VAL.MISC.ACTION.resync_1000_firstusage | C |  |  |
| 3 | 3.3.3 | A2A.LSMS.VAL.MISC.ACTION.resync_2000_firstusage | C |  |  |
| LARGE, SINGLE PDU RECOVERY, LSMS, SV CREATE |
| 1 | 3.4.1 | A2A.LSMS.VAL.MISC.ACTION.resync_500_sv | C |  |  |
| 2 | 3.4.2 | A2A.LSMS.VAL.MISC.ACTION.resync_1000_sv | C |  |  |
| 3 | 3.4.3 | A2A.LSMS.VAL.MISC.ACTION.resync_2000_sv | C |  |  |
| 4 | 3.4.4 | A2A.LSMS.VAL.MISC.ACTION.resync_5000_sv | C |  |  |
| 5 | 3.4.5 | A2A.LSMS.VAL.MISC.ACTION.resync_10000_sv | C |  |  |