NPAC SMS Release 3.3.4.1

Turn Up Test Plan

Release 3.3.4.1a

July 30, 2010

Publication History

| Version | Release Date | Description |
| --- | --- | --- |
| 3.3.4.1a | July 30, 2010 | Initial draft of NPAC Release 3.3.4.1 Test Cases. This represents a new release testing document. |

Table of Contents

1.	Preface	4

1.1	Purpose of this Document	4

1.2	Assumptions	4

1.3	Audience	4

1.4	Conventions Used in this Document	5

1.4.1.	Test Case Template	5

1.4.2.	Test Case Numbering	6

1.4.3.	Test Case Priority	6

1.4.4.	Test Case Prerequisites	7

1.4.5.	Test Case Steps and Expected Results	7

1.4.6.	Pass/Fail Analysis	7

1.5	Related Documents	7

1.6	Document Structure	7

1.7	Requirements for Turn-Up Testing	8

1.8	Turn-Up Testing Execution Considerations	9

1.8.1	Pseudo-LRN:	9

2.	RSMS 3.3.4.1 Turn Up Test Cases	10

NANC 442 – Pseudo-LRN	10

3.	Regression Testing Considerations	17

Appendix A: Test Case Matrix	19

Appendix B: Test Plan Issues	21

# Preface

## Purpose of this Document

The purpose of this document is to identify the NPAC Release 3.3.4.1 Test Cases.  These Test Cases are based on NPAC SMS Release 3.3.4.1 (and all respective point release) requirements.

Actual Entrance and Exit criteria for test execution/completion are an agreement between individual Service Providers and the NPAC SMS vendor based upon the functionality supported by the local Service Provider SOA and/or LSMS systems.

This Test Plan contains Test Cases per functional component of the Software Release.  The Test Cases cover basic Success scenarios.  Test Case Priority is indicated by the systems that participate in each respective Test Case.  It is assumed that the NPAC SMS/NPAC personnel participate in every Test Case of the Turn Up Test Plan.  If the Test Case Priority for a system is marked as Required that system shall participate as the Test Case describes.  A Test Case Priority of Conditional for a system means that the system shall participate in the Test Case as described, if the respective functionality has been implemented for that system.  When the Test Case Priority is marked as Optional for a system, it is at the discretion of the Service Provider if they use the respective system to participate in the Test Case as described.  Finally, the Test Case Priority may be marked as N/A for a Service Provider system, which means that the functionality tested in this Test Case does not apply to this respective Service Provider system.

The different NPAC regions will turn-up Point Release 3.3.4.1 software at different times.  As a result Service Providers that operate in multiple regions will need to handle Release 3.3.4 and Release 3.3.4.1 interfaces (and respective data) simultaneously.  This test plan does not include any guidelines or test cases for the purpose of testing backward compatibility between NPAC SMS releases.

## Assumptions

All Test Cases should be executed where the Service Provider profile attributes are set such that they emulate the Service Provider’s production environment unless otherwise stated in an individual test case.

Please refer to the NPAC/SMS User Profile – U.S. Mechanized User Readiness Form and NPAC/SMS User Profile – Canadian Mechanized User Readiness Form for the complete list of SOA and LSMS Service Provider Configurables.

## Audience

The intended audience for this document is NPAC SMS, SOA and LSMS system testers and anyone who is involved with NPAC SMS, SOA and LSMS testing.  It is assumed that individuals using this test plan have an understanding of Local Number Portability, Number Pooling and related specification documents.  The Test Cases are written from the Interface Interoperability Specification (IIS) perspective so users should have an understanding of this document specifically.

## Conventions Used in this Document

### Test Case Template

Test Cases are the bulk of the information presented in this document.  Test Cases are comprised of the following information:

| A. | TEST IDENTITY |  |
| --- | --- | --- |
|  | Test Case Number: | Unique Test Case Identifier | SUT Priority: | SOA | Required –This Service Provider systems shall participate. Conditional – If the Service Provider system has implemented the functionality represented in this Test Case, then the system shall participate. Optional – Service Provider may include this system as indicated by the Test Case. N/A – This Test Case does not apply to this system. |
|  |  |  |  | LSMS | Required, Conditional, Optional or N/A. |
|  | Objective: | Test Case Objective. The Title specifies relevant systems to the test (NPAC SMS, SOA or LSMS) and the type of Test Case (success or error). |
| B. | REFERENCES |  |
|  | NANC Change Order Revision Number: | If a change order revision is relevant – it’s indicated here. | Change Order Number(s): | If a Change Order(s) is relevant – it is indicated here. |
|  | NANC FRS Version Number: | FRS version is indicated here. | Relevant Requirement(s): | Requirement(s) related to this Test Case are indicated here. |
|  | NANC IIS Version Number: | IIS version is indicated here. | Relevant Flow(s): | IIS Flow(s) related to this Test Case are indicated here. |
| C. | PREREQUISITE |  |
|  | Prerequisite Test Cases: | Test Case, if any, to be successfully executed prior to this Test Case |
|  | Prerequisite NPAC Setup: | Steps to be executed by NPAC personnel prior to Test Case execution |
|  | Prerequisite SP Setup: | Steps to be executed by Service Provider personnel prior to Test Case execution |
| D. | TEST STEPS and EXPECTED RESULTS |
| Row # | NPAC or SP | Test Step | NPAC or SP | Expected Result |
| 1. | [system indicated here] | This test step is described here. | [system indicated here] | The expected results associated with this respective test step are indicated here. |
| E. | Pass/Fail Analysis, TC # |
| Pass | Fail | NPAC personnel performed the test case as written. |
| Pass | Fail | Service Provider personnel performed the test case as written. |

### Test Case Numbering

Test Case Numbers are alphanumeric numbers that identify the sections of functional component based on the respective Change Order to ensure a unique Test Case number.  Below is a table identifying the Change Orders that are included in this release and their associated alphanumeric numbering prefix.  These test case numbers are assumed to be static:

| Numeric Prefix | Respective Functional Component |
| --- | --- |
| NANC 442 | Pseudo-LRN |

### Test Case Priority

Each Test Case will have an associated Test Case Priority.

Required: This Test Case represents required functionality and shall be executed by the respective Service Provider system and/or NPAC SMS Vendor.

Conditional: This Test Case represents optional functionality.  If a Service Provider has implemented the suggested functionality for this respective Service Provider system in the Test Case, they shall execute the Test Case as written.  If there are not any Service Providers that have implemented the functionality, and therefore cannot verify the NPAC SMS behavior, the NPAC personnel shall execute the Test Case with the use of simulators.

Optional: Service Provider may execute the Test Case as written if they have implemented the suggested functionality for this respective system.  Typically ‘optional’ Test Cases verify ‘additional’ attributes of a requirement.

N/A: This Test Case does not apply to this Service Provider system.  Thus the Service Provider does not need to test this respective system during this Test Case.

### Test Case Prerequisites

Each Test Case contains a section for Prerequisites including Prerequisite Test Cases and/or Prerequisite NPAC Setup and/or Prerequisite SP Setup.  When Prerequisite Test Cases are identified this is simply referencing a Test Case that, when appropriately executed, will setup the proper scenario for executing that respective Test Case.  Prerequisite Test Cases are not a good source for Test Case ordering to ensure efficient execution.  Ordering of Test Cases for efficient execution should be reviewed on a Service Provider by Service Provider basis, based on their specific suite of Test Cases for exiting Turn Up Test.

### Test Case Steps and Expected Results

Test Case steps and Expected results have fields to indicate the respective systems, test steps and their expected results.

### Pass/Fail Analysis

Each Test Case contains a general analysis of either Pass or Fail.

## Related Documents

North American Number Council (NANC) Functional Requirements Specification Number Portability Administration Center (NPAC) Service Management System (SMS), Release 3.3.4c

NPAC SMS Interoperable Specifications NANC Version 3.3.4b

## Document Structure

This document is organized into sections as defined below:

|  | Preface (1) | This section describes the purpose and structure of this document |
| --- | --- | --- |
|  | RSMS 3.3.4.1 Turn Up Test Cases (Section 2) | NANC 442: Pseudo-LRN Test Cases |
|  | Additional/Optional Regression (Section 3) | A subset of regression test scenarios service providers may optionally perform using specific service provider profile settings for the “other” service provider party to the testing scenario which demonstrate backward compatibility when using the core functions of the application. *This is not the regression phase of Turn Up Test, only additional, optional testing. |
|  | Appendix A | Test Case Matrix including a List of Objectives and Results Table |
|  | Appendix B | Issues [indicate open/date and closed/date] |

## Requirements for Turn-Up Testing

Turn-Up Testing, which includes new NPAC SMS software release functionality testing and regression testing, must be performed on a Service Provider’s SOA/LSMS software anytime that a change is made to the interface (GDMO or ASN.1) of the NPAC  SMS.  In the event that the interface change is initiated by the NPAC SMS, the Users shall perform Turn-Up Testing on each version of SOA/LSMS software that may potentially be used with the new NPAC SMS interface.

If any of the following scenarios apply, Turn-Up Testing is required by Users.  The following outlines the required level of testing for specific scenarios (as defined in the current version of SOW 24, Continuing Certification Testing.  If updates are made to SOW 24, those updates take precedence over the scenarios defined below):

    - When the operating system software of a local product (i.e., a SOA or LSMS that connects to the NPAC SMS) is upgraded, and this results in any OSI stack or CMIP toolkit change, then ITP testing is required [standard regression test cases].

    - When the operating system of a local product (i.e., a SOA or LSMS that connects to the NPAC SMS) is changed (e.g. OS vendor A to OS vendor B), then ITP testing is required [standard regression test cases].

(c) When a local product (SOA/LSMS) is compiled with the current interface model, and a new local feature (SOA/LSMS feature) is implemented that does NOT involve a change in the use of the interface model, and the NPAC SMS is compiled with the current model, then Turn-Up Testing is optional.  Test cases to be performed are at the discretion of the Service Provider. [standard regression test cases].

(d) When a local product is compiled with the current interface model, and no new local features are implemented that involve the interface, and the NPAC SMS is compiled with the new interface model, then Turn-Up Testing is required [standard regression test cases].

(e) When a local product is compiled with the new interface model, and no new local features are implemented that involve the interface, and the NPAC SMS is compiled with the new interface model, then Turn-Up Testing is required [standard regression test cases].

(f) When a local product is compiled with the new interface model, and new local features are implemented that involve the interface, and the NPAC SMS is compiled with the new interface model, then Turn-Up Testing is required [standard regression test cases and new functionality test cases].

(g) When a local product is compiled with the current interface model, and new local features are implemented that involve the interface, and the NPAC SMS is compiled with the current model, then Turn-Up Testing is required [standard regression test cases and new functionality test cases].

## Turn-Up Testing Execution Considerations

### 1.8.1	Pseudo-LRN:

A Pseudo-LRN (PLRN) is not a new attribute but is an LRN value of 000-000-0000.  This value can only be specified on subscription versions and number pool blocks when the region and the respective New/Block Holder Service Provider supports PLRN.  Service providers that support PLRN can configure a list of SPIDs for which they wish to receive PLRN downloads/notifications and as such, NPAC will only download or provide notifications based on this SPID List.  BDD files will also contain data based on whether the requesting service provider supports this functionality and when they do, their accepted SPID List.

# RSMS 3.3.4.1 Turn Up Test Cases

### NANC 442 – Pseudo-LRN

This change order enables a Pseudo-LRN (PLRN) value (000-000-0000) to be specified in Intra-SP subscription versions for TNs that have never been ported and number pool blocks where the Code Holder is the Block Holder and the TNs have never been ported - when the region and the New/Block Holder service provider support PLRN.

The following (existing) test case is enhanced specifically for the NANC 442 features of the rsms 3.3.4.1 release and should be executed as part of “new release” testing.

| A. | TEST IDENTITY |  |
| --- | --- | --- |
|  | Test Case Number: | NANC 348-1 | SUT Priority: | SOA | Optional |
|  |  |  |  | LSMS | N/A |
|  | Objective: | SOA - NPAC personnel create a Bulk Data Download file for SOA notification data specifying a service provider ID and time range. Verification steps are performed to ensure the BDD file was processed successfully by the service provider system. – Success |
| B. | REFERENCES |  |
|  | NANC Change Order Revision Number: |  | Change Order Number(s): | NANC 348 |
|  | NANC FRS Version Number: |  | Relevant Requirement(s): | RR3-220, RR3-462, RR3-463, RR3-464, RR3-465, RR3-466, RR3-467, RR3-468, RR3-469 |
|  | NANC IIS Version Number: |  | Relevant Flow(s): | N/A |
| C. | PREREQUISITE |  |
|  | Prerequisite Test Cases: |  |
|  | Prerequisite NPAC Setup: | Work with the Service Provider under test to create porting scenarios that result in a subset of the following notifications: subscriptionVersionCancellationAcknowledgeRequest subscriptionVersionRangeCancellationAcknowledgeRequest subscriptionVersionDonorSP-CustomerDisconnectDate subscriptionVersionRangeDonorSP-CustomerDisconnectDate subscriptionVersionNewSP-CreateRequest subscriptionVersionRangeNewSP-CreateRequest subscriptionVersionOldSP-ConcurrenceRequest subscriptionVersionRangeOldSP-ConcurrenceRequest subscriptionVersionStatusAttributeValueChange subscriptionVersionRangeStatusAttributeValueChange subscriptionVersionNPAC-ObjectCreation (*including Medium Timer indicator and at least one notification with a PLRN value if supported by the Service Provider under test) subscriptionVersionRangeNPAC-ObjectCreation (*including Medium Timer indicator and at least one notification with a PLRN value if supported by the Service Provider under test) subscriptionVersionNPAC-attributeValueChange (*including Medium Timer indicator if supported by the Service Provider under test) subscriptionVersionRangeAttributeValueChange (*including Medium Timer indicator if supported by the Service Provider under test) subscriptionVersionNewSP-FinalCreateWindowExpiration subscriptionVersionRangeNewSP-FinalCreateWindowExpiration subscriptionAudit-DiscrepancyRpt subscriptionAuditResults subscriptionAudit-objectCreation subscription Audit-objectDeletion lnpNPAC-SMS-Operational-Information subscriptionVersionNewNPA-NXX subscriptionVersionOldSPFinalConcurrenceWindowExpiration subscriptionVersionRangeOldSPFinalConcurrenceWindowExpiration numberPoolBlock-objectCreation (*including at least one numberPoolBlock-objectCreation with a PLRN value if supported by the service provider under test.) numberPoolBlock-attributeValueChange numberPoolBlockStatusAttributeValueChange Note: In the objectCreation notifications within a notification BDD file: Medium Timer indicator, Timer Type and Business Hours are included uniquely (either a value or an empty placeholder when applicable) when the respective Service Provider configurable for each unique attribute is set to TRUE. Additionally, the Region supports tunable for the Medium Timer indicator must also be set to TRUE for the Medium Timer indicator to be included. These conditions must be true both at the time the notification was generated and at the time the BDD is created. If, for example the Service Provider supports only Medium Timers and Timer Type, and the Region Supports Medium Timers indicator both at the time the notification was originally generated and at the time the BDD was created, then the BDD will contain Medium Timer Indicator and Timer Type, but not Business Hours. In the attributeValueChange notifications within a notification BDD file: Timer Type is included when the Service Provider under test supports both the Timer Type and Medium Timer Indicators and the Region supports the Medium Timer indicator. The Business Hours attribute is included when the Service Provider under test supports Medium Timers and Business Hours and the Region supports Medium Timer indicator. Medium Timer indicator is included when the Service Provider supports Medium Timers and the Region supports the Medium Timer indicator. Like in the objectCreation notification scenario, the Service Provider configurables and Region supports tunable must be set in these combinations at the time the notification was originally generated as well as at the time the BDD is requested for the attributes to be included in the AVC notification within the BDD. |
|  | Prerequisite SP Setup: | Verify all Service Provider configurable settings reflect production values prior to performing functions to generate notifications for the BDD. |
| D. | TEST STEPS and EXPECTED RESULTS |
| Row # | NPAC or SP | Test Step | NPAC or SP | Expected Result |
| 1. | NPAC | NPAC personnel request a Bulk Data Download for Notification Data, specifying the Service Provider under test and a Time Range equal to the prerequisite activities. | NPAC | 1. The NPAC SMS receives the request from the NPAC OP GUI. 2. The NPAC SMS generates the Bulk Data Download File. NOTE: The BDD file will contain data (MTI, Timer Type, Business Hours, PLRN records, etc.) based on the requesting service provider profile settings. If a service provider does not support PLRN for example, their BDD file will not contain any object-Creation notifications for PLRN records. |
| 2. | SP | Service Provider personnel FTP the Bulk Data Download File and load the file into their SOA. | SP | Service Provider personnel successfully process the BDD file. |
| 3. optional | SP | Service Provider personnel, using their SOA, perform a local query for the Notification Data to verify that the Notification data was loaded. | SP | The Notification data was loaded. |
| E. | Pass/Fail Analysis, NANC 348-1 |
| Pass | Fail | NPAC personnel performed the test case as written. |
| Pass | Fail | Service Provider personnel performed the test case as written. |

| A. | TEST IDENTITY |  |
| --- | --- | --- |
|  | Test Case Number: | NANC 442-1 | SUT Priority: | SOA | N/A |
|  |  |  |  | LSMS | Conditional |
|  | Objective: | NPAC OP GUI – NPAC Personnel initiate a Bulk Data Download of Subscription Data – Specifying Active/Disconnect Pending/Partial Failure Subscription Versions Only and NOT specifying a TN range that includes PLRN records. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system - Success |
| B. | REFERENCES |  |
|  | NANC Change Order Revision Number: |  | Change Order Number(s): | NANC 442 |
|  | NANC FRS Version Number: |  | Relevant Requirement(s): | RR3-320, RR3-312, RR3-313, RR3-314, RR3-319, RR3-323 |
|  | NANC IIS Version Number: |  | Relevant Flow(s): | N/A |
| C. | PREREQUISITE |  |
|  | Prerequisite Test Cases: |  |
|  | Prerequisite NPAC Setup: | For the Service Provider under test, verify their LSMS Supports PLRN Indicator is set to TRUE and their PLRN Accepted SPID List does not include the New Service Provider ID you are going to use in Prerequisite A, but does include the SPIDs your are using in the rest of the prerequisites for this test case. While the LSMS is ‘dis-associated’ from the NPAC SMS, NPAC personnel perform the following functions: a) Create and Activate 100 Intra-Service Provider Subscription Versions using an NPA-NXX that is open for porting, and for which the Service Provider under test is accepting downloads for this NPA-NXX. Also specify a PLRN value for the range of SVs. This Service Provider is neither the Old nor New Service Provider for these Subscription Versions. The New Service Provider for the ports is NOT included on the Accepted SPID List for PLRN records for the SUT. Use simulators that are associated with the NPAC and are receiving downloads for this NPA-NXX. Verify that the Subscription Versions have a status of ‘Active’. (SV group a ___________________) b) Create and Activate 100 Intra-Service Provider Subscription Versions using an NPA-NXX that is open for porting, and for which the Service Provider under test is accepting downloads for this NPA-NXX. Also specify a PLRN value for the range of SVs. This Service Provider is neither the Old nor New Service Provider for these Subscription Versions. The New Service Provider for the ports IS included on the Accepted SPID List for PLRN records for the SUT. Use simulators that are associated with the NPAC and are receiving downloads for this NPA-NXX. Verify that the Subscription Versions have a status of ‘Active’. (SV group b ___________________) c) Activate 50 Subscription Versions with a status of ‘Pending’ and a PLRN value. The Service Provider under test is the New Service Provider for these Subscription Versions and the Code Holder for this NPA-NXX. Use simulators that are associated with the NPAC and are receiving downloads for this NPA-NXX. Verify that these Subscription Versions have a status of ‘Active’. (SV group c_________________) d) Activate a Number Pool Block using a PLRN value on behalf of the Service Provider under test. This Service Provider is the Code Holder for this NPA-NXX. Use simulators that are associated with the NPAC and are receiving downloads for this NPA-NXX. Verify that the Pooled Subscription Versions have a status of ‘Active’. (SV group d_____________________) (NPB d______________) |
|  | Prerequisite SP Setup: |  |
| D. | TEST STEPS and EXPECTED RESULTS |
| Row # | NPAC or SP | Test Step | NPAC or SP | Expected Result |
| 1. | NPAC | Using the NPAC OP GUI, NPAC Personnel request a Bulk Data Download for Subscription Data, specifying Active/Disconnect Pending/Partial Failure Subscription Versions Only and NOT specifying a TN range, for the Service Provider under test. | NPAC | The NPAC SMS performs the request, generates the appropriate Bulk Data Download File(s) and automatically “FTP’s” the file(s) to the Service Provider’s directory on the NPAC SMS. |
| 2. | SP | Service Provider Personnel receive the Bulk Data Download File(s) and load the file into their LSMS. | SP | The LSMS successfully processes the Bulk Data Download file(s) and reflects the updates described in the prerequisites above. The systems are still ‘dis-associated’ from the NPAC SMS. |
| 3. | SP | Service Provider Personnel, using their LSMS, perform a local query for the Subscription Data to verify that the Subscription Version data and Number Pool Block data (if supported) was loaded. SV group b SV group c For non EDR LSMS, SV group d For EDR LSMS, SV group d was not loaded | SP | Using the LSMS system, verify: SV group b exists on the LSMS. SV group c exists on the LSMS. For non EDR LSMS, SV group d exists on the LSMS. For EDR LSMS, SV group d DOES NOT exist on the LSMS but NPB d does exist. |
| 4. | NPAC | NPAC Personnel perform multiple, Full audits for each NPA-NXX included in the range of TNs specified in the prerequisites above for the Service Provider’s LSMS to verify that all the appropriate updates were processed from the Bulk Data Download File by the LSMS. | NPAC | Using the Audit Results Log, verify that there were no updates made. If any updates were made as a result of running this audit, this test case fails. Verify that: SV group b exists on the LSMS. SV group c exists on the LSMS. For non-EDR LSMS, SV group d exists on the LSMS. For EDR LSMS, SV group d DOES NOT exist on the LSMS. |
| E. | Pass/Fail Analysis, NANC 442-1 |
| Pass | Fail | NPAC Personnel performed the test case as written. |
| Pass | Fail | Service Provider Personnel performed the test case as written. |
| Pass | Fail | Service Provider Personnel were able to successfully process the Bulk Data Download file updates with their local databases in a timely fashion. |

For RSMS3.3.4.1 testing perform the following test case but rather than specifying a valid LRN owned by the New Service Provider, specify a PLRN value.  All other test case prerequisites and steps remain unchanged.

| 8.1.2.1.1.17 Create 1st time intra-service provider ‘pending’ port of a TN Range via the SOA Mechanized Interface. – Success |
| --- |
| Purpose: | Create an intra-service provider ‘pending’ port consisting of a TN Range and mandatory/Optional Data elements via the SOA Mechanized Interface. |
| Requirements: | RR5-6.1, RR5-4 |
| Prerequisites: | The NPA-NXX of the TN Range is owned by the New Service Provider. The TN Range involves the first ported TN for the NPA-NXX. The LRN is a valid LRN value for a switch owned by the New Service Provider. The new SP due date is greater than or equal to the NPA-NXX Live Timestamp and is set to a future date. NOTE: If the region and the SUT support PLRN, this range of TNs may be created specifying a PLRN value. |
| Expected Results: | A subscription version with a status of ‘pending’ is created on the NPAC SMS for each TN in the TN Range. The NPAC SMS issues a successful action reply to the New Service Provider’s SOA (originating SOA). The successful action reply is received by the New Service Provider’s SOA. The NPAC SMS issues an objectCreation notification for each TN in the TN Range containing : subscriptionVersionID subscriptionTN subscriptionOldSP subscriptionNewCurrentSP subscriptionNewSP-CreationTimeStamp subscriptionVersionStatus subscriptionNewSP-DueDate subscriptionTimerType – if supported by the Service Provider SOA subscriptionBusinessType – if supported by the Service Provider SOA The New Service Provider’s SOA receives each objectCreation notification and issues a confirmed reply to the NPAC SMS. The New NPA-NXX notification is sent to all SOAs and LSMSs. |
| Actual Results: |  |

# Regression Testing Considerations

For Service Provider’s that support Pseudo-LRN perform the following Regression Test Cases in consideration of these notes.

| 8.1.2.1.1.16 Create 1st time intra-service provider ‘pending’ port of a single TN via the SOA Mechanized Interface. – Success |
| --- |
| Purpose: | Create an intra-service provider ‘pending’ port consisting of a single TN and all mandatory data elements via the SOA Mechanized Interface. |

Specify a PLRN value.

| 8.1.2.4.1.10 Activate intra-service provider ‘pending’ port of a single TN that has been previously ported. – Success |
| --- |
| Purpose: | Activate an intra-service provider ‘pending’ port consisting of a single TN via the SOA Mechanized Interface. All valid LSMSs are successful. |

Activate a pending, intra-service provider port that has never been ported before where the Code Holder is the same as the New Service Provider and a PLRN value is specified in the pending port.

| 8.1.2.4.1.13 Activate intra-service provider ‘pending’ port of a range of TNs that has been previously ported. – Success |
| --- |
| Purpose: | Activate an intra-service provider ‘pending’ port consisting of a range of TNs via the SOA Mechanized Interface. For all TNs, all LSMSs are successful. |

Activate a range of pending, intra-service provider ports that have never been ported before where the Code Holder is the same as the New Service Provider and a PLRN value is specified in the pending ports.

| A. | TEST IDENTITY |  |
| --- | --- | --- |
|  | Test Case Number: | 3.1.1 | SUT Priority: | SOA LTI | N/A |
|  |  |  |  | SOA | C |
|  |  |  |  | non-EDR LSMS | C |
|  |  |  |  | EDR LSMS | C |
|  | Objective: | NPAC OP GUI - NPAC Personnel create NPA-NXX-X Information, where the Block Holder SPID is the same as the Code Holder SPID and the NPAC SMS schedules the Number Pool Block create, and the NPAC SMS activates upon scheduled date and time.- Success |
|  | Specify a PLRN value. |  |

| A. | TEST IDENTITY |  |
| --- | --- | --- |
|  | Test Case Number: | 4.1.1 | SUT Priority: | SOA LTI | N/A |
|  |  |  |  | SOA | C |
|  |  |  |  | non-EDR LSMS | R |
|  |  |  |  | EDR LSMS | R |
|  | Objective: | SOA - Service Provider Personnel create a non-contaminated Number Pool Block – Success |

Specify a PLRN value.

# Appendix A: Test Case Matrix

| NANC 442: Pseudo-LRN |
| --- |
| Test Case Priority | Test Case # | Test Case Description | Req. | IIS Flow | Test Results/Issues/Comments |
| SOA - Optional | 348-1 | SOA - NPAC personnel create a Bulk Data Download file for SOA notification data specifying a service provider ID and time range. Verification steps are performed to ensure the BDD file was processed successfully by the service provider system. – Success | RR3-220, RR3-462, RR3-463, RR3-464, RR3-465, RR3-466, RR3-467, RR3-468, RR3-469 | N/A |  |
| LSMS – N/A |  |  |  |  |  |
| SOA – N/A | 442-1 | NPAC OP GUI – NPAC Personnel initiate a Bulk Data Download of Subscription Data – Specifying Active/Disconnect Pending/Partial Failure Subscription Versions Only and NOT specifying a TN range that includes PLRN records. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system - Success | RR3-320, RR3-312, RR3-313, RR3-314, RR3-319, RR3-323 | N/A |  |
| LSMS – Conditional |  |  |  |  |  |
| SOA - Required | 8.1.2.1.1.17 | Create 1st time intra-service provider ‘pending’ port of a TN Range via the SOA Mechanized Interface. – Success |  | N/A |  |
| LSMS – N/A |  |  |  |  |  |
| Regression Testing Considerations |
| Test Case Priority | Test Case # | Test Case Description | Req. | IIS Flows | Test Results/Issues/Comments |
| SOA – Required | 8.1.2.1.1.16 | Create 1st time intra-service provider ‘pending’ port of a single TN via the SOA Mechanized Interface. – Success Specify a PLRN value in the SV create. | RR5-6.1, RR5-4 |  |  |
| LSMS – N/A |  |  |  |  |  |
| SOA – Required | 8.1.2.4.1.10 | Activate intra-service provider ‘pending’ port of a single TN that has been previously ported. – Success Activate a pending, intra-service provider port that has never been ported before where the Code Holder is the same as the New Service Provider and a PLRN value is specified in the pending port. |  |  |  |
| LSMS – N/A |  |  |  |  |  |
| SOA – Required | 8.1.2.4.1.13 | Activate intra-service provider ‘pending’ port of a range of TNs that has been previously ported. – Success Activate a range of pending, intra-service provider ports that have never been ported before where the Code Holder is the same as the New Service Provider and a PLRN value is specified in the pending ports. |  |  |  |
| LSMS – N/A |  |  |  |  |  |
| SOA – Conditional | 3.1.1 | NPAC OP GUI - NPAC Personnel create NPA-NXX-X Information, where the Block Holder SPID is the same as the Code Holder SPID and the NPAC SMS schedules the Number Pool Block create, and the NPAC SMS activates upon scheduled date and time.- Success Specify a PLRN value. | RR3-61, RR3-63, RR3-64, RR3-65, RR3-66, RR3-67.1, RR67.2, RR3-68, RR3-69, RR3-70, RR3-71, RR3-72, RR3-73, RR3-75.1, RR3-75.3, RR3-76.1, RR3-76.2, RR3-78, RR3-79.1, RR3-79.2, RR3-84, RR3-85, RR3-92, RR3-93, RR3-94, RR3-119, RR3-120, RR3-121, RR3-122, RR3-123, RR3-128, RR3-129, RR3-130, RR3-149, RR3-151, RR5-85, RR5-86, RR5-87, RR3-477 | 1.1 Service Provider NPA-NXX-X Create by NPAC SMS 2.2 Number Pool Block Create by NPAC SMS 2.3 Number Pool Block Create Broadcast: Successful 2.3.1 Number Pool block Create Broadcast Successful to Local SMS 2.3.2 Number Pool Block Create: Successful Broadcast |  |
| LSMS – Conditional |  |  |  |  |  |
| SOA – Conditional | 4.1.1 | SOA - Service Provider Personnel create a non-contaminated Number Pool Block – Success Specify a PLRN value. | RR3-124, RR3-125, RR3-126, RR3-130, RR3-132, RR3-144, RR3-146, RR3-150, RR3-151, RR3-152, RR3-143, RR3-180, RR5-85, RR5-86, RR5-87, RR5-89 | 2.1 Number Pool Block Create by SOA 2.3.1 Number Pool Block Create Broadcast to Local SMS 2.3.2 Number Pool Block Create: Successful Broadcast |  |
| LSMS – Required |  |  |  |  |  |

# Appendix B: Test Plan Issues

Following are issues related to the NPAC Release 3.3.4.1 Test Plan:

| # | Date | Issue | Status |
| --- | --- | --- | --- |
| 1. |  |  |  |