| Test Case # | Test Case Description | Req. | IIS Flow | Comments/Issues |
| --- | --- | --- | --- | --- |
| 1. NANC 169 – Delta Download File Creation by Time Range for SVs |
| NANC 169-1 | NPAC OP GUI – NPAC Personnel Initiate a Bulk Data Download of Subscription Data – Specifying Active/Disconnect Pending/Partial Failure Subscription Versions Only and NOT specifying a TN range. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system. – Success | 169-1 : 4, 169-9 |  |  |
| NANC 169-2 | NPAC OP GUI – NPAC Personnel Initiate a Bulk Data Download of Subscription Data – Specifying Active/Disconnect Pending/Partial Failure Subscription Versions Only and specifying a TN range of at least 1000 TNs. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system – Success | 169-8, 169-9, 169-13 |  | Be sure to include POOLED SVs in the Range |
| NANC 169-3 | NPAC OP GUI – NPAC Personnel Initiate a Bulk Data Download of Subscription Data – Specifying Latest View of Subscription Version Activity, a valid Time Range, and NOT specifying a TN range. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system – Success | 169-5 :7, 169-9 |  |  |
| NANC 169-4 | NPAC OP GUI – NPAC Personnel Initiate a Bulk Data Download of Subscription Data – Specifying Latest View of Subscription Version Activity, a valid Time Range, and a TN range of at least 1000 TNs. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system – Success | 169-9 : 12 |  | Make sure there is an appropriate NPA-NXX filter set |
| 2. NANC 187 - Linked Action Replies |
| NANC 187 –1 | LSMS – Service Provider Personnel for either an EDR or non-EDR LSMS submit a resynchronization request for Network Data, Block Data, SV Data and Notification Data by time range, over the LSMS to NPAC SMS Interface, with the Service Provider’s Local SMS Linked Replies Indicator set to their production setting. The recovery response includes a number of Network Data objects, Number Pool Block objects, Notifications and Subscription Versions less than or equal to their respective Linked Replies Blocking Factors. – Success | 187-16, 187-20, 187-25RR6-105 | B.7.1.1, B.7.1.2 | In Prerequisites, need to have ND, Blocks, SVs and Notifications based on Blocking factors. |
| NANC 187-2 | LSMS - Service Provider Personnel for either an EDR or non-EDR LSMS submit a resynchronization request for Network Data, and SV Data by time range, over the LSMS to NPAC SMS Interface, with the Service Provider’s Local SMS Linked Replies Indicator set to their production setting. The recovery response includes a number of Subscription Versions greater than the Subscription Data Linked Replies Blocking Factor and less than the Subscription Data Maximum Linked Recovered Objects as well as a number of Network Data updates greater than the Network Data Linked Replies Blocking Factor and less than the Network Data Maximum Linked Recovered Objects. – Success | 187-9, 187-10, 187-16, 187-20, 187-25, 187-30, 187-34, 187-39 | B.7.1.1, B.7.1.2 | Need to have ND based on ND Blocking factor. |
| NANC 187-3 | LSMS - Service Provider Personnel for either an EDR or non-EDR LSMS submit a resynchronization request for Network Data, Number Pool Block data and SV Data by time range, over the LSMS to NPAC SMS Interface, with the Service Provider’s Local SMS Linked Replies Indicator set to their production setting. The recovery response includes a number of Network Data objects, Number Pool Block objects and Subscription Versions greater than the respective Maximum Linked Recovered Objects parameters. – Failure | 187-30, 187-34, 187-39 | B.7.1.1, B.7.1.2 | Need to have ND SVs and NPBs based on Max Linked Recovered Objects. |
| NANC 187-4 | SOA - - Service Provider Personnel submit a resynchronization request for Network Data and Notification Data by time range, over the SOA to NPAC SMS Interface, with the Service Provider’s SOA Linked Replies Indicator set to their production setting. The recovery response includes a number of Network Data updates less than or equal to the Network Data Linked Replies Blocking Factor and a number of Notifications less than or equal to the Notification Data Linked Replies Blocking Factor. – Success | 187-15, 187-24 | B.7.2 |  |
| NANC 187-5 | SOA - Service Provider Personnel submit a resynchronization request for Notification Data by time range, over the SOA to NPAC SMS Interface, with the Service Provider’s SOA Linked Replies Indicator set to their production setting. The recovery response includes a number of Notifications greater than the Notification Data Linked Replies Blocking Factor and less than the Notification Data Maximum Linked Recovered Notifications. – Success | 187-4, 187-5, 187-11, 187-15, 187-24, 187-29, 187-38 | B.7.2 |  |
| NANC 187-6 | SOA - Service Provider Personnel submit a resynchronization request for Notification Data by time range, over the SOA to NPAC SMS Interface, with the Service Provider’s SOA Linked Replies Indicator set to their production setting. The recovery response includes a number of Notifications greater than the Notification Data Maximum Linked Recovered Notifications. – Failure | 187-29, 187-38 | B.7.2 |  |
| 3. NANC 191 - DPC/SSN Value Edits |
| 4. NANC 291 - SSN Edits in the NPAC SMS |
| NANC 191/291-1 | SOA – Service Provider Personnel attempt to create a subscription version specifying some valid and some invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-1 :10, 291-6 : 10 |  | Prerequisites need to cover Edit Flag settings. TC directions need to explicitly state what type of invalid data to specify based on settings to test desired functionality. E.R. need to explicitly state what to validate based on settings. |
| NANC 191/291-2 | SOA – Service Provider Personnel attempt to modify a pending subscription version specifying some valid and some invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-1 : 10, 191-26 : 30, 291-6 : 10 |  | Ditto comments for 191/291-1 |
| NANC 191/291-3 | SOA – Service Provider Personnel attempt to activate a ‘pending’ subscription version that contains some valid and some invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-48 |  | Ditto comments for 191/291-1 |
| NANC 191/291-4 | SOA – Service Provider Personnel attempt to modify an ‘active’ subscription version that contains some valid and invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-1 : 10, 191-26 : 30, 191-36 : 41, 291-6 : 10 |  | Ditto comments for 191/291-1 |
| NANC 191/291-5 | NPAC OP GUI – NPAC Personnel attempt to submit a mass update request for a range of subscription versions specifying some valid and invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-1 : 10, 191-31 : 35, 191-36 : 41, 191-50, 291-6 : 10 |  | Ditto comments for 191/291-1 |
| NANC 191/291-6 | SOA – Service Provider Personnel attempt to schedule a Number Pool Block specifying some valid and some invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-11 : 20, 191-21 : 25, 291-6 : 10 |  | Ditto comments for 191/291-1 |
| NANC 191/291-7 | SOA – Service Provider Personnel attempt to modify a Number Pool Block specifying some valid and some invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-11 : 20, 191-21 : 25, 191-26 : 30, 191-42 : 47, 291-6 : 10 |  | Ditto comments for 191/291-1 |
| NANC 191/291-8 | NPAC OP GUI – upon Number Pool Block schedule activation, NPAC SMS fails Number Pool Block activation based on some invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-11 : 20, 191-21 : 25, 191-49 ? 291-6 : 10 |  | Ditto comments for 191/291-1 |
| NANC 191/291-9 | NPAC OP GUI – NPAC Personnel attempt to submit a mass update request that includes an ‘active’ Number Pool Block specifying some valid and invalid DPC/SSN information. The regional SSN Edit Flags (CLASS, LIDB, CNAM, ISVM and WSMSC) are set to production values. – Failure | 191-11 : 20, 191-21 : 25, 191-31 : 35, 191-42 : 47, 191-50, 291-6 : 10 |  | Ditto comments for 191/291-1 |
| 5. NANC 192 - NPA Split NPAC SMS Load File |
| NANC 192- | New NPA Split Test Script to be written and executed in Group Test. This script will closely emulate a production scenario where NPA Splits occur. Test Data, including Network – Subscription and Pooled Data, will be created. NPA Split Load Flat Files will be processed causing some automated broadcasts over the interface. Appropriate data validation will be verified prior to, during and after PDP. Multiple NPA Split Load Flat Files will be processed to demonstrate modification of NPA Split data including PDP dates as well as automated broadcasts over the interface as a result of these changes. This test case will also include scenarios where the NPA Split applies to Wireless carriers who’s PDPs are typically longer than those of Wireline. |  | B.8.2, B.8.2.1 |  |
| 6. NANC 218 - Conflict Timestamp Broadcast to SOA |
| NANC 218-1 | SOA – (Old) Service Provider Personnel submit a single TN, subscription version modify request specifying Authorization (FALSE) and a valid status change cause code setting the subscription version status to conflict. – Success | R5-44.2, R5-44.3 | B.5.2.3, B.5.2.4, B.5.5.1 |  |
| 7. NANC 230 - Donor SOA Port-To-Original of an Intra-Service Provider Po |
| NANC 230-1 | SOA – Service Provider Personnel create an Intra-Service Provider, Porting to Original Subscription where a previously ‘active’ Subscription Version exists, that is not a part of a Number Pool Block – Success | RR5-4, 230-1, RR5-6.1 | B.5.1.11.1 |  |
| NANC 230-2 | NPAC OP GUI – NPAC Personnel create an Intra-Service Provider, Porting to Original Subscription Version where a previously ‘active’ Subscription Version exists with a matching NPA-NXX-X, after the NPA-NXX-X Creation and prior to the NPA-NXX-X Effective Date – Failure | 230-2 | B.5.1.11.1 |  |
| NANC 230-3 | SOA - Service Provider Personnel create an Intra-Service Provider, Porting to Original subscription version after NPA-NXX-X Effective Date and Block Activation – Success | RR5-57 | B.5.1.11.1 |  |
| 8. NANC 249 - Modification of Dates for a Disconnect Pending SV |
| NANC 249-1 | SOA – Service Provider Personnel submit a subscription version modify request for a ‘disconnect-pending’ subscription version, modifying the Effective Release Date and Customer Disconnect Date to the current date/time or a date/time in the past. – Success | 249-1 : 4, 249-6, RR5-11 | B.5.2.7 |  |
| NANC 249-2 | SOA – Service Provider Personnel submit a subscription version modify request for a range of ‘disconnect-pending’ subscription versions, modifying the Effective Release Date and Customer Disconnect Date to a different date/time in the future. The range of subscription versions had Effective Release Dates that were not the same prior to the modification. - Success | 249-3 | B.5.2.7 |  |
| NANC 249-3 | SOA – Service Provider Personnel submit a subscription version modify request for a ‘disconnect-pending’ subscription version, without specifying the Customer Disconnect Date. – Failure | 249-5, R5-39.1, R5-29.2 | B.5.2.7 |  |
| NANC 249-4 | SOA – Service Provider Personnel submit a subscription version modify request for a ‘disconnect-pending’ subscription version, specifying an invalid format for the Effective Release Date and/or Customer Disconnect Date. – Failure | 249-2 | B.5.2.7 |  |
| 9. NANC 287 - ASN.1 Change for Required Field in VersionNewNPA-NXX and VersionNewNPA-NXX Recovery Notification |
| 10. NANC 297 - Sending SV Problem During Recovery |
| NANC 297-1 | LSMS – Service Provider Personnel submit a recovery request for SV Data specifying a TN range that includes SVs that have a sending status at the start of the Subscription Data recovery process. – Success | 297-1:3 |  | Some SVs need to have a Failed SP List populated |
| NANC 297-2 | LSMS – Service Provider Personnel submit a recovery request for Number Pool Block Data specifying a Block range that includes Blocks that have a sending status at the start of the Number Pool Block recovery process. - Success | 297-4 : 6 |  | Some NPB need to have a Failed SP List populated |
| 11. NANC 316 - Change the NSAP Field Size Declaration in ASN.1 – ASN.1 Recompile |
| 12. NANC 319 - NPAC Edit to Ensure NPA-NXX of LRN is in Same LATA as NPA-NXX of Ported TN |
| NANC 319-1 | SOA – Service Provider Personnel attempt to create a subscription version specifying a TN and an LRN with different LATA IDs. – Failure | 319-6 |  |  |
| NANC 319-2 | SOA – Service Provider Personnel attempt to modify a ‘pending’ subscription version specifying a TN and an LRN with different LATA IDs. - Failure | 319-7 |  |  |
| NANC 319-3 | NPAC OP GUI – NPAC Personnel submit a mass update request for a range of ‘active’ subscription versions specifying an LRN with a LATA ID the same as some of the TNs and different than othersTNs in the subscription version range specified. - Success | 319-10 |  |  |
| NANC 319-4 | SOA – Service Provider Personnel attempt to schedule a Number Pool Block specifying an LRN with a different LATA ID than the TNs in the Number Pool Block. – Failure | 319-8 |  |  |
| NANC 319-5 | SOA – Service Provider Personnel attempt to modify a Number Pool Block specifying an LRN with a different LATA ID than the TNs in the Number Pool Block. – Failure | 319-9 |  |  |
| NANC 319-6 | NPAC OP GUI – NPAC Personnel submit a mass update request including at least three complete Number Pool Blocks, specifying an LRN with a LATA ID the same as one of the Number Pool Blocks specified and different than the other Number Pool Blocks specified. - Success | 319-10 |  |  |
| 13. NANC 322 - Clean Up of Failed SP Lists based on Service Provider BDD Response File |
| NANC 322-1 | LSMS –Service Provider Personnel create a Bulk Data Download Response File for subscription version information. NPAC Personnel process the Bulk Data Download Response File. The Service Provider was previously on the Failed SP list for at least some of the subscription versions in the respective file. Verification steps are performed to ensure the Service Provider system is now in synch with the NPAC SMS. – Success | 322-1, 322-3, 322-5 : 8 |  |  |
| NANC 322-2 | LSMS –Service Provider Personnel create a Bulk Data Download Response File for Number Pool Block information. NPAC Personnel process the Bulk Data Download Response File. The Service Provider was previously on the Failed SP List for at least some of the Number Pool Blocks in the respective file. Verification steps are performed to ensure the Service Provider system is now in synch with the NPAC SMS.- Success | 322-2, 322-4 : 7, 322-9 |  |  |
| 14. NANC 323 - Partial Migration of a SPID via Mass Update These TCs are going to be left in the core 3.2 functional test section so that the ability for the NPAC SMS to demonstrate a SIC-SMURF file and a SP to process the file can be tested in a one-to-one NPAC to SP scenario – however these test cases shall also be part of Group Test. |
| NANC 323-1 | NPAC OP GUI – NPAC Personnel submit a request for a Partial SPID migration via Mass Update, where NPA-NXX, LRN, Subscription Version, NPA-NXX-X and Block Information exist for the migrating away from SPID. Verification steps are performed to ensure the Service Provider system is now in synch with the NPAC SMS. - Success | 323-1:20, 323-24, 323-25 |  | Make sure that Test Cases includes Primary and Secondary SPID scenarios. |
| NANC 323-2 | NPAC OP GUI – NPAC Personnel submit a request for a Partial SPID migration via Mass Update, where ‘pending’ Subscription Versions exist for the migrating away from SPID. Verification steps are performed to ensure the Service Provider system is now in synch with the NPAC SMS. - Failure | 323-21 |  |  |
| 15. NANC 354 - Delta Download File Creation by Time Range for Network Data (cousin of 169) |
| NANC 354-1 | NPAC OP GUI – NPAC Personnel initiate a Bulk Data Download of Network Data – Specifying the Latest View of Network Data Activity and a valid time range. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system. - Success | 354-1 : 3, 354-5 : 12 |  | NPA-NXX filter applied. |
| NANC 354-2 | NPAC OP GUI – NPAC Personnel initiate a Bulk Data Download of Network Data – Specifying All Network Data and a valid time range. Verification steps are performed to ensure the BDD file was processed successfully by the Service Provider system – Success | 354-4, 354-8 : 12 |  |  |

40 New TCs to be written.